ALMN (CCP4: Supported Program)
                                       
NAME

   almn - calculates rotation function overlap values using FFT
   techniques
   
SYNOPSIS

   almn hklin foo_mol1[.mtz] hklin2 foo_mol2[.mtz] mapout foo_almn[.map]
   [Keyworded input]
   
DESCRIPTION

   almn is a fast rotation function which works in Eulerian angles, an
   extension of the Crowther Rotation program by Eleanor Dodson (York
   University). The program calculates rotation function overlap values
   using FFT techniques (ref. R.A.Crowther The Molecular Replacement
   Method ed. M. Rossmann). The original three programs have been merged
   into the one here by Eleanor Dodson. She has also extended the output
   to detail symmetry related Eulerian angles, spherical polars and
   direction cosines for each peak in the output Eulerian angle map.
   
   The position of peaks is given for all symmetry related positions in
   both Eulerian and polar angles.
   
   The axis conventions have been generalised and it is possible to deal
   with all space groups.
   
   The correlation between self- and cross-rotation functions can be
   analysed with the program RFCORR.
   
   Options are provided in the program for various restart points.
    1. The results of the first stage of the calculation (ALMN) may also
       be saved for subsequent rotation function summations on different
       grids. Beware however these spherical harmonics change for
       different resolution and integration sphere cut off values.
    2. The calculated rotation map is written to a standard CCP4 map
       file, which can be used as input for the program extend, if a set
       of spacegroup symmetry operations can be derived, or can be
       plotted with a standard package (e.g., npo). The program will
       reread this file to do a peak search (see description of the
       keyword FIND for details of symmetry).
    3. A list of peaks may be read in, and all symmetry related peaks
       generated (option PEAK).
       
A NOTE ON SYMMETRY AND ASYMMETRIC UNITS

   If the spacegroups have more than one symmetry operation, additional
   rotation solutions are generated by their combination. The asymmetric
   units required are calculated in the program.
   
KEYWORDED INPUT

   Only the first 4 letters of each keyword are necessary. All input is
   free format. Many data cards are optional. The input to this program
   is intended to be as similar as possible to that for the polar angle
   rotation function program POLARRFN; however there are a few
   differences, so beware.
   
   The various data control lines are identified by keywords, those
   available being:
   
     CROSS, CRYSTAL (compulsory), END, FIND, LABIN, LIMITS, LSPHERE,
     MAP, MAXREF, NOPRINT, PEAK, PRINT, READ, RESOLUTION, ROTS, SAVE,
     SELF, SUM, TITLE, XMLOUTPUT
     
  TITLE title
  
   The rest of the line is taken as a title.
   
  SELF sphmin sphmax
  
   Set flag for self rotation (c.f. keyword CROSS), and set radii for
   integration (in either order).
   
   SPHMAX
          outer radius of the cutoff sphere in Patterson function space
          (Angstrom).
          
   SPHMIN
          inner radius of the cutoff sphere in Patterson function space
          (Angstrom) Sphmin should be more than 0.9*RESMAX.
          
  CROSS sphmin sphmax
  
   Set flag for cross rotation (c.f. keyword SELF), and set radii for
   integration as for SELF
   
  LSPHERE no
  
   If the sphere radius is so large that the sphere volume is greater
   than 50% of the asymmetric unit volume, and the logical flag LSPHERE
   is not set, then the radius is automatically reset to give sphere
   volume = 50% of asymmetric unit volume.
   
  RESOLUTION resmin resmax
  
   Read resolution limits in Angstroms, in either order. If only one is
   given, it is treated as the high resolution limit. Note that because
   of the limit of 60 Bessel functions in this version, the integration
   radius SPHMAX cannot be greater than 12*RESMAX: if it is, the program
   resets RESMAX to SPHMAX/12.0.
   
   The program chooses whether to use the 30 or 60 Bessel function tables
   as appropriate: 30 if SPHMAX/RESMAX < 5.83, and 60 otherwise.
   
  CRYSTAL
  
   Followed by subsidiary keywords and numbers.
   
   This card is COMPULSORY for each hklin set (one for self-rotation, two
   for cross-rotation). The first keyword FILE indicates whether this
   CRYSTAL card refers to crystal 1 or to crystal 2.
   
   subsidiary keyword FILE
          followed by crystal number 1 or 2 (default 1). The syntax is
          any one of `FILE 1' or `FILE 2'.
          
   subsidiary keyword ORTH
          followed by orthogonalisation code NCODE for this crystal.
          
 = 1 orthogonal x y z along a,c*xa,c* (Brookhaven, default)
 = 2 b,a*xb,a*
 = 3 c,b*xc,b*
 = 4 a+b,c*x(a+b),c*
 = 5 a*,cxa*,c   (Rollett)

   subsidiary keyword BFAC
          followed by temperature factor B (default = 0). This can be
          used to sharpen the input F by
          exp**-[BFAC*sin**2(theta)/lambda**2] before squaring, i.e. a
          negative BFAC will sharpen the data.
          
   subsidiary keyword FLIMITS
          followed by minimum F (default = 0) and maximum F (default =
          1000000000) in either order. The test is done after application
          of the temperature factor, but before squaring to intensities.
          This is used to restrict the number of reflections used in the
          calculation to less than 10000. The program dimensions can be
          increased but there is little point in including weak data.
          
   subsidiary keyword SCALE
          followed by scalfactor to divide Fsquared. Sometimes needed to
          reduce overflows.
          
   subsidiary keyword CELL
          followed by a b c (alpha beta gamma - default = 90.0) Rarely
          needed - just for peak analysis.
          
   subsidiary keyword SYMMETRY
          followed by space group number or name. The crystal symmetry
          will be read from a symmetry library (logical name SYMOP). The
          spacegroup name is e.g. P212121.
          
  LABIN
  
   Followed by subkeyword FILE followed by file number and then followed
   by MTZ file assignments for F and optionally for SIGF, e.g. LABIN FILE
   1 F=FO
   
  LIMITS btmin btmax bstep
  
   Read limits and step on beta in degrees
   
  PRINT lprint
  
   Reset print threshold LPRINT (default = 1). The rotation function is
   scaled to a maximum on the first section of 50.
   
  NOPRINT
  
   Switch off printing of map
   
  MAP
  
   Write rotation function to a map file: this is the default unless only
   the PEAK option is used. This may be read back later for plotting,
   peak searching, etc using the READ option.
   
  MAXREF
  
   Limit the number of reflections used to MAXREF - default 10000.
   
  FIND peak maxpek [RMS] [OUTPUT filename]
  
   Read peak threshold and maximum number of peaks. MAXPEK is the maximum
   number of peaks to find (default = 20). Up to MAXPEK peaks above PEAK
   will be found, and all symmetry related peaks generated.
   
   If the keyword RMS is present, then the peak threshold is PEAK * RMS
   density, otherwise PEAK is the absolute threshold in the scaled map.
   
   If the keyword OUTPUT is present, the unique peaks will be output to a
   file whose name may also be given (default filename or logical name
   PEAKS). The keyword RMS must precede OUTPUT if both are present.
   
   Note that the program finds rho(max) in a 3x3x3 box. It attempts to
   interpolate the peak positions, but may not do very well at this near
   beta = 0 or 180 where the peaks are very elongated. It DOES NOT deal
   with map edges properly - if you want to do this you will need to run
   the program EXTEND with the proper rotational Eulerian angle symmetry.
   This can be deduced from the symmetry equivalents generated for a
   Alpha Beta Gamma set in a general position. The map is written with a
   cell with dimensions 360 360 360 90 90 90, and a grid in steps of 5
   degrees or 2.5 degrees. A symmetry operation (120 + alpha, 180 - beta,
   -gamma) would be generated by an entry 1/3+x,1/2-y,-z in a fake
   spacegroup.
   
  SAVE
  
   Save ALMN coefficients files (i.e., open them `NEW' not `SCRATCH') for
   future use with the SUM option (q.v.). Not useful.
   
  SUM
  
   Read ALMN coefficients from files generated in a previous run of the
   program (saved with the SAVE command). Not useful.
   
   It is possible to start again after the first stage of rotation has
   been done. The ALMN coefficients for each crystal are written to files
   with the default names COEFFS1 and COEFFS2. These files can be used to
   save time on a later run of the program.
   
  ROTSYM irsygp
  
   If you know the rotation symmetry, you can make an entry into the
   SYMOP file with `spacegroup number' IRSYGP, then it will be written to
   the output map. This can be helpful for some fancy plots, but is not
   normally useful.
   
  READ [btmin] [btmax]
  
   Instead of calculating the rotation function, read a previously
   calculated map, written out using the MAP command. This allows you to
   FIND peaks at a lower or higher level, and generate symmetry
   equivalents, or to PRINT it to the lineprinter. To generate symmetry
   the program requires cards SELF or CROSS, and SYMMETRY (i.e. the
   number of symmetry operators must be defined).
   
   If parameters and BTMAX are present, only sections between these
   values of Beta are read. Otherwise the whole map is read.
   
  PEAK
  
   Read a list of peak positions (alpha beta gamma in degrees) from
   subsequent lines,
   terminated by a blank line, `END' or end of file. The program will not
   calculate a rotation function, but will generate all symmetry related
   peaks from the peaks given, and print out the corresponding matrices.
   This option requires cards SELF or CROSS, CELL, and SYMMETRY (i.e. the
   number of crystals, their symmetry and orthogonalisation codes must be
   defined).
   
  XMLOUTPUT
  
   This keyword is of little use for the 'user'. When specified almn will
   output a small XML file of the reindex operator. The name and location
   of the XML file can be specified on the command line with XMLFILE,
   otherwise the file will be called ALMN.xml.
   
   Example of output file
<?xml version="1.0"?>
 <almn_run>
  <ALMN
    ccp4_version="4.1"
    date=" 1/24/02"
   />
  <reindex_operator
    required="yes"
    operator="-h,-k,l"
   />
 </almn_run>

INPUT AND OUTPUT FILES

   HKLIN
          input amplitudes for crystal 1
          
   HKLIN2
          input amplitudes for crystal 2
          
   MAPIN
          input map for READ option
          
   MAPOUT
          output map for MAP option
          
   SYMOP
          symmetry library
          
   COEFFS1
          ALMN coefficients for crystal 1
          
   COEFFS2
          ALMN coefficients for crystal 2
          
   By default COEFFS1 and COEFFS2 are created as scratch files.
   
NOTES

    1. If intensities are to be included to a Fourier cut-off of RESMAX
       A, for a cut-off sphere of radius a A in the Patterson density,
       the maximum value of L (Bessel coefficient) that should be
       included is approximately
       Lmax = 2 pi a / RESMAX
       The program allows Bessel functions up to order 60, hence the
       following restrictions on values of RESMAX and a:

 RESMAX           a
 ------           -
 6  A          72 A
 8  A          96 A
 10 A         120 A

    2. If there are two crystals, it is the crystal represented by the
       second data stream which is rotated, while the crystal represented
       by the first data stream is held fixed. The output of final angles
       are therefore those required to rotate the second crystal to the
       orientation of the first. In particular the alpha, beta, gamma are
       the Eulerian angles for rotating axes as defined by Tony Crowther.
       They convert the density of crystal 2 to that of crystal 1 by
       rotating crystal 2 first through gamma about Zo, then through beta
       about Yo, then through alpha about Zo relative to the fixed axes.
       Positive rotation clockwise is when looking along the axis from
       the origin. The rotations are carried out in the ORTHOGONAL frame,
       which is related to the crystallographic frame according to the
       setting of the ORTH flag. Beware of the permutations introduced by
       ORTH .ne. 1.
       
PRINTER OUTPUT

   The line printer output contains details of the input parameters, the
   orientation matrices for hkl and xyz for each crystal, summaries of
   the reflection data and finally values of the rotation function maxima
   and the associated angles including symmetry related sets. A map will
   also be printed if this was requested.
   
   The program also automatically performs extra analysis to see whether
   the indexing is consistent between HKLIN and HKLIN2, and if reindexing
   is required then it will suggest which reindexing operation should be
   used on HKLIN2 to give consistent indexing. The REINDEX program can be
   used to perform the actual reindexing.
   
ERROR MESSAGES

   The program calculates the array sizes required for a given problem,
   lists these, and will stop if the values exceed those set in the
   program. There is also a limit of 10000 reflections for any given
   reflection data set: the program will try to reset the minimum
   intensity to get an acceptable number.
   
REFERENCES

    1. R.A.Crowther, The Fast Rotation Function in The Molecular
       Replacement Method ed. M.G. Rossman, Int. Sci. Rev. Ser., no. 13,
       pp. 173-178 (1972).
    2. E.J.Dodson, in Molecular Replacement, Proceedings of the Daresbury
       Study Weekend, (1985) DL/SCI/R23
       
AUTHORS

   Originator: Tony Crowther/Eleanor Dodson
   Contact: Daresbury Laboratory/York University
   
PROGRAM STRUCTURE

   The main program carries out the following functions:
    1. Initialisations
    2. Input of control data
    3. Checks limits determined by array sizes
    4. Calculates and sets up a table of spherical Bessel function
       coefficients
    5. Input of one (or two reflection files) including summation loop to
       calculate ALMN and BLMN
    6. Fast rotation function summation (subroutine FRFS)
    7. Checks consistency of indexing between input files
       
SEE ALSO

   extend, npo, polarrfn, rfcorr, reindex.
   
EXAMPLES

   The following are examples of control data.
   
  A complete self rotation calculation
  
#
# PPb R-state self-rotation function
#
almn  hklin ppbt_calc mapout almnself << eof
TITLE PPb R-state Fcalc self-rotn fn, res 15-6, radius 0 30
SELF 3 30
RESOLUTION  15 6
CRYSTAL  FILE 1 ORTHOG 3 BFAC -20
LABIN FILE 1 F=FC
LIMITS 0 90 5
PRINT
FIND  2 30 RMS OUTPUT self_peaks
END
eof
#
#  Now read back map to search at different limits
#
almn  hklin ppbt_calc mapout almnself << eof
TITLE PPb R-state Fcalc self-rot fn, res 15-6, radius 0 30
SELF 3 30
RESOLUTION  15 6
CRYSTAL  FILE 1 ORTH 3 BFAC -20
LABIN FILE  1 F=FC
LIMITS 0 90 5
NOPRINT
READ
FIND  30 30 OUTPUT self_peaks
END
eof

  A complete cross rotation calculation
  

#
almn hklin ovalnat   hklin2 alpha1t  map cross1 << eof
TITLE Cross rotation function ovalbumin to tetragonal alpha1-PI
CROSS 5 30
RESOLUTION 10 6
CRYSTAL FILE 1 ORTHOG 1  BFAC 0
LABIN FILE 1 F=FOVALNAT
CRYSTAL FILE 2 ORTHOG 1  BFAC 0
LABIN FILE 2  F=FCALPHA1T
LIMITS  0 180 5
MAP
PRINT
FIND  2 20  RMS
END
eof
#
#
npo mapin cross1 plot cross << eof
TITLE  Ovalbulmin cross rotation
MAP
CONTRS   60 TO 200 BY 20
SECTNS 0 36
SIZE   160
PLOT
eof
#

#
# PPb R-state cross-rotation function
#
#
almn  hklin ppb/p21all1   hklin2 ppbt_calc mapout almncross << eof
TITLE PPb R-state cross-rot fn, Fobs, res 8-4, radius 0 20
CROSS  3 20
RESOLUTION  8 4
CRYSTAL  FILE 1 ORTHOG 3 BFAC -20 FLIMITS 100 999999 SYMMETRY 4
LABIN FILE 1 F=F
CRYSTAL  FILE 2 ORTHOG 1 BFAC -20 FLIMITS 100 999999 SYMMETRY 1
LABIN FILE  1 F=FC
LIMITS 0 90 5
FIND   3 20 RMS
END
eof
#
#
# Plot cross rotation function from ALMN
#
npo mapin almncross plot cross << eof
TITLE PPb R-state cross-rot fn, Fobs, res 8-3, radius 0 20
CELL 100 100 100 90 90 90
MAP  SCALE 1.4
CONTRS  50 TO 200 BY 20
SECTNS  0 19
PLOT
eof
#