DETWIN (CCP4: Supported Program)
                                       
NAME

   detwin - tests for merohedral twinning, and detwins data
   
SYNOPSIS

   detwin HKLIN foo_in.mtz HKLOUT foo_out.mtz
   [Keyworded input]
   
DESCRIPTION

   Twinned data is measured when two or more copies of the reciprocal
   lattice overlap. Hence we need to deconvolute the two twinned
   components to obtain useable data. The equations for two overlapping
   reflections, Itrue(h1) and Itrue(h2), are:
     ITw(h1) = (1-tf)*Itrue(h1)  +     tf*Itrue(h2)
     ITw(h2) =     tf*Itrue(h1)  + (1-tf)*Itrue(h2)

     where tf is the twin fraction, often denoted as 'alpha'


     thus Itrue(h1) = ((1-tf)*iTw(h1) -tf*iTw(h2)) / (1-2tf)
     thus Itrue(h2) = ((1-tf)*iTw(h2) -tf*iTw(h1)) / (1-2tf)
     also
     var(h1) = ((1-tf)/(1-2tf))**2 * sdTw(h1)**2 + (tf/(1-2tf))**2 * sdTw(h2)**
2
     var(h2) = ((1-tf)/(1-2tf))**2 * sdTw(h2)**2 + (tf/(1-2tf))**2 * sdTw(h1)**
2

   This deconvolution is only possible if tf is not exactly 0.5. As it
   approaches this value the variances become extremely large.
   
   The occurrence of twinning can be recognised from the intensity
   statistics of the data set. This program carries out several tests for
   twinning as a function of both twinning fraction, and resolution. It
   can also detwin merohedrally twinned data for a given twinning
   fraction. It reads and writes either intensities or amplitudes from an
   MTZ file, with the output information corrected for a given twinning
   fraction.
   
   The twin operator is required (see TABLE OF POSSIBILITIES), and for
   MTZ output, the chosen twin fraction.
   
   The twinning tests performed are:
   
   The partial twin test (see reference [4]) <H> = <|Itw1 -Itw2|/(Itw1
   +Itw2)> plotted against theoretical expectations.
   
   The estimate of the twinning factor as (0.5 -<H>), plotted against
   resolution.
   
   Those tabulated against the twinning factor, for values ranging from
   0.00 to 0.48, are
   (N.B. it is impossible to evaluate Itrue if the twinning-factor is
   exactly 0.5):
    a. Number of negative intensities after detwinning (Britten plot)
       This is plotted for all data, and for the subset where Itw is
       greater than 3 Sigma.
       If the twinning fraction is too small there should be no negative
       intensities generated; if it is too large, the number will
       increase linearly. Fitting a straight line through the plot gives
       a good estimate of the twinning fraction.
    b. The second moment of <I> (<I^2>/ <I>^2 as a function of resolution
       and twinning fraction. For untwinned acentric data this should
       equal 2; and for a perfect twin it should be 1.5.
    c. The correlation between I1 and I2 before and after detwinnig. The
       overall correlation is dominated by the low resolution data and is
       therefore not very sensitive, and can be misleading. However for
       high resolution data it should drop to 0.00 UNLESS there is an NCS
       operator related to the twinning operator.
       
   If the output MTZ file contains IMEAN, it can be run through TRUNCATE
   again, and the other moments and the N(z) test examined to see if the
   intensity statistics now follow the expected distribution for
   non-twinned data. twinned. See Cumulative distribution plot, which for
   twinned data becomes sigmoidal, and the moments of I (or E or z) which
   are different for twinned data than for untwinned.
   
   The general formulas for expected moments <I^k> /<I>^k for untwinned
   acentric data are:
Table of moments:

  k-th moment is Gamma(k+1)  = k!  if k is an integer
  k-th moment                = sqrt(PI) k!  if k equals integer+0.5
  i.e. the (2k+1)th moment of E = sqrt(PI) 2k * 2k-2 * ... *2

  In general Gamma(k+1) = k Gamma(k)

               Acentric                        Centric
         Untwinned data Perfect twin.   Untwinned data Perfect twin.
  <E>         0.866         0.94             0.798       ?
  <E^3>       1.339         1.175            1.596       ?
  <I^2>       2.0           1.5              3.0         ?
  <I^3>       6.0           3.0             15.0         ?

  <I^4>      24.0           7.5            105.0         ?

INPUT AND OUTPUT FILES

   The following input and output files are used by the program:
   
   Input Files:
   
   HKLIN
          Input MTZ file.
          This would normally be the output of SCALA or SCALEPACK2MTZ
          containing the measured intensities, but structure factor
          amplitudes can also be used as input. See the LABIN keyword for
          details.
          
   Output Files:
   
   HKLOUT
          Output MTZ file.
          A file containing corrected Is or Fs for a single twin
          fraction, which must be specified with the TWIN_FRACTION
          keyword. If the file contains IMEAN, it can be run through
          TRUNCATE, which tests whether the data has been successfully
          detwinned. If no TWIN_FRACTION keyword is given, then no output
          file is written.
          
KEYWORDED INPUT

   The various data control lines are identified by keywords. Only the
   first 4 letters of each keyword are necessary. The possible keywords
   are:
   
     DEBUG, LABIN, RESOLUTION, OPERATOR, SIGMACUT,TITLE, TWIN_FRACTION
     
  TITLE <title>
  
   [OPTIONAL INPUT]
   
   Title to write to output reflection file.
   
   Default is to keep the title on the input MTZ file. If there is no
   title on the input MTZ file, then the title is set to: "From Detwin on
   the <date>"
   
  SIGMACUT <Nsig>
  
   [OPTIONAL INPUT]
   
   The various tests are carried out with all reflections, and repeated
   for those reflections which are greater than <Nsig>*I. Tests such as
   the Britten plot or those using <H> are unreliable for weak data.
   
  RESOLUTION <Dmin> <Dmax>
  
   [OPTIONAL INPUT]
   
   Resolution limits - either 4(sin theta/lambda)**2 or d in Angstroms
   (either order). Reflections outside these limits will be excluded from
   all analysis and omitted on output. Defaults are taken from the range
   of data in the input file (i.e. all data included).
   
  OPERATOR <string>
  
   Twinning operator, given as the indices of the reflection that is
   related to the reflection (h,k,l) by the twin operator. See TABLE for
   likely operators for each space group. If there is only one
   possibility for a spacegroup this will be used, and there is no need
   to input an operator. Otherwise it is COMPULSORY.
   
   For example for P31 either OPERATOR -h,-k, l
   or OPERATOR k, h,-l
   or OPERATOR -k,-h,-l
   
  TWIN_FRACTION <alpha>
  
   If this is given, an output MTZ file will be written to HKLOUT with Is
   or Fs corrected assuming the twin fraction <alpha>. It is difficult to
   estimate the twinfrac accurately unless the data is of very good
   quality, but look at all the information plotted. To carry out the
   exhaustive TRUNCATE tests you will need to run the program several
   times and look at the resulting intensity statistics. The value which
   gives the best fit to the theoretical distribution for the acentric
   terms should be used. Alternatively, run the Uppsala program "dataman"
   (keyword GEminin) which will estimate the twin fraction.
   
   Once a refined model has been obtained, it is possible to use the
   Fcalc values from this model to obtain a better estimate of the twin
   fraction (not yet implemented).
   
  LABIN <program label>=<file label>...
  
   Specify input column lables. [OPTIONAL INPUT]
   
   Truncate takes output from SCALA and SCALEPACK2MTZ which generate
   standard labels. This is the most common usage of the program, in
   which case LABIN records are not required.
   
   The program labels defined are: F SIGF IMEAN SIGIMEAN I(+) SIGI(+)
   I(-) SIGI(-)
   NB: ONLY the single data pair (F SIGF) or (IMEAN SIGIMEAN) assigned by
   LABIN is detwinned.
   
   F
          A Structure Amplitude. The structure intensity used for
          detwinning is generated on input.
          
   SIGF
          Standard deviation of the above
          
   IMEAN
          Original average Structure Intensity
          
   SIGIMEAN
          Standard deviation of the above
          
   I(+)
          Structure Intensity of hkl
          
   SIGI(+)
          Standard deviation of the above
          
   I(-)
          Structure Intensity of -h -k -l
          
   SIGI(-)
          Standard deviation of the above
          
  DEBUG <ndebug>
  
   [OPTIONAL INPUT]
   
   Debug output will be printed for <ndebug> reflections
   
SEE ALSO

   truncate
   
REFERENCES

    1. Rees, D.C. Acta Cryst. (1980) A36, 578-581. The influence of
       Twinning by Merohedry on Intensity Statistics.
    2. Redinbo, M.R. and Yeates, T.O. (1993) Acta Cryst. D49, 375-380.
       Structure Determination of Plastocyanin from a Specimen with a
       Hemihedral Twinning Fraction of One-Half.
    3. Gomis-Ruth, F.X., Fita, I., Kiefersauer, R., Huber, R., Aviles,
       F.X. and Navaza, J. (1995) Acta Cryst D51, 819-823. Determination
       of Hemihedral Twinning and Initial Structural Analysis of Crystals
       of the Procarboxypeptidase A Ternary Complex.
    4. Yeates, T.O. (1997) Methods in Enzymology 276, 344-358. Detecting
       and Overcoming Crystal Twinning.
       
AUTHOR

   A.G.W. Leslie
   andrew@mrc-lmb.cam.ac.uk
   Modifications by E.J.Dodson (York)
   
EXAMPLES


#!/bin/csh -fv
detwin hklin /ss5/hotaylor/andrew/h1_scala.mtz  \
         hklout $scr0/detwin.mtz  << eof-detwin
title DETWIN WITH TWIN FRAC 0.4
SYM -k,-h,-l
twin 0.4
LABI IMEAN=I SIGIMEAN=SIGI
eof-detwin

# Run TRUNCATE to check all moments and N(z) statistics
trunc:
truncate hklin $scr0/detwin.mtz  hklout $scr0/trunc_detwin.mtz  <

#!/bin/csh -f
#
detwin HKLIN  s100_tetpt.mtz   \
HKLOUT $SCRATCH/s100_tetpt-detw.mtz   \
<< eof
TITLE Sp100 test R3
RESO 10 3.5
#SYMM k,h,-l         #  No need for detwinning operator this is the only possib
ility for R3
TWIN 0.19            #  the output file will have Idetw1 and Idetw2
SIG  6               #  only analyse data where Ih1 and Ih2 are greater than 6S
igma
LABI F=F SIGF=SIGF
END
eof