DMMULTI (CCP4: Supported Program)
                                       
NAME

   dmmulti - multi-xtal density modification package, release 0.9, 4/5/98
   
SYNOPSIS

   dmmulti HKLIN1 foo1.mtz [HKLIN2 ...] HKLOUT1 bar1.mtz [HKLOUT2 ...]
   [SOLIN1 foosol1.msk [SOLIN2 ...]] [SOLOUT1 barsol1.msk [SOLOUT2 ...]]
   [MSKIN1 foomsk1.msk [ MSKIN2 ...]]
   [Keyworded input]
   
REFERENCE

   K. Cowtan (1994), Joint CCP4 and ESF-EACBM Newsletter on Protein
   Crystallography, 31, p34-38.
   
DESCRIPTION

   'dmmulti' is a package which applies real space constraints based on
   known features of a protein electron density map in order to improve
   the approximate phasing obtained from experimental sources. The
   program may be applied to data from one or more crystal forms
   simultaneously. Various information can be applied, including such
   diverse elements as the following (see keyword MODE):
   
   SOLV
          Solvent flattening (8)
          
   HIST
          Histogram mapping (9)
          
   SKEL
          Skeletonisation (1,7) (alpha release)
          
   AVER
          NCS averaging, including multi-crystal averaging (2,6)
          
   A discriminator analogous to the crystallographic free-R factor (3)
   plays an important part in the procedure, providing a good indication
   of the effectiveness of a particular density modification calculation,
   and also an accurate method for determining weights for new phases
   calculated by the procedure. This avoids the problems of
   over-consistency and overestimated weights which could arise in
   earlier density modification procedures. Note that the dm-free-R is
   not truly a free-R factor since it is impossible to completely isolate
   a set of reflections: all structure factor magnitudes are
   fundamentally interrelated through the density constraints in real
   space.
   
   The program can either use a free-R set from the mtz file, or generate
   its own set internally. It is also possible to recycle the
   calculation, performing the density modification once or more times
   with different free-R sets, and then once with no free-R set but using
   the information obtained from the free-R cycles. This has been found
   to give a slight improvement in the overall results.
   
   Calculation of scale and B-factor for the data are automatic. This is
   performed by comparison with an empirically derived database of map
   variance at different resolutions, and is more reliable than the
   conventional Wilson plot.
   
   Non-crystallographic symmetry averaging can be performed for both
   proper and improper symmetries, and different NCS averaging operations
   can be applied to different parts of the protein (Thanks to Dave
   Schuller for his help with this). Spectral B-spline interpolation is
   used for fast calculation on a low resolution grid; this has been
   developed by Dr. Eric H. Grosse.
   
   Multi-crystal averaging can be performed between phased and/or
   unphased forms. The calculation is performed efficiently and entirely
   in-core.
   
   Skeletonisation is by the core-tracing algorithm of Swanson (7). This
   is faster than Greer's algorithm and allows adjustment of the
   skeletonisation parameters without recalculating the skeleton. As a
   result the skeletonisation calculation is rendered largely automatic.
   
   Operation is by standard keyworded card input. Input masks may be on
   any grid and axis order, however if the mask grid is too fine the
   program may run out of space to store it.
   
INPUT FILES

  HKLINi
  
   Input mtz file for i'th crystal form - This should contain the
   conventional (CCP4) asymmetric unit of data (see CAD).
   
  [SOLINi]
  
   Input solvent mask for i'th crystal form - This overrides the
   automatic Wang mask determination. The input mask can have any grid
   and axis ordering, and may have any extent from the protein region of
   a single asymmetric unit to the whole cell.
   
  [MSKINj]
  
   Input averaging masks for j'th domain - These are used with the AVER
   option. The input masks can have any grid or axis ordering, and should
   cover a single monomer or domain, however correct results will still
   be obtained (more slowly) if the mask covers a proper symmetry related
   multimer. 'dmmulti' does not perform overlap removal.
   
OUTPUT FILES

  HKLOUTi
  
   Output mtz file for i'th crystal form.
   
  [SOLOUTi]
  
   Output solvent mask for i'th crystal form - This will be on the
   program grid with default axis order, and will cover the whole unit
   cell.
   
MAJOR KEYWORDS

   Input is keyworded. Available keywords are:
   
   AVERAGE, GRID, LABIN, LABOUT, MODE, NCYCLE, RESOLUTION, SCALE, SCHEME,
   SKEL, SOLC, WANG, XTAL.
   
   (MODE and SOLC are compulsory)
   
  XTAL <xtal>
  
   Select the <xtal>'th crystal form. Keywords following the keyword will
   apply to this crystal form. Any keywords before the first XTAL card
   apply to form 1.
   
  MODE [SOLV] [HIST] [AVER] [SKEL]
  
   Select the calculation to be performed:
   
   SOLV
          = Solvent flattening
          
   HIST
          = Histogram mapping
          
   AVER
          = Non-crystallographic symmetry averaging
          
   SKEL
          = Skeletonisation
          
  SOLC <solc> [ MASK <solvfrac> <protfrac> ] [ MEAN <solvval> <protval> ]
  
   <solc>
          = solvent content. ALWAYS INPUT THE CORRECT SOLVENT CONTENT
          HERE TO ENSURE CORRECT SCALING. 0.0=all protein, 1.0=all
          solvent.
          
   MASK
          - used to set different mask volumes to the above for histogram
          matching and solvent flattening.
          <solvfrac> = fraction of cell to be masked as solvent.
          <protfrac> = fraction of cell to be masked as protein.
          If <solvfrac>+<protfrac> < 1.0 then there will be a buffer
          region between solvent and protein which is neither histogram
          matched nor solvent flattened. This feature is provided by
          popular demand, but makes things worse in most of my test
          cases.
          
   MEAN
          - used to set mean density for solvent and protein regions.
          This affects scaling and density modification.
          <solvval> = mean density in solvent region.
          <protval> = mean density in protein region.
          (defaults 0.32, 0.43 electrons per cubic angstrom)
          
  RESOLUTION <rmin> <rmax>
  
   Resolution range of reflections to be included in the calculation. By
   the end of the calculation all the reflections in this range will be
   included, however at the start only a subset are used, chosen on the
   basis of the SCHEME card (default is the whole range of the input mtz
   file).
   
  NCYCLE <ncycle> [ FREE <ncross> ]
  
   Number of cycles of phase extension to perform (defaults <ncycle>=10
   <ncross>=1).
   
   <ncycle>
          = Number of cycles over which to perform phase extension. Use
          10 cycles for a quick result, try more (20-100) but check the
          free-R factor.
          
   <ncross>
          = Number of times each step is performed to provide statistics
          for the free-R and phase weighting.
          For <ncross>=1 a changing random set of reflections are omitted
          each cycle for the free-R factor.
          For <ncross>=2 a fixed set is chosen (using the free-R flag if
          available) and omitted for the free-R factor, then the cycle is
          run a second time using all the reflections.
          For <ncross> > 2 (<ncross>-1) multiple free-R sets are
          generated, then on the <ncross>-th cycle all reflections are
          included.
          
   The total time taken is proportional to the product of these two
   values. Use <ncross> = 1 for large structures where the time becomes a
   significant factor, otherwise use <ncross> = 2. Only use <ncross> > 2
   for small structures where the statistics are particularly poor (<
   5000 reflections).
   
   In the case of a multi-crystal calculation only one NCYCLE card is
   allowed, which applies to all forms.
   
  SCHEME AUTO | RES | MAG | FOM [ [ FROM <res> ] | [ FRAC <frac> ] ]
  
   RES
          - perform phase extension in resolution steps, starting with
          the low resolution data.
          
   MAG
          - perform phase extension in magnitude steps, starting with the
          largest reflections.
          
   FOM
          - perform phase extension in FOM steps, starting with the best
          phased data.
          
   AUTO
          - perform phase extension using a combination of the above
          chosen on the basis of what the data set looks like. This
          option will also pick a reasonable value for <frac>.
          
   FRAC <frac>
          - fraction of the input data to use as a starting set.
          
   FROM <res>
          - sets <frac> to the fraction of the data within a resolution
          sphere radius <res>.
          
   (default: AUTO)
   
  LABIN FP=.. SIGFP=.. [PHIO=.. FOMO=..] [HLA=.. HLB=.. HLC=.. HLD=..]
  [PHIDM=.. FOMDM=..] [FREE=..]
  
   Normally just the first four columns (FP,SIGFP,PHIO,FOMO) are input.
   However if you have Hendrickson-Lattman coefficients you may want to
   input these to the program as well (the difference is marginal except
   for SIR data). If you want to start from the end of a previous density
   modification calculation then the PHIDM, FOMDM columns are used.
   
   For multi-crystal averaging, if a crystal form is unphased the PHIO
   and FOMO columns may be omitted. There should be some sort of phases
   for at least one form.
   
   FP
          = F magnitude
          
   SIGFP
          = standard deviation, 0 for unmeasured
          
   PHIO
          = best initial phase estimate
          
   FOMO
          = weight attached to PHIO
          
   HLA-HLD
          = Hendrickson Lattman coefficients
          
   PHIDM
          = phase from previous density modification calculation to use
          as starting value
          
   FOMDM
          = weight from previous density modification calculation to use
          as starting value
          
   FREE
          = free-R flag (only used if ncross>1)
          
  LABOUT PHIDM=.. FOMDM=.. [FCDM=.. PHICDM=..]
  
   Normally just the first two columns are output. Don't use the other
   two unless you are a very clever person.
   
   PHIDM
          = modified phase
          
   FOMDM
          = weight attached to PHIDM
          
   FCDM
          = F from final modified map before phase recombination
          
   PHICDM
          = Phase from final modified map before recombination
          
OTHER KEYWORDS

  SKEL [ LENGTH <joinlen> <endlen> ] [ BFAC <bfac> ] [ EVERY <nskl> ]
  
   Perform iterative skeletonisation on the map. Cyles of skeletonisation
   are interspersed with cycles of conventional density modification
   (defaults <joinlen>=6.0 <endlen>=6.0 <bfac>=45 <nskl>=3).
   
   <joinlen>
          = length of skeleton in Angstrom/residue to generate between
          density peaks.
          
   <endlen>
          = length of skeleton in Angstrom/residue to generate in
          'trailing ends'.
          
   <bfac>
          = temperature factor to apply to the sharpened map before
          skeletonisation.
          
   <nskl>
          = apply skeletonisation instead of every <nskl>-th density
          modification cycle.
          
   See also dm_skeletonisation.
   
  AVERAGE [DOMAIN <domn>} [ REFINE [ STEP <dr> <dphi> ] [ EVERY <nref> ]]
  
   Set a NCS symmetry averaging operator. This card is followed by one
   rotation/translation matrices on subsequent lines in either CCP4 or
   O/RAVE format (defaults <dr>=0.5 A, <dphi>=2.5 degrees, <nref>=3).
   
   CCP4 Formats (see also lsqkab)
          ROTA EULER <alpha> <beta> <gamma> (Euler angles)
          TRAN <t1> <t2> <t3>
          
   or
          ROTA POLAR <omega> <phi> <kappa> (Polar angles)
          TRAN <t1> <t2> <t3>
          
   or
          ROTA MATRIX <r11> <r12> <r13> <r21> <r22> <r23> <r31> <r32>
          <r33>
          TRAN <t1> <t2> <t3>
          
   O/RAVE Format
          OMAT
          r11   r21   r31    (note that the rotation matrix is
          r12   r22   r32    transposed with respect to CCP4
          r13   r23   r33    or conventional matrix format)
          t1     t2      t3
          
   where
          x' = r11 x + r12 y + r13 z + t1
          y' = r21 x + r22 y + r23 z + t2
          z' = r31 x + r32 y + r33 z + t3
          
   These are the operations which map the density in the region covered
   by the input mask onto the appropriate regions in the current crystal
   form. The first operator must be the identity matrix. The mask is
   input in CCP4 mask (map mode 0) format on the input file label MSKIN1,
   and should cover just one monomer or averaging domain, NOT the whole
   unit cell. The mask grid need not agree with the program grid.
   
   If you want to apply different ncs operations to different domains of
   the protein, then each AVER card should contain a DOMAIN card to
   indicate which to domain this operator applies.
   
   The REF, STEP and EVERY cards will enable refinement of the ncs
   rotation matrices between averaging cycles. The REF card enables the
   refinement of a particular set of NCS parameters. Note that the STEP
   card allows different refinement step sizes can be used for different
   domains, however all but one EVERY card will be ignored. The refined
   matrices will be written out at the end of the log file.
   
   <dr>
          = step size for refinement of positional parameters in
          Angstrom.
          
   <dphi>
          = step size for refinement of rotational parameters in degrees.
          
   <nref>
          = the number of phase extension cycles between each parameter
          refinement.
          
   See also dm_ncs_averaging
   
  GRID <nx> <ny> <nz>
  
   Set the grid for the calculation. You may want to do this if you want
   to include your own mask or dump a map or mask (defaults: minimum
   efficient factors above Nyquist spacing).
   
  WANG <radius> <mode> [ LIMITS <rhomin> <rhomax> ]
  
   Set the averaging radius and mode for calculating the solvent mask
   (defaults: <radius>=8.0 <mode>=1 <rhomin>=0.32 <rhomax>=2.0 e/A^3).
   
   <radius>
          = radius of averaging sphere (Angstroms)
          
   <mode>
          = 1: Use weighting scheme w=1-(r/R) (Wang's method)
          = 2: Use weighting scheme w=1-(r/R)**2
          
   Heavy atoms can bias the mask calculation procedure, resulting in a
   mask of spheres around the heavy atom sites. The LIMITS card can be
   used to set the values at which the electron density is truncated
   before smoothing. To truncate heavy atoms set <rhomax> to the maximum
   electron density due to non-heavy atoms at the appropriate resolution.
   
  SCALE <scale> <bfac>
  
   Override internal scaling and scale input data by F^2 = <scale> * exp
   (<bfac> * s / 2.0) * F^2 Scaling is critical to histogram mapping and
   Sayre's equation. In some cases you may want to override the B-factor,
   but run without this card first, and consider long and hard before
   changing scale.
   
LOOKING AT YOUR OUTPUT

   Look at the free-R factor: but you will have to disentangle the output
   for the different crystal forms.
   
   The script 'multilog' can be used to roughly separate those portions
   of the output dealing with different crystal forms. Type:
> multilog name-of-your-dmmulti-logfile

CHANGES FROM 'dm'

   The XTAL keyword for separating keywords for different forms is new.
   
   The format of the AVER keyword is consistent with dm version 1.8 and
   later
   
   There are now multiple input and output reflection and solvent masks
   for the various forms.
   
   Only the last NCYC or EVERY keyword in the command file will have any
   effect, since cycles must be synchronised across the different forms.
   Only the last REF or STEP keyword in any crystal form will have an
   effect and will apply for all matrices in that form.
   
COMMON PROBLEMS

   Refinement of averaging operators only works when the first operator
   given for each domain is the identity. This restriction does not apply
   when averaging without refining the operators.
   
   Check the averaging correlation on the first cycle: this is a strong
   indication of whether the mask and matrices have been correctly
   determined.
   
   Averaging operators must be FROM the masked region TO the copy in the
   unit cell. All averaging operators are defined in orthogonal
   coordinates using the convertional CCP4/Uppsala axis conventions.
   
AUTHOR

   Kevin D. Cowtan, Department of Chemistry, University of York
   email: cowtan@yorvic.york.ac.uk
   
REFERENCES

    1. Baker D., Bystroff C., Fletterick R., Agard D. (1994) Acta Cryst
       D49 429-439
    2. Bricogne, G. (1974) Acta Cryst A30 395-405
    3. Brunger, A. T. (1992) Nature 355, 472-474
    4. Cowtan K. D., Main, P. (1993) Acta Cryst D49 148-157
    5. Sayre, D. (1974) Acta Cryst A30 180-184
    6. Schuller D. (1996) Acta Cryst D52 425-434
    7. Swanson, S. (1994) Acta Cryst D50 695-708
    8. Wang, B. C. (1985) Methods in Enzymology 115, 90-112
    9. Zhang, K. Y. J., Main P. (1990) Acta Cryst A46 377-381
       
EXAMPLES

  [ a simple solvent/histogram calculation ]
  
dmmulti                                 \
        hklin gmto.mtz                  \
        hklout gmtodm.mtz               \
        histlib dm/hist.lib             \


  [ a better solvent/histogram calculation, ]
  [ takes 2x as long, uses fixed free-R set ]
  [ starts at 3.0A and extends from there ]


dmmulti                                 \
        hklin gmto.mtz                  \
        hklout gmtodm.mtz               \
        histlib dm/hist.lib             \


  [ a two fold averaging calculation with ]
  [ two domains and refinement of the 2nd ]
  [ set of averaging matrices. ]


dmmulti \
 hklin hpattj.mtz \
 hklout dm1.mtz \
 mskin1 cwnads.mask \
 mskin2 cwglobs.mask \
 histlib /usr/people/schuller/dm/hist.lib \


  [ a two crystal averaging calculation ]
  [ where a single domain is being averaged. ]
  [ There is no ncs within either form. ]


dmmulti \
  hklin1  hkl/gmtomir.mtz  hklin2 hkl/gmtmmir.mtz  \
  hklout1 dmgmto.mtz       hklout2 dmgmtm.mtz      \
  mskin1  gmto.msk

  [ a three crystal averaging calculation ]
  [ where a single domain is being averaged. ]
  [ The first form has MIR phases and a ncs ]
  [ dimer. The second form is unphased and ]
  [ contains a monomer. The third form is ]
  [ unphased and contains a trimer. ]


dmmulti \
 hklin1 ins6a.mtz                         hklout1 dmins1.mtz \
 hklin2 ins_hagfish_tetr_T_dim.mtz        hklout2 dmins2.mtz \
 hklin3 ins_mi3_crosslinked_fred_p321.mtz hklout3 dmins3.mtz \
 mskin1 insab.msk \