ECALC (CCP4: Supported Program)

NAME

   ecalc - calculate normalised structure amplitudes

SYNOPSIS

   ecalc hklin foo.mtz hklout foo_e.mtz
   [Keyworded input]

DESCRIPTION

   The program ECALC is used to calculate normalised structure amplitudes
   for a reflection data set. The normalised structure amplitude for a
   reflection is taken as the structure amplitude divided by the product
   of the r.m.s. value of the structure amplitudes at its
   sin(theta)/lambda value and the epsilon factor which is dependent on
   the Laue group symmetry. The structure "amplitude" may be a difference
   term representing the contribution of a sub-structure, either heavy
   atoms or anomalous scatterers.

   Normalised structure amplitudes are used for direct methods programs,
   molecular replacement searches, etc. ECALC also generates the terms
   required to calculate origin-removed Pattersons.

   The normalisation procedure used is done using the "Karle" approach,
   and NOT by applying an overall temperature factor taken from a Wilson
   plot, i.e. the amplitudes are modified so that <E**2> = 1.0 in each
   resolution shell. This is necessary for macromolecular structures
   where the low resolution <I> distribution is very different from the
   Wilson ideal.

   The output MTZ file will contain all entries in the input file plus F
   E SIGE F2OR E2OR. These are described in more detail below.

KEYWORDED INPUT

   The various data control lines are identified by keywords, those
   available being:

     LABIN (compulsory), LABOUT, EXCLUDE, MODDIFF, RESOLUTION, SCALE,
     SHELL, SPACEGROUP, TITLE, MULTAN, REFLECTIONS, SNB

  LABIN <program label>=<file label> ...

   Column label assignments for H, K, L, and optionally FP, SIGFP, FPH,
   SIGFPH, DPH, SIGDPH.

   FP is one structure amplitude, possibly a native amplitude, or maybe
   F(+) for data with an anomalous signal
   SIGFP is its standard deviation
   FPH is another structure amplitude, either a derivative set or F(-)
   SIGFPH is its standard deviation
   DPH is the derivative anomalous difference
   SIGDPH is its standard deviation

   The behavior of the program is largely governed by the column
   assignments. Data is assumed missing if the associated SIG is less
   than or equal to 0, or the missing number flag is set.
    1. If only FP (and SIGFP) are assigned, the amplitude assigned to FP
       is used to calculate the E value.
    2. If FPH is also assigned, the structure "amplitude" used to
       calculate the F and E values for output is the magnitude of the
       difference between the columns assigned to FP and FPH (i.e., if FP
       is a native, and FHP a derivative amplitude this is the
       isomorphous difference, or if FP is set as F(+) and FPH as F(-) it
       is an anomalous difference ). If using this to define an
       "anomalous difference" it is sensible to use the EXCLUDE keyword
       to exclude centric terms. The difference may be reduced to take
       into account the overestimation due to the noise in each
       measurement. See MODDIFF.
    3. If DPH is assigned, then none of FP SIGFP FPH or SIGFPH should be
       assigned. The structure "amplitude" used to calculate the F and E
       values for output is the magnitude of the anomalous difference
       DPH. Centric reflections will not be used. Again, the difference
       may be reduced to take into account the overestimation due to the
       noise in the measurement. See MODDIFF.

  EXCLUDE [CENTRIC] [SIGP <nsigp>] [SIGPH <nsigph>] [FPMAX <fpmax>] [FPHMAX
  <fphmax>] [DIFF <diffmax>]

   Set criteria for excluding data from the generation of E values. Large
   errors can distort the normalisation seriously.

   Excluded data will still be written to the output file but there will
   be no associated value for E; it will be flagged as a "Missing
   number". The default is to include all data.

   The following subkeys select the tests to be applied:

        CENTRIC
                exclude all centric reflections - required for the use of
                anomalous differences

        SIGP <nsigp>
                exclude reflections if FP < <nsigp>* SIGP

        SIGPH <nsigph>
                exclude reflections if FPH < <nsigph>* SIGPH

        FPMAx <fpmax>
                exclude reflections if FP > <fpmax>

        FPHMax <fphmax>
                exclude reflections if FPH > <fphmax>

        DIFF <diffmax>
                exclude reflections if the isomorphous or anomalous
                difference is greater than <diffmax> See LABIN and
                MODDIFF for further discussion on generating these
                differences.

  MODDIFF [ YES | NO ]

   Default NO.

   In general the differences used to estimate the isomorphous or
   anomalous contributions will be overestimated as a result of noise in
   the measurements. It is possible to apply a correction and approximate
   the difference by sqrt( |FPH-FP|**2 - Sqrt*(SIGFP**2 + SIGFPH**2) ) or
   sqrt( |DPH|**2 - Sqrt*(SIGDPH**2) ). If the term to be square-rooted
   is negative the difference is set to 0.0. It is obviously important
   that the standard deviations are reasonably reliable.

  LABOUT <program label>=<file label> ...

   This card is required when outputting reflections to an MTZ file to
   assign customised labels to the additional output columns.

   The following columns will be output and labels can be assigned.
     F    E  SIGE      F2OR      E2OR

   where

   F
          is the "amplitude" used for the normalisation, either FP or
          |FPH-FP| or |DPH|

   SIGF
          is the standard deviation of this "amplitude"; either SIGFP or
          Sqrt*(SIGFP**2 + SIGFPH**2) or |SIGDPH|

   E and SIGE
          the normalised "amplitude" and standard deviation modified so
          that <E**2> = 1.0 in all resolution shells.

   F2OR and E2OR
          The terms required for calculating an origin removed Patterson.
          F2OR = F**2 -<E**2> and E2OR = E**2 - <E**2> = E**2 - 1.0. They
          can be used as input to the fft programs using LABI I=F2OR, etc
          ( See fft documentation)

  RESOLUTION <resmax>

   Default: take the maximum resolution from the MTZ header. The value
   <resmax> is the resolution cutoff in Angstroms. Usually 0 to include
   all reflections.

  SHELL <number>

   Specifies the approximate number (default 200) of reflections wanted
   to average for each shell. If this is too small you are likely to get
   wildly fluctuating or even shells with no reflections at all. The
   program will stop with the message Empty shell. If it is too big there
   may not be enough shells to give sensible averages. Note this number
   refers to independent reflections; however the output shows the number
   in a hemisphere of reciprocal space.

  SPACEGROUP <group>

   The space group is read from file with logical name SYMOP. Default:
   Take the SPACEGROUP from the MTZ header. Group is the space group name
   or number in International Tables. Only the rotation part of the
   symmetry operations is used, so for example 177 (P622), 178 (P6122)
   and 179 (P6522) are all equivalent. This keyword is required only if
   the symmetry information in the reflection file header is missing or
   wrong.

  TITLE <title>

   Title for the output file (up to 80 characters). The text PRODUCED BY
   ECALC will be appended to this title automatically.

  SCALE <scale>

   The output columns F will be scaled by the value <scale>. The default
   scale is 1.0.

  MULTAN

   No further data are required on this line. Outputs E values in a
   formatted ASCII file e.g. for Direct Method packages such as MULTAN.
   Normally however, most Direct Method programs will calculate Es
   internally. Default is to output E values in standard MTZ format e.g.,
   for ALMN.

  SNB

   No further data are required on this line. Outputs E values in a
   formatted ASCII file suitable for SnB (Shake-and-Bake).

  REFLECTIONS <nwant>

   This only applies when outputting reflections to an ASCII file and not
   an MTZ file i.e. in conjunction with the MULTAN/SNB cards. The largest
   <nwant> Es are written to HKLOUT, the default is to write all
   reflections. This cutoff may be necessary because some programs will
   only accept a limited number of reflections. Also, when generating Es
   from isomorphous or anomalous differences, i.e. |FPH-FP| or
   |F(+)-F(-)|, small E values will not necessarily reflect the true E
   value calculated from the heavy atom sub-structure. For instance, for
   anomalous differences all the centric reflections have an E of zero.

INPUT AND OUTPUT FILES

   The input files are

   The control data file.

   HKLIN
          The input reflection data file in standard MTZ format.

   HKLOUT
          If no MULTAN/SNB keyword is specified, the output file is a
          reflection data file in MTZ format containing the items H K L
          (all input) + F E SIGE where F=FP is copied from the input file
          if only FP is asigned, or F=sqrt(max((FPH-FP)^2 -
          SIGFP^2-SIGFPH^2,0)) if FPH is assigned as well. E is the
          normalised structure amplitude, SIGE is its standard deviation.

   For the MULTAN option the output is H K L 1000*E in FORMAT(3I4,I6)
   terminated by E=-1.

   SYMOP
          The library symmetry data file, normally defaulted.

PRINTER OUTPUT

   The line printer output may be divided into the following sections:
    1. Echo of the input control data.
    2. A table showing the distribution of the reflections in shells
       (chosen to give roughly equal numbers per shell) with mean d*^3,
       F^2, E^2-1 and (E^2-1)^2.
    3. Scatter plot of F versus d*^2 with a smoothed plot of r.m.s. F
       versus d*^2 superimposed.
    4. Mean values of E^2 and (E^2-1)^2 by parity groups.
    5. Mean values of E^n where n = 1 to 6.
       Mean values of |E^2-1|^n where n = 1 to 3.
       For each mean the theoretical value for the acentric, centric and
       hypercentric distributions is also tabulated.
    6. Cumulative distribution of E's for centric and acentric with
       theoretical values. This table can also be graphed with xloggraph.

EXAMPLES

   Example of the control data for calculating a set of normalised
   structure factors.


ecalc hklin junk1.mtz hklout junk2.mtz << eof
TITLE TEST OF PROGRAM ECALC WITH C2HKL REFLECTION DATA
LABI FP=FO  SIGFP=SIGFO
eof


ecalc hklin junk1.mtz hklout junk2.dat << eof
TITLE TEST OF PROGRAM ECALC For isomorphous differences
LABI FP=FO  SIGFP=SIGFO  FPH=FPH1 SIGFPH=SIGFPH1
MULTAN
REFLECTION 1500
eof


ecalc hklin junk1.mtz hklout junk2.dat << eof
TITLE TEST OF PROGRAM ECALC For anomalous differences
LABI FP=FO(+)  SIGFP=SIGFO(+) FPH=FO(-)  SIGFP=SIGFO(-)
EXCL CENTRIC
LABO E=E_ano
eof


ecalc hklin junk1.mtz hklout junk2.dat << eof
TITLE TEST OF PROGRAM ECALC For anomalous differences from DPH
LABI DPH=DANO  SIGDPH=SIGDANO
EXCL CENTRIC
LABO E=E_dano
eof


ecalc hklin junk1.mtz hklout junk2.mtz << eof
TITL Es from isomorphous differences removing sigma bias etc
LABI FP=FP SIGFP=SIGFP FPH=FPHderv1 SIGFPH=SIGFPHderv1
EXCLUDE SIGP 3
EXCLUDE SIGPH 3
EXCLUDE DIFF 120
MODDIFF YES
eof

  Using coefficients from ECALC for origin-removed Patterson map

   ECALC produces squared F's or square E's with the origin contribution
   removed in the F2OR or E2OR columns. These can be used as input to FFT
   to produce an origin-removed Patterson function. Since the terms may
   be positive or negative you need to assign LABI I=F2OR in the fft, not
   F1 - see below.

   For example:
ecalc hklin nat_der_scal.mtz hklout nat_der_scal_e.mtz << eof-ec
exclude SIGP 2 SIGPH 2 DIFF 100.
scale 1.
shell 50
labin FP=F_CNAT2 SIGFP=SIGF_CNAT2   FPH=F_CEMS SIGFPH=SIGF_CEMS
labout F=DISO E=E F2OR=F2OR E2OR=E2OR
eof-ec

fft hklin nat_der_scal_e.mtz mapout pat_der.map << eof-fft
title origin removed diff-patterson
PATT
LABIN I=F2OR
END
eof-fft

   (With thanks to Steve Prince)

PROGRAM STRUCTURE

   The program structure is straightforward and involves three passes
   through the input reflection data file. The structure is outlined
   below:
     * Open files
     * Pass 1 through reflection data: Find maximum F and S values and
       count the number of reflections. Print these values.
     * Pass 2 through reflection data: Collect F^2 values in bins of d*^3
       (sums and numbers of reflections). Print a table of these results.
       Apply adjacent channel smoothing for points giving the average F^2
       and d*^3 values for these bins.
     * Open the output mtz file.
     * Pass 3 through reflection data: Calculate E values (using the
       function AVF, write the output reflection data and collect data
       for the statistics.
     * Print scatter plot, average values of E^1 to E^6 and cumulative
       distribution of E's.

AUTHOR

   Originator: Ian Tickle
   Contact: Ian Tickle, Birkbeck College