NAME
       libfft  -  fast Fourier transform routines used in the fft
       program

PROGRAM STRUCTURE
       Control of the calculation

       A small main program must be set up as  follows  in  order
       to  run  the program.
             REAL     X(size)
             IS = size
             CALL FFTCTL(X,IS)
             STOP
             END

       The  value  of size determines the amount of work space to
       be  used  by the program.   The  subroutine  FFTCTL  calls
       CARDIN to read in  and interpret the control data. A space
       group specific routine is then  called for  the  requested
       space  group.  For space group number 'n' the name of  the
       subroutine called is FFTn  (e.g.  FFT19  for  space  group
       P212121)

       The  flow of control in a typical  space  group  dependent
       routine  is  as follows:

       1)     Calculate the dimensioning parameters which  decide
              how many  times  the first and second passes of the
              program will have to be executed. The  variable  P1
              is  the  number of planes of constant h that can be
              accommodated  in the buffer while the first  trans-
              form  is  being calculated. The variable  P2 is the
              maximum number of planes of electron  density  that
              can  be  calculated  at one time in the second pass
              through the data.

       2)     Calculate the first of  the  three  Fourier  trans-
              forms.  This   consists   of three steps which  are
              repeated  until  the  structure  factor  input   is
              exhausted.

       a)  Read  a block of structure factors into the  transform
       buffer  for some h, all k, and all l.

       b) Calculate the Fourier transforms  along  k  (or  l,  if
       z-sections  are being calculated).

       c)  Write the intermediate results on  the  scratch  file.
       These  are written in blocks  which  contain  all  of  the
       available  values for h, P2 values of k (or l), and all of
       the values of l (or k). If  the  space group  is  one   of
       the  orthorhombic  space  groups  for  which  the interme-
       diate results for -h, k, l are derived from those for  +h,
       k,  l  by  symmetry relations, the symmetry relations  are
       applied  and  the intermediate results for -h,  k,  l  are
       also written.

       3)     Calculate  the  transforms  on  the  remaining  two
              dimensions. This consists of three steps which  are
              repeated  until   all  of  the  desired  planes  of
              electron density have been calculated.

       a) Read through the scratch file picking  up  all  of  the
       values   of  h and l (or k) for the  range  of  k  (or  l)
       values  currently   being  processed.  The  data  must  be
       placed in memory in such a way that after the last Fourier
       transform the  resulting  real  numbers  are   stored   by
       planes of electron density.

       b) Calculate the remaining two Fourier transforms.

       c)  Write  the  electron  density sections. If this is the
       first block of sections calculated, derive the scale  fac-
       tors.

       4)     After  all  of  the  electron density sections  are
              calculated,  terminate the output  file  and  print
              the timing statistics.

       The  steps  described above are carried out  by  different
       subroutines for  the  various  space  groups.  The   table
       given   below   shows    which subroutines are used in the
       various steps:

        Space  Control   2a     2b     2c      3a        3b         3c
       group   prog
       P1      FFT1    SFIPYC CMPLFT YOUT2    YIN2  CMPLFT/HERMFT PRINTY
       P1bar   FFT2    SFIPYR REALFT YOUT2    YIN2  CMPLFT/HERMFT PRINTY
       P2      FFT3    SFIPYC HERMFT YOUT1    YIN1  REALFT/HERMFT PRINTY
       P21     FFT4    SFIPYC SDIAD  YOUT2    YIN2  CMPLFT/HERMFT PRINTY
       P2/m    FFT10   SFIPYR RSYMFT YOUT1    YIN1  REALFT/HERMFT PRINTY
       P222    FFT16   SFIPYC HERMFT YOUT1    YIN3  REALFT/HERMFT PRINTY
                                     TRNSP1
                                     YOUT1
       P21212  FFT18   SFIPYC SDIAD  YOUT2    YIN5  CMPLFT/HERMFT PRINTY
                                     TRANSP3
                                     YOUT2
       P21212  FFTR18  SFIPYC SDIAD  YOUT4    YIN4  CMPLFT/HERMFT PRINTY
                                     TRNSPR
                                     YOUT4
       P212121 FFT19   SFIPZC MULTI  ZOUT2    ZIN4  CMPLFT/HERMFT PRINTZ
                              SDIAD  TRNSP2
                              DIVI   ZOUT2
       I222    FFT23   SFIIYC HERMFT YOUT1I   YIN3  REALFT/HERMFT PRINTY
                              HSEP1I TRNP1I
                                     YOUT1I
       Pmmm    FFT47   SFIPYR RSYMFT ZOUT47   ZIN47 RSYMFT/RSYMFT PRINTZ
       P41212  FFT92   SFIP92 SDIAD  YOUT92   YIN92 CMPLFT/HERMFT PRINTZ
       P43212  FFT92   SFIP92 SDIAD  YOUT92   YIN92 CMPLFT/HERMFT PRINTZ
       P31     FFT144  SFIPZC CMPLFT OUT144   ZIN   CMPLFT/HERMFT PRINTZ
       P32     FFT144  SFIPZC CMPLFT OUT144   ZIN   CMPLFT/HERMFT PRINTZ
       R3      FFT147  SFIPZ3 CMPLFT OUT147   ZIN   CMPLFT/HERMFT PRINTZ
       P3121   FFT152  SFIP92 CMPLFT OUT152   ZIN   CMPLFT/HERMFT PRINTZ
       P3221   FFT152  SFIP92 CMPLFT OUT152   ZIN   CMPLFT/HERMFT PRINTZ


       The structure factor input subroutine (step 2b) calls  the
       subroutine  GETHKL  and  its entry point GETF to input the
       reflection data (via the  MTZ routines), to calculate  the
       required coefficients from the  selected  data items, and,
       if required, to generate symmetry related reflection data.
       The  subroutine   further   prepares  the  terms  required
       for  calculating  the transform.

   Description of the FFT routines
       The  main  entry  to  the  FFT  subroutines  is  via   the
       subroutine   CMPLFT  which is an organisational subroutine
       calling the following subroutines:

       a)   SRFP (Symmetrised Reordering Factoring Program)  fac-
       tors  N   and   saves  some  information about the factors
       which will be useful later.

       b)   MDFTKD  (Multi-Dimensional  Fourier  Transform   Ker-
       nel   Driver)   goes  through the list of factors of N and
       calls an appropriate  subroutine to deal with each one. If
       one  inspects the calling sequences for  the is a trick of
       coding due to G. Sande  which  will   force   any    idiot
       FORTRAN compiler to produce optimal code for subscipts  of
       the  form I*J+K by converting  them   into   simple   sub-
       scripts.   This   trick   is perfectly legitimate standard
       FORTRAN; if your compiler  objects,  it is compiling some-
       thing other than FORTRAN.

       c)   DIPRP  (Double  In-Place  Reordering  Program)  sorts
       the   Fourier transform into its natural order  using  the
       information saved by SRFP.  This subroutine contains a set
       of fourteen nested DO-loops, which may cause some  compil-
       ers  trouble. If so, reduce the value of the variable NEST
       in both  SRFP and DIPRP from fourteen  to   some   smaller
       value,  remove  the  appropriate  number of loops from the
       innermost   part  of the nest, and replace the variable  N
       inside  the  loops with  with  the control variable of the
       innermost remaining loop.

       MDFTKD calls RPCFTK for all factors not treated as special
       cases   by  another  subroutine. RPCFTK is capable of han-
       dling all factors  from   three  to  nineteen,  inclusive.
       Therefore the minimum requirement for the  program to work
       is R2CFTK and RPCFTK. There is  a  substantial   advantage
       in   using  specific routines for other low factors and in
       the present version subroutines R3CFTK, R4CFTK, R5CFTK and
       R8CFTK  are  used  for  factors of 3,  4,  5 and 8 respec-
       tively.

       In total six Fourier transform subroutines  are   provided
       to   exploit  various  transform  symmetries. As mentioned
       above the basic  subroutine  is CMPLFT, which calculates a
       complex  Fourier  transform  on  one  dimension  of multi-
       dimensional data. The remaining five subroutines are  con-
       cerned   with data which have special symmetries along the
       axis  being  transformed;  in all cases they calculate the
       unique  portion  of the  transform  given  only the unique
       portion of the data. The subroutines  provided  correspond
       to  the  reciprocal space symmetries asociated with diads,
       screw  diads,  inversion centres, and mirror planes. These
       subroutines  are  also  sufficient for  the calculation of
       structure factors from electron  density  maps  containing
       the  specified  symmetry  elements. No subroutines to deal
       with glide planes have yet been written. All of the  other
       subroutines  call CMPLFT,  and  all  of them have the same
       parameter structure.

        CMPLFT

             CMPLFT is called as follows:

                    CALL CMPLFT (X, Y, N, I)

       where X and Y are  the  real  and   imaginary   parts   of
       the   data   to   be  transformed,  N is the length of the
       transform, and I is an  integer  array of length  5  which
       specifies  the  mapping function to index through X and Y.
       If X and Y are dimensioned for k subscripts, each with   a
       range   ni,   the elements of I are specified thus for the
       j'th subscript:

                k
        I(1) =  Pi  ni = total size of the array.
              i=1

               j-1
        I(2) =  Pi  ni = separation between elements of X differing
              i=1        by 1 in subscript j.

                j
        I(3) =  Pi  ni = separation between elements of X differing
               i=1       by 1 in subscript j+1.

        I(4) = I(2)

        I(5) = 1.


       The extra information in I(4) and I(5)  is  used  to  pro-
       vide   some   extra  flexibility  in  indexing  as will be
       described later. The values are used  in  DOloop  indices.
       When calculating multiple transforms in parallel one  must
       cover all elements of X and Y for which subscript  j   has
       some   particular value. To cover all elements for which j
       = j0, the  following  formula  is used.

                  J1 = (J0 - 1)*I(2) + 1
                  DO 100 J2 = J1, I(1), I(3)
                  J3 = J2 + I(4) - 1
                  DO 100 J = J2, J3, I(5)
                  ........
              100 CONTINUE


       Naturally  the  DO-loop  parameters  in  the  actual  pro-
       grams   are   not subscripted.

       The  parameter  I(5) is a spacing between consecutive ele-
       ments of X and Y which permits the interleaving of X and Y
       in  storage  --  i.e. they may be stored as normal FORTRAN
       complex numbers with the real and imaginary parts  occupy-
       ing consecutive storage locations. In this case I(5)  =  2
       and  all other elements of I are  doubled.  The  parameter
       I(4)  is  used  in  those  cases in which it is desired to
       avoid calculating the transform of part  of  the data; for
       example certain rows may be known to be zero.

       Another use for I(4) and I(5) is in transforming the first
       dimension of an array. In this  case  application  of  the
       given   formulae   causes  the calculation to be driven by
       the outer DO-loop. The  following  definitions cause it to
       be driven more efficiently by the inner loop.

                          k
             I(1) = I(2)  Pi  ni.
                         i=1

             I(2) = 1 for separate real and imaginary  parts,
                    2  for  interleaved data.

             I(3) = I(1)
             I(4) = I(1)
             I(5) = I(2)n1


       The   following   examples  illustrate  the  use  of  CMPL
       FT   on   a three-dimensional problem for the  two   cases
       of  separately  stored  and interleaved data.

             DIMENSION X(30,20,40), Y(30,20,40), Z(30,20,40), A(2)
             DIMENSION I(5)
             COMPLEX Z
             EQUIVALENCE (A(1), Z(1,1,1))
        C    first separate data
             I(1) = 30*20*40
             I(2) = 30*20
             I(3) = 30*20*40
             I(4) = 30*20
             I(5) = 1
             CALL CMPLFT (X, Y, 40, I)
             I(2) = 30
             I(3) = 30*20
             I(4) = 30
             CALL CMPLFT (X, Y, 20, I)
             I(2) = 1
             I(3) = I(1)
             I(4) = I(1)
             I(5) = 30
             CALL CMPLFT (X, Y, 30, I)
        C    now for the case of fortran complex data
             I(1) = 2*30*20*40
             I(2) = 2*30*20
             I(3) = 2*30*20*40
             I(4) = 2*30*20
             I(5) = 2
             CALL CMPLFT (A(1), A(2), 40, I)
             I(2) = 2*30
             I(3) = 2*30*20
             I(4) = 2*30
             CALL CMPLFT (A(1), A(2), 20, I)
             I(2) = 2
             I(3) = I(1)
             I(4) = I(1)
             I(5) = 2*30
             CALL CMPLFT (A(1), A(2), 30, I)
             STOP
             END


   HERMFT
       HERMFT  is designed to transform data which  is  Hermitian
       symmetric along   the   axis   being   transformed   .  It
       accepts   as   input  the  unique half of the sequence and
       replaces it with  the  real  transform.  Since   a  Hermi-
       tian  symmetric  sequence of length 2N contains N+1 unique
       real numbers and N-1 unique imaginary  numbers,  the  real
       value  for  X(N)  is stored in the imaginary part of X(0).
       (Add one to the  true  subscripts  to  obtain  the FORTRAN
       subscripts). The call is

                  CALL HERMFT (X, Y, N, I)

       where I is as described for CMPLFT. The program returns 2N
       real  numbers, with the even terms (when indexed  starting
       from zero) in  X  and  the  odd terms in Y.

   REALFT
       REALFT  is the inverse of HERMFT. Given a real sequence of
       length 2N it will return the unique portion of the Fourier
       transform   as   a   complex  sequence  of length N+1. The
       first  and  last  elements  of  the  sequence returned are
       real.  Note that this differs from  the  arrangement  used
       in HERMFT. The reason for this choice is that the point at
       1/2 is frequently of special interest. The input data must
       allow for the extra location. The call is

                         CALL REALFT (X, Y, N, I)

       where X contains the even numbered part of the data and  Y
       contains  the  odd  numbered  part of the data. (True sub-
       scripts, not FORTRAN  subscripts).   On  return  the  real
       parts will be in X and the imaginary parts will be in Y.

   RSYMFT
       RSYMFT   calculates   the  Fourier  transform  of  a  real
       symmetric sequence. The transform is also  real  and  sym-
       metric.  A  real  symmetric sequence of length 2N contains
       N+1 unique points. These are the   input   to  RSYMFT;  no
       scratch locations are required. The call is.

                         CALL RSYMFT (X, N, I)

       where  the  axis  being transformed contains N+1 values. N
       must be a multiple of four. RSYMFT calls HERMFT.

   SDIAD
       SDIAD calculates the Fourier transform of a sequence  with
       alternating  Hermitian symmetry and anti-symmetry,  as  is
       found  with  a  screw  diad passing  through  the  origin.
       Only  the  unique  half  of the data is presented, and the
       unique half of the Fourier transform  is   returned.   The
       remaining  half  of the transform is the complex conjugate
       of  the  first  half.  One scratch location is required at
       the end of each sequence transformed.  The call is
                          CALL SDIAD (X, Y, N, I)

       where  the length of the axis to be transformed is N+1  to
       allow  for  the scratch location.  The  correct  transform
       value  is returned in  the  scratch location, so it is not
       a complete loss. N must be even.