MAPMASK (CCP4: Supported Program)
                                       
NAME

   mapmask - map/mask extend program
   
SYNOPSIS

   mapmask MAPIN/MSKIN/MAPIN1/MSKIN1 foo.map [ MAPIN2/MSKIN2 bar.map ] [
   XYZIN foo.pdb ] [ MAPOUT foobar.map ] [ MSKOUT foobar.msk ]
   [Keyworded Input]
   
DESCRIPTION

   `mapmask' is a general map and mask manipulation program. It will
   change the extent of a map or mask file, re-order a map or mask, scale
   a map or mask, and generate a mask from a map and vice versa. It will
   also produce a print out of arbitrary map or mask sections. It can
   combine two input maps or masks to produce a sum or product map, or a
   solvent flattened/flipped map.
   
   It can be used in conjunction with SFALL to make a solvent mask, which
   can be used for solvent flattening using 'dm' or FLATMAP. In this case
   SFALL is used to make a atom map, and then MAPMASK is used to mask the
   non-zero areas of this map.
   
   Scaling options from Andrew Leslie's FLATMAP program can be used to
   scale the map for solvent flattening (SCALE card). Jan Pieter
   Abraham's solvent flipping and density truncation techniques may be
   applied (SOLV card).
   
INPUT/OUTPUT FILES

  MAPIN/MAPIN1/MSKIN/MSKIN1
  
   Input map or mask. If MAPIN or MAPIN1 is specified, the values of the
   map grid points will converted to real numbers (even if the input file
   is a mask). If MSKIN or MSKIN1 is specified, the values of the grid
   points will be set to 0 or 1 (even if the input file is a real map).
   
  MAPIN2/MSKIN2
  
   Second input map, used when combining maps or performing solvent
   flattening (used by SOLV, MAPS cards). Must be on the same grid as the
   first input map.
   
  MAPLIM
  
   is for use with XYZLIM MATCH option.
   
  XYZIN
  
   is for use with BORDER option.
   
  MAPOUT
  
   is an output map.
   
  MSKOUT
  
   is an output mask, 1 wherever MAP>MSKCUT and 0 elsewhere.
   
   Either MAPOUT, or MSKOUT, or neither, or both may be assigned. If both
   are assigned then MAPOUT will contain the real map values and MSKOUT
   the values 0/1.
   
KEYWORDED INPUT

   Possible keywords are:
   
     AXIS, BORDER, EXTEND, MAPS, MASK, MODY, PAD, PRINT, SCALE, SOLV,
     SYMMETRY, XYZLIM.
     
  XYZLIM [ASU] [CELL] [MATCH] <x1> <x2> <y1> <y2> <z1> <z2>
  
   Set the output map extent as `extend'. <x1>-<z2> are given in grid
   units or in fractional coordinates. It is possible to automatically
   extend to the CCP4 default asymmetric unit, or a whole unit cell, by
   specifying `XYZLIM ASU' or `XYZLIM CELL'. It is also possible to
   extend the map to match another map (given as MAPLIM) by specifiying
   `XYZLIM MATCH'. The default is to keep the extent of the input map.
   
  BORDER <n>
  
   Extend the map to cover the volume of a coordinate model given in
   XYZIN, as `extend'. <n> is the border in Angstrom around the edge of
   the model.
   
  EXTEND COPY | XTAL | OVERLAP
  
   Selects how the map is to be extended.
   
   COPY
          copies density from the input to the output map without
          applying symmetry or cell repeat.
          
   XTAL
          applies both symmetry and cell repeat to generate density
          outside the input map extent
          
   OVERLAP
          applies both symmetry and cell repeat to generate density, and
          when multiple values are available for a grid point, the
          highest is taken. This option can be used to generate a solvent
          mask from an averaging mask covering the whole complex.
          
   Default: If the input map contains the output map: EXTEND COPY. If the
   input map must be extended: EXTEND XTAL.
   
  PAD <rho>
  
   Normally if you try to extend a map which does not contain at least an
   (arbitrary) asymmetric unit, mapmask will give an error since it will
   be impossible to generate some of the map. PAD <rho> supresses the
   error message and specifies a density value <rho> to be used for such
   regions.
   
  SYMMETRY <spacegroup name or number>
  
   Override the spacegroup of the input map.
   
  AXIS <fast> <medium> <slow>
  
   Change the output axis order. Default is input axis order. <fast>,
   <medium>, <slow> must be some permutation of X Y Z.
   
  MASK [CUT <mskcut>] [FRAC <mskfrc>] [VOLUME <mskvol>]
  
   Set the threshold value for making a mask from a map: all density
   values above this level in the final map will be set to 1.0 in the
   output mask if one is specified.
   
   CUT <mskcut>
          sets the density cutoff value directly.
          
   FRAC <mskfrc>
          sets the fraction of the output mask that should be above the
          threshold. This is used when making a solvent mask, and will
          work correctly on a unit cell or asymmetric unit.
          
   VOLUME <mskvol>
          sets the volume of the mask that should be above the threshold
          as a fraction of the unit cell volume. This is used when making
          an averaging mask from a correlation map (see MAPROT).
          
  MODE <logical_name1> [ <logical_name2> ]
  
   [Optional]
   Overrides the default mapmask behaviour of looking for any assignment
   or file with a likely name. The names correspond to logical
   assignments on the command line (e.g. MODE MSKIN MAPIN2). This keyword
   is not compulsory but is recommended to explicitly ensure that the
   correct data is being used as input.
   
  PRINT MAP <axis> [ <first> [ <last> [ <step> ]]]
  
   Print out map sections using the specified section axis. <axis> must
   be one of X/Y/Z and specifies the section axis. <first>, <last> and
   <step> specify the range of sections to print. The density values are
   output as integers, and so this command will normally be used in
   conjunction with the SCALE card.
   
  PRINT MASK <axis> [ <first> [ <last> [ <step> ]]]
  
   Print out mask sections using the specified section axis. <axis> must
   be one of X/Y/Z and specifies the section axis. <first>, <last> and
   <step> specify the range of sections to print. Density values below
   the current density cutoff will be marked as `*', density values above
   the cutoff as ` '.
   
  SCALE [FACTOR [c1 [c2]]]
  
   Multiply the map by <c1> and add <c2>. Thus rho'=rho*<c1>+<c2>.
   Default <c1>=1.0, <c2>=0.0.
   
  SCALE [SIGMA [c1 [c2]]]
  
   Scale the map to have a standard deviation of <c1> and a mean of <c2>.
   Default <c1>=1.0, <c2>=0.0.
   
  SCALE [MEAN [rhop [rhos]]]
  
   Scale the map so that the mean of the protein region is <rhop> and the
   mean of the solvent region is <rhos>. This option attempts to put the
   density on an absolute scale and depends on the low resolution terms
   being used in the map calculation. MSKIN2 must be assigned. Default
   <c1>=0.433, <c2>=0.330.
   
  SCALE [RATIO [ratio]]
  
   Scale the map so that the standard deviation of the protein region is
   <ratio> times the mean of the protein region. As the values of the
   electron density are approximately normally distributed about the
   mean, one can use standard tables of the area under a Gaussian curve.
   Thus <ratio>=0.5 corresponds to approximately 31% of the grid points
   in the protein being negative, <ratio>=1.0 corresponds to 16% being
   negative. Default <ratio>=1.0.
   
  SOLV [FLIP <flipfac>] [ATTN <attnu>]
  
   Perform solvent flattening on MAPIN1 using the mask MSKIN2. If FLIP is
   specified, the density shifts are multiplied by <flipfac>, thus
   <flipfac>=1.0 corresponds to solvent flattening, <flipfac>=2.0
   corresponds to solvent flipping. If ATTN is specified, then negative
   density in the protein region is multiplied by <attnu>. <attnu>=0.0
   corresponds to density truncation. Default <flipfac>=1.0, <attnu>=1.0.
   
  MAPS ADD/MULT
  
   Combine maps by addition or multiplication. No scaling is performed.
   MAP/MSKIN1 and MAP/MSKIN2 must be specified.
   
EXAMPLES

  Simple unix example script found in $CEXAM/unix/runnable/
  
     mapmask.exam (Contains several examples of how mapmask can be used).
   
   (A vms version found in $CEXAM/vms/mapmask.com)
   
  ....and non runnable examples in $CEXAM/unix/non-runnable/
  
     mapcutting (using ncsmask, mapmask and overlapmap).
   
SEE ALSO

   maprot, ncsmask, sfall, bones2pdb.