MAPROT (CCP4: Supported Program)
                                       
NAME

   maprot - map skewing, interpolating, rotating, averaging and
   correlation masking program
   
SYNOPSIS

   maprot MAPIN foo.map [ WRKIN bar.map ] [ MSKIN bar.msk ] [ MAPOUT
   foobar.map ] [ WRKOUT foobar.map ] [ CUTOUT foobar.map ]
   [Keyworded input]
   
DESCRIPTION

   `maprot' is a general map skewing, interpolating, rotating and
   averaging program. It can be used to interpolate a map onto a coarser
   or finer grid, to skew density into a different unit cell, to rotate a
   map to allow plotting of arbitrary sections, to rotate fragments for
   molecular replacement or NCS searching, or as part of a single- or
   multi-crystal averaging calculation. It can also be used to generate
   `correlation maps' for the automatic determination of averaging masks
   (reference [1]). Finally, it may be used to 'cut' density from a map
   and transfer it into another cell with or without a rotation. This is
   a step in the identification of cross-crystal translations, and
   general 6-d ncs searches.
   
   `maprot' works with two maps. The first is the `cell' map, which obeys
   the crystall symmetry and unit cell repeat. The second is 'work' map
   which does NOT have any symmetry or repeat. The input cell map (MAPIN)
   must generally cover exactly one unit cell. The work map may store
   density copied from the cell map, or supply density to be copied into
   the cell map.
   
   Multiple transformation operators may be supplied. When copying
   density from the cell map into the work map, then all the related
   regions of the cell map are all averaged onto the work map. If a mask
   is specified for the work map, then it is only filled within this
   mask.
   
   It is also possible to expand from the work map onto the crystal map.
   This allows a full map averaging calculation to be performed in two
   steps, or multi-xtal averaging to be performed by multiple runs of the
   program.
   
   The correlation mode produces a `local correlation map' from the input
   density (either from the crystal-map in the case of a single crystal
   with NCS, or between the crystal- and work-maps in the multi-crystal
   case). This can be contoured in a graphics program to locate the
   NCS-related part of the unit cell, and/or used to generate an
   averaging mask using `mapmask'. Multiple correlation maps from
   different combinations of operators can be combined by summation in
   `mapmask' (Note: In the case of proper NCS, a correlation mask will
   show the multimer. In the case of improper NCS it will give just one
   monomer).
   
   Finally, `maprot' can be used to cut a region of density out of a map
   and insert it into a blank map, as a step in a phased NCS
   determination or cross-crystal translation function. In this mode only
   the work map and mask are supplied. The crystal map cell and grid are
   set by program keywords. The masked density is transferred from the
   work map into the crystal map using `MODE TO' and the supplied
   operator (which may be the identity operator). Only that portion of
   the crystal map covering the masked density is output to `CUTOUT'.
   
   Remember that "cell" maps will obey crystal symmetry and unit cell
   repeats; "work" maps do not. See the examples for the calculation you
   are performing.
   
INPUT/OUTPUT FILES

  MAPIN
  
   Input crystal map. This must cover the whole unit cell (not an
   asymmetric unit). A suitable map may be prepared using the `mapmask'
   with just the `XYZLIM CELL' keyword.
   
  WRKIN
  
   Optional starting density for the work map. If this map is not
   supplied, the density in the work map defaults to zero, and the grid
   sampling and extent will be determined from MSKIN or the user keywords
   (BE CAREFUL if you have created a "dummy" map using a set of atomic
   coordinates; it is important to scale that map by 0.00 to avoid
   transferring unwanted electron density into the output work map. See
   example). The values of WRKIN outside any input mask will remain
   unchanged in WRKOUT, the values inside a mask will be scale * (initial
   value + rotated density 1 + rotated density 2 + ...)
   
  MSKIN
  
   Optional mask for the work map. This can determine the grid and cell
   for the work map, and must be consistent with WRKIN. If neither WRKIN
   nor MSKIN are specified, then the work map must be described by the
   CELL, GRID, XYZLIM cards. If a mask is not specified, then the whole
   of the work map will be considered inside the mask and filled with
   rotated density.
   
  MAPOUT
  
   is the final crystal map. This will only differ from MAPIN if the MODE
   TO or MODE BOTH options are used.
   
  WRKOUT
  
   is the output work map, which will contain rotated density from the
   cell MAPIN plus density transferred from WRKIN.
   
  CUTOUT
  
   is the output map from density cutting, containing the rotated masked
   data. This map only covers the volume of the rotated mask.
   
   Either MAPOUT or WRKOUT or both may be assigned.
   
KEYWORDED INPUT

   Possible keywords are:
   
     AVERAGE, CELL, GRID, INVERT, MODE, RADIUS, SCALE, SYMMETRY, XYZLIM
     
  MODE FROM/TO/BOTH/CORR
  
   Sets the mode of operation.
   `FROM' signals that one or more copies of the electron density from a
   cell map (MAPIN) will be transferred to a work map (WRKOUT). The cell
   map is transformed by each set of operators in turn, and all copies
   are summed in the WRKOUT map.
   `TO'' signals that density from a work map (WRKIN) will be transferred
   to a cell map (MAPOUT) using symmetry operators and unit cell repeats
   obtained from the MAPIN header. It overwrites the density in the input
   cell map with the masked density from the work map.
   `BOTH' performs both operations in turn and is only useful if you have
   multiple copies of a molecule in the asymmetric unit. It first
   averages the electron density from the cell map (MAPIN) to WRKOUT,
   then recreates the cell map (MAPOUT) with the averaged and (hopefully
   improved) electron density. It requires a mask.
   `CORR' calculates a local correlation over the whole of the work map.
   If two averaging operators are given, then the two regions of density
   mapped from the cell to the work map by those operators are
   correlated, otherwise the density of the input work map is correlated
   with the density of the cell map mapped by the one operator (the first
   case is used when identifying a non-crystallographic symmetry mask,
   the second can be used to identify correlated density between crystal
   forms).
   
  CELL [ WORK | XTAL ] <a> <b> <c> <alpha> <beta> <gamma>
  
   Set the unit cell parameters for the work map (CELL WORK) or the
   crystal map (CELL XTAL). CELL WORK should be specified if and only if
   neither MSKIN nor WRKIN are set. CELL XTAL should only be specified if
   MAPIN is not set.
   
  GRID [ WORK | XTAL ] <nx> <ny> <nz>
  
   Set the grid for the work map (GRID WORK) or the crystal map (GRID
   XTAL). GRID WORK should be specified if and only if neither MSKIN nor
   WRKIN are set. GRID XTAL should only be specified if MAPIN is not set.
   
  XYZLIM <x1> <x2> <y1> <y2> <z1> <z2>
  
   Set the work map extent. <x1>-<z2> are given in grid units or in
   fractional coordinates. This should be specified if and only if
   neither MSKIN nor WRKIN are set.
   
  SYMMETRY [ WORK | XTAL ] <spacegroup name or number>
  
   Set spacegroup symmetry of the work or crystal map. Unlike the normal
   SYMMETRY cards, the spacegroup MUST be given by number. Alternatively,
   the conventional SYMM <spacegroup name> keyword may be used to set the
   symmetry of the work map only.
   
  SCALE <s>
  
   Set scale factor to apply to the work map inside the mask between
   rotating FROM and TO the cell map.
   
  RADIUS <r>
  
   Set the radius of with the local correlation is performed in `MODE
   CORR'. Increase this if the correlation mask shows many spurious
   peaks. Default <r>=8.0 Angstrom.
   
  AVERAGE
  
   Set a density rotation and translation operator. This keyword is
   followed by a rotation/translation matrix on subsequent lines in
   either CCP4 or O/RAVE format. One AVERGE keyword, followed by the
   corresponding operator, is given for each rotation/translation
   operation to be performed. The format is the same as the `dm' and
   `ncsmask' `AVERAGE' cards).
   
   CCP4 Formats: (see also the program `lsqkab')
          
ROTATE EULER <alpha> <beta> <gamma>     (Euler angles)
TRANSLATE <t1> <t2> <t3>

   or
          
ROTATE POLAR <omega> <phi> <kappa>      (Polar angles)
TRANSLATE <t1> <t2> <t3>

   or
          
ROTATE MATRIX <r11> <r12> <r13> <r21> <r22> <r23> <r31> <r32> <r33>
TRANSLATE <t1> <t2> <t3>

   O/RAVE Format
          OMAT
          <r11> <r21> <r31>
          <r12> <r22> <r32>
          <r13> <r23> <r33>
          <t1> <t2> <t3>
          where
          x' = <r11>x + <r12>y + <r13>z + <t1>
          y' = <r21>x + <r22>y + <r23>z + <t2>
          z' = <r31>x + <r32>y + <r33>z + <t3>
          (note that the rotation matrix is transposed with respect to
          CCP4 matrix format.)
          
   These are the operations which map the density in the region covered
   by the input mask onto the other equivalent regions. The first
   operator must be the identity matrix. The mask is input in CCP4 mask
   (mode 0) format on the input file label MSKIN, and should cover just
   one monomer or averaging domain, NOT the whole unit cell.
   
  INVERT
  
   Invert all the operators.
   
EXAMPLES

  To interpolate a map to a different grid:
  
#
maprot mapin ins.map wrkout ins_fine.map << eof
MODE FROM
CELL WORK 82.5 82.5 34 90 90 120
GRID WORK 120 120 60
XYZLIM 0 119 0 119 0 59
SYMM WORK R3
AVER
ROTA POLAR 0 0 0
TRANS 0 0 0
eof

  To rotate a map 30 degrees about z for plotting (note cell and symm are no
  longer useful)
  
#
maprot mapin ins.map wrkout ins_fine.map << eof
MODE FROM
CELL WORK 100 100 50 90 90 120
GRID WORK 180 180 90
XYZLIM 0 179 0 179 0 89
SYMM WORK P1
AVER
ROTA MATRIX  0.866  0.500  0.000  -
            -0.500  0.866  0.000  -
             0.000  0.000  1.000
TRANS    0.000  0.000  0.000
eof

  To make an averaged copy of the molecule covered by MSKIN to look at on the
  graphics
  
#
maprot mapin chm.map mskin chm.msk wrkout chm_for_graf.map << eof
MODE FROM
AVER
OMAT
  1.000  0.000  0.000
  0.000  1.000  0.000
  0.000  0.000  1.000
  0.000  0.000  0.000
AVER
OMAT
 -0.43073    -0.62689    -0.64921
  0.04987     0.70173    -0.71070
  0.90110    -0.33850    -0.27099
  43.635 38.059 62.726
AVER
OMAT
 -0.43073     0.04987     0.90110
 -0.62689     0.70173    -0.33850
 -0.64921    -0.71070    -0.27099
  82.989 15.401 -8.928
eof

  To make an averaged map which can be back-transformed for phase improvement
  
#
maprot mapin chm.map mskin chm.msk mapout chm_av.map << eof
MODE BOTH
SCALE 0.33333
AVER
ROTA POLAR  0.0  0.0  0.0
TRANS  0.0  0.0  0.0
AVER
ROTA POLAR  113.28130 103.41944 120.33858
TRANS  43.635 38.059 62.726
AVER
ROTA POLAR   66.58067 -76.78019 119.69176
TRANS  82.989 15.401 -8.928
eof

  To make a correlation map, convert it to a mask, and tidy up the mask
  
#
maprot mapin $SCRATCH/chm_mir.map
       wrkout $SCRATCH/chmcorrel.map << eof
SYMM WORK P1
CELL WORK 90.3 90.3 129.8 90 90 90
XYZLIM     -20 80 24 120 -60 48
GRID WORK 80 80 120
RADI 6
MODE CORR
AVER
ROTA POLAR  0.0  0.0  0.0
TRANS  0.0  0.0  0.0
AVER
ROTA POLAR  113.28130 103.41944 120.33858
TRANS  43.635 38.059 62.726
END
eof
#
# now mask the multimer: multimer is 6% of unit cell
#
mapmask mapin $SCRATCH/chmcorrel.map
        mskout $SCRATCH/chmcorrel.msk << eof
MASK VOLU 0.06
eof
#
# Now we might edit this mask by hand, or use ncsmask to get rid of
# all but the largest lump of mask
#
ncsmask mskin $SCRATCH/chmcorrel.msk
        mskout $SCRATCH/cmncs.msk << eof
PEAK 1
eof

  Density cutting: density is cut from one cell and placed in a new cell
  
#
# Cut density into a 100A virtual cell.
# The density could be moved by specifying a non-identity operator.
# For cross-crystal translation function, give the rotation
# operator and the cell from the alternate crystal form.
#
maprot wrkin gmtocut.map mskin gmtocut.msk cutout cut.map << eof
MODE TO
CELL XTAL 100. 100. 100. 90. 90. 90.
GRID XTAL 150 150 150
AVER
ROTA POLAR  0.0  0.0  0.0
TRANS  0.0  0.0  0.0
eof

BUGS

   Since the work map will take the same grid as the mask, it is
   necessary to use a fine grid for the mask, especially when doing
   averaging calculations. The grid should be at least as fine as the
   cell map.
   
   When performing density cutting, If the masked region is larger than
   the dimensions of the crystal map in any direction, the overlapped
   density will appear at the edges of the CUTOUT map.
   
REFERENCES

    1. Stein et al., Structure 2, 45-47 (1994)
       
SEE ALSO

   mapmask, ncsmask, rotmat, dm