MAPSLICER (CCP4: Supported Program)

NAME

   mapslicer - interactive viewer for contoured sections through CCP4 map
   files.

SYNOPSIS

   mapslicer [ mapfilename ]

DESCRIPTION

   MapSlicer 2.1

   MapSlicer reads in CCP4 format map files and can display contoured
   sections though the map along any of the principal axes. MapSlicer
   uses code from the CCP4 graphical user interface ccp4i in addition to
   a set of custom Tcl commands (see ccp4mapwish).

   MapSlicer offers the following functions:
     * Read in CCP4 map file, pick any section or stack of sections
       (``slab'') on any axis and display contour levels
     * Shortcuts to Harker sections
     * Can alter contour levels, section limits and grid
     * Can alter screen scaling
     * Can zoom into areas of the display
     * Can display info on map header and currently displayed section
     * Displays cursor position in fractional coordinations, and the
       density at that point
     * Print section to a postscript file with user-defined scaling (eg
       mm per angstrom)

   The mapslicer script runs through ccp4mapwish, which is a customised
   version of the TCL/Tk interpreter wish.

USAGE

   Most of MapSlicer's functionality can be accessed quickly through the
   controls on the left-hand side of the window. Other options are
   available through menus at the top of the main window.

  File menu:

   Open new map file
          Select a new map to view. Any existing map currently being
          viewed will be overwritten in the viewer's memory.

   Save section
          Save the current section to a postscript file.

   Print
          Print the current section to a postscript file.

   Exit
          Close the viewer.

  Section menu:

   Section limits
          Allows you to change properties of the grid and the extent of
          the section displayed.

   Contour levels
          Allows you to change the contour levels displayed. This is
          based on the old NPO keywords.

  Info menu:

   About map ...
          Displays a window with information about the current map.

   About section ...
          Displays a window with information about the current section,
          including the contour levels.

   About MapSlicer ...
          Starts a hypertext viewer to display this file.

  MapSlicer Modes

   MapSlicer operates in three distinct modes, which are selected via the
   Mode menu on the left-hand side of the screen. Depending on the mode,
   different controls will be become visible:

   Section mode
          MapSlicer displays a single section at a time. The current
          section can be changed by editing the section number in the
          entry box, or by clicking on the arrows to move up or down by
          one section.
          The current axis can be changed by selecting the new axis from
          the menu.

   Slab mode
          Similiar to Section mode, except that the display shows a stack
          of sections superimposed one on top of the other. The slab is
          defined by a starting section, a depth (number of sections
          between the start and end) and a step size (specifying how many
          sections in the slab will actually be drawn).
          Any of these attributes can be edited directly to change the
          current slab display. Alternatively the arrows can be used to
          move the start position up or down by one section.
          The current axis can be changed by selecting the new axis from
          the menu.

   Harker mode
          This requires that the Harker spacegroup be specified. A menu
          will then list the possible Harker sections for that
          spacegroup, and selecting a particular menu entry will jump
          directly to the appropriate axis and section.
          If the selected Harker section is not in the current map then a
          warning will be displayed. If no Harker sections are available
          then the menu will display "None".

  Other controls

   The remaining controls are not dependent on the mode

   Scale
          Specifies how large each Ångstrom is shown on the display, in
          either mm or screen pixels. The scale is a real number for
          either units, and can be edited directly in the display.

   AutoScale
          Resets the view to show the whole section at a scale of 2mm per
          Ångstrom.

   Undo Zoom
          Restores the view to that prior to the last zoom operation that
          was performed.

  Zoom Facility

   The Zoom facility allows the user to select a smaller area of the
   current display and rescales to show that area only.

   The Zoom is enabled by click-and-holding the right mouse button (to
   set one corner of the zoom area), dragging the mouse pulls out a box
   which defines the zoom area, releasing the mouse button then performs
   the zoom operation.

   The scale will be reset automatically so that the screen area occupied
   by the new view is roughly the same as before the zoom. This is
   calculated based on area, and seems to work best for roughly square
   zoom areas.

   A zoom operation can be reversed using the Undo Zoom button.

AUTHORS

   Peter Briggs