OVERLAPMAP (CCP4: Supported Program)
                                       
NAME

   overlapmap - calculates the average of two maps
   
SYNOPSIS

   overlapmap mapin1 foo.map mapin2 bar.map [ mapin3 baz.map ] mapout
   quux.map
   [Keyworded input]
   
DESCRIPTION

   overlapmap has basically three modes of operation, combining two maps
   to produce an output map, correlating two maps or generating a
   real-space R-factor between two maps. Here are the modes in more
   detail:
    1. Average MAPIN1 and MAPIN2 with output to MAPOUT (MAP AVERAGE).
    2. Sum the desity from MAPIN1 and MAPIN2, output to MAPOUT (MAP ADD).
    3. Set density to zero in MAPOUT if present in MAPIN1 (i.e. non zero
       MAPIN1 density). Otherwise grid points in MAPOUT are set to MAPIN2
       (MAP EXCLUDE). This requires MAPIN1 has some grid points which are
       EXACTLY zero; you are unlikely to have this unless you have
       generated a map from coordinates.
    4. Set density in MAPOUT to MAPIN2 if the grid point in MAPIN1 > 0.
       Otherwise set to zero (MAP INCLUDE).
    5. Correlate the density between MAPIN1 and MAPIN2 (CORRELATE ...).
       There are three correlation modes, two of which require a third
       map (see MAPIN3). This map is not a true map but is used to flag
       which grid points are associated with which atom or residue.
       MAPOUT is not used in this mode.
    6. Remember the correlation transcends any need to scale the 2 maps.
       Below is the definition of the correlation coefficient:


corr. coeff.  =    (<x y> - <x><y>) /
              ( sqrt(<x^2> - <x>^2)  *  sqrt(<y^2> - <y>^2) )


where x represents the density values from one map and y the
values from the other.

< >  represents the mean value of the quantities inside the
bracket.

    7. Calculates a Real Space R factor à la Branden/Jones (reference
       [1]).


Real space R factor =
          Sum(RHO_obs - RHO_calc)/Sum(RHO_obs + RHO_calc)

   summed over all points within a residue. This requires that RHO_obs
       and RHO_calc are ON THE SAME SCALE. It is also sensitive to the
       atom radius you chose in SFALL. Eleanor Dodson believes it is not
       as useful as the correlation coefficient. MAPIN3 will be needed
       for this mode of operation calulated from SFALL in the RESMOD mode
       - see below.
       
KEYWORDED INPUT

   The available keywords are:
   
     CHAIN, CORRELATE, MAP, PATTERSON, REAL SPACE R
     
  MAP [ ADD | AVERAGE | EXCLUDE | INCLUDE ]
  
   ADD <scale1> <scale2>
          add <scale1>*map1 + <scale2>*map2 and output new map. (Default
          <scale1> = <scale2> =1.)
          
   AVERAGE
          average two maps and output new map.
          
   EXCLUDE
          exclude points from output map if they exist in MAP1. Any grid
          point that is is not zero in MAP1 will be set to zero in
          MAPOUT. Grid points in MAPOUT will be set to the value in MAP2
          if the grid point in MAP1 is zero.
          
   INCLUDE
          include points in output map from MAP2 if they exist in MAP1.
          The value of the grid point in MAPOUT will be that of MAP2 if
          the grid point in MAP1 > 0. Otherwise the point in MAPOUT will
          be set to zero.
          
  CORRELATE [ SECTION | RESIDUE | ATOM ]
  
   SECTION
          correlation is section by section.
          
   RESIDUE
          correlation is residue by residue.
          
   ATOM
          correlation is atom by atom.
          
  REAL SPACE R
  
   tabulated residue by residue.
   
  CHAIN <chain_ID> <1st_residue_number> <last_residue_number>
  
   Repeat residue numbering by chain, as in SFALL.
   
  PATTERSON <sigmin> sigmax>
  
   Calculate a correlation coefficient as in GROPAT ([2]). <sigmin> and
   <sigmax> are the minimum and maximum grid value/sigma ratio, typically
   3. and 10. It is recommended that origin removed difference Pattersons
   should be calculated.
   
NOTES

   MAPIN3 may be assigned to the modified map output of SFALL. This map
   flags each grid point according to certain criteria; the most useful
   is the residue flag created by MODE ATMMAP RESMOD. This flags each
   point in the map space to indicate which atom of a residue it is near
   (using the Atom Radii specified in SFALL), and whether the atom
   involved is main chain, or side chain. This is required if you want to
   use CORRELATE RESIDUE or REALSPACE Rfactor.
   
   The program must have both maps calculated in exactly the same way.
   Since any Fc map generated from coordinates has a fixed asymmetric
   unit and AXIS ORDER do them first and make sure your FFT calculation
   matches that.
   
   EXCLUDE is useful for flattening the protein density when you want to
   inspect the residual density only. Used in solvent searches and also
   in the PHASED TRANSLATION function (part of the FFT package). Generate
   the protein density in SFALL outputting an Fc map.
   
   CORRELATE can be done section by section or by RESIDUE or ATOM.
   CORRELATE RESIDUE is only possible if MAPIN3 is generated in SFALL
   outputting an Fc map with mode = mode atmmap resmod).
   
   CORRELATE ATOM is only possible if MAPIN3 is generated in SFALL
   outputting an Fc map with mode = mode atmmap atmmod).
   
SEE ALSO

   fft(CCP4),
   sfall(CCP4),
   maprot(CCP4)
   
REFERENCES

    1. Branden C. and Jones A., Nature 343 687-689 (1990)
    2. Jones Y. and Stuart D, Proc. of CCP4 Study Weekend on Isomorphous
       Replacement And Anomalous Scattering, 1991 39-48.
       
EXAMPLES

overlapmap  MAPIN1 rnasatomfc.map  MAPIN2 rnas2fo_fc.map << END
CORRELATE RESIDUES
END

  Averaging 2 maps
  
overlapmap  MAPIN1 chmi_phase_extend.ext  MAPIN2 wang_cycle3.ext
  MAPOUT chmi_wang_av.map << END
MAP AVERAGE
END

   See also $CEXAM/unix/runnable/mapcorrelation_procedures and
   $CEXAM/unix/non-runnable/mapcorrelation.exam.