PHISTATS (CCP4: Supported Program)

NAME

   phistats - Analysis of agreement between phase sets, and checking it
   against weighting factors.

SYNOPSIS

   phistats HKLIN foo_in.mtz 
   [Keyworded input]

DESCRIPTION

   PHISTATS analyses the differences between two sets of phases. The
   analysis can be binned against two types of weights; for example a
   figure of merit, and the magnitude of Fobs. It is probably more
   informative to do map correlation using OVERLAPMAP.

KEYWORDED INPUT

   The various data control lines are identified by keywords. Only the
   first 4 characters are significant. Those available are:

     END, LABIN, RANGES, RESOLUTION, SHIFT, HAND, TITLE

  LABIN <program label>=<file label> ...

   Input column assignments. The program labels are: FP SIGFP PHIBP WP
   PHIB2 W2. For details of these, see INPUT AND OUTPUT FILES.

  RANGES <nbin> [ <mon> ]

   Set the number of resolution bins <nbin> and the reflection monitoring
   interval <mon>.

   <nbin> is the number of resolution bins (equal width in
   [sin(theta)/(lambda)]**2) in which to divide partial structure data
   for normalization and sigmaA estimation. It is IMPORTANT that
   resolution ranges contain sufficient reflections. It is best to use as
   large a value of <nbin> as possible, as long as the estimates of
   sigmaA vary smoothly with resolution. If they do not, <nbin> should be
   reduced until sigmaA does vary smoothly. A good first guess is the
   number of reflections divided by 1000. If sigmaA refinement converges
   to zero in one or more of the ranges (which happens sometimes when the
   correct value is low), this can usually be circumvented by decreasing
   <nbin>.

   Information about every <nmon>-th reflection will be written to the
   log file.

   Defaults: 20 1000; maximum <nbin> allowed: 50.

  RESOLUTION [ <rmin> ] <rmax>

   Low and high resolution limits in either order or upper limit if only
   one is specified. These are in Angstroms or, if both are <1.0, units
   of 4(sintheta/lambda)**2. By default, all the data in the file are
   used.

  SHIFT <X_fracshift Y_fracshift Z_fracshift>

   PHI2 phases adjusted for a fractional Shift - especially useful when
   the two phase sets refer to different crystal origin:
  PHI2_used = PHI2_input + 2PI(h X_fracshift + k Y_fracshift + l Z_fracshift)

  HAND

   PHI2 phases adjusted to change hand.
  PHI2_used = -PHI2_shifted + 2PI(h CX + k CY + l CZ)
where CX,CY,CZ are the centre of symmetry for this space group.
(CX,CY,CZ) is (0,0,0) except for spacegroups
I41, I4122, F4132,I4132. See reindexing notes.

  TITLE <title>

   A title written to the log file.

  END

   End of input.

INPUT AND OUTPUT FILES

  INPUT

   This is an MTZ file assigned to logical name HKLIN. The following
   column assignments are required:

   FP, SIGFP
          native amplitude and standard deviation;

   PHIBP
          first phase (degrees), maybe an isomorphous phase;

   WP
          first `weight' to analyse against, for example, the figure of
          merit;

   W2
          second `weight' for analysis, for example, the native
          amplitude.

   PHIB2 may optionally be assigned. This is the second phase (degrees).
   If it is not assigned the program gives the correlation between WP and
   W2.

  OUTPUT

   There is no output file from this program.

   Normally the program compares two sets of phases. They can be any set
   of phases you like, not just experimental phases against calculated
   model phases. Obviously, if you have calculated phases from a model
   there is no experimental weight. These phases are broken up into those
   from centric reflections and acentric.

   Since centric reflections have a limited number of possible values
   PHISTATS compares the agreement between phases. That is if the phases
   are the same they agree but if they are different they disagree. Thus
   if the fraction that agree is unity then all the centric phases are
   equivalent.

   The correlation with the weigths is exactly that. The linear
   correlation coefficient is calculated between the phase difference and
   a weight. It is calculated twice, once for WP and then W2. This
   coefficient can range between 1.0 and -1.0. The optimum set of weights
   would produce a correlation of -1.0 because this would mean that the
   largest weights would correspond to the smallest phase error. The
   linear correlation coefficient is also calculated between weight and
   cos(phase_difference).

   There are similar calculations made for acentric reflections, however
   in this case a phase error or difference is calculated. Also, an
   estimated phase error is calculated. This is based on the principles
   used in SIGMAA where a quantity sigma_a is calculated. This is
   calculated from the two sets of structure factor magnitudes and need
   not be relevant.

   Tables are produced where these quantities are compared against
   resolution and the value of the weight.

SEE ALSO

   overlapmap, sigmaa

AUTHORS

   Eleanor Dodson, University of York

EXAMPLES

  Phase analysis

#  Assign weight 1 to FOM, weight 2 to FC magnitude.
phistats hklin $CCP4_SCR/toxd_sf_mir << END
TITLE   Phase analysis
RESOLUTION  40. 2.
RANGES 10   500
LABIN FP=FTOXD3 SIGFP=SIGFTOXD3 PHIBP=PHI_mir WP=W_mir -
      PHIB2=PHICtoxd W2=FCtoxd
END

  Phase analysis for alternative origin for mir phases and calculated ones

#  Assign weight 1 to FOM, weight 2 to FC magnitude.
phistats hklin $CCP4_SCR/toxd_sf_mir << END
TITLE   Phase analysis
SHIFT 0.5 0.5 0.0
RESOLUTION  40. 2.
RANGES 10   500
LABIN FP=FTOXD3 SIGFP=SIGFTOXD3 PHIBP=PHI_mir WP=W_mir -
      PHIB2=PHICtoxd W2=FCtoxd
END

  Phase analysis for other hand

#  Assign weight 1 to FOM, weight 2 to FC magnitude.
phistats hklin $CCP4_SCR/toxd_sf_mir << END
TITLE   Phase analysis
HAND
RESOLUTION  40. 2.
RANGES 10   500
LABIN FP=FTOXD3 SIGFP=SIGFTOXD3 PHIBP=PHI_mir WP=W_mir -
      PHIB2=PHICtoxd W2=FCtoxd
END

  Correlation

phistats hklin os_lu_shhg2_pt_pt4_khg_os2_nat.mtz
<< END
TITLE   Phase analysis chmi model vs MIR phases
RANGES 20 1000        ! Number of analysis bins, monitor interval
RESOLUTION  100.0 2.6 ! Resolution limits in Angstroms
LABIN FP=FP SIGFP=SIGFP WP=FOM  PHIB2=PHI W2=FP
END