POLARRFN (CCP4: Supported Program)
                                       
NAME

   polarrfn - fast rotation function which works in polar angles
   
SYNOPSIS

   polarrfn hklin foo_in_Fobs.mtz hklin2 foo_in_Fmodel.mtz mapin bar.map
   mapout foo.map PLOT fred.plt
   [Keyworded input]
   
DESCRIPTION

   This is a fast rotation function which works in polar angles, written
   by W. Kabsch. The program produces sections of constant rotation angle
   kappa for different axis directions defined by omega (angle from pole)
   and phi (angle around equator). The direction cosines of the axis is
   given by:

        (  sin omega  cos phi  )
        (  sin omega  sin phi  )
        (     cos omega        )

   These sections may be plotted as stereograms. The position of peaks is
   given for all symmetry related positions in both polar and Eulerian
   angles.
   
   Options are provided in the program for writing the calculated
   rotation to a map file, which can be read by the program on another
   occasion for plotting, peak searching etc (options MAP, READ). The
   results of the first stage of the calculation (ALMN) may also be saved
   for subsequent rotation function summations on different grids (SAVE,
   SUM). A list of peaks may be read in, and all symmetry related peaks
   generated (option PEAK).
   
   Compared to the Crowther program (ALMN), this program is a little
   slower but a self rotation function in polar angles is easier to
   understand. This program can also be used to calculate a small part of
   the rotation function on a fine grid (down to 1 degree steps).
   However, the crystal symmetry is expressed less fully in polar angle
   space than in Eulerian angle space, so for cross-rotation functions
   the Eulerian program is normally more appropriate.
   
KEYWORDED INPUT

   Only the first 4 letters of each keyword are necessary. All input is
   free format. Most data cards are optional. The various data control
   lines are identified by keywords, those available being:
   
     CROSS, CRYSTAL, END, FIND, JOIN, LABIN, LIMITS, MAP, NOPRINT, PEAK,
     PLOT, READ, RESOLUTION, SAVE, SELF, SUM, TITLE
     
   The following keywords are compulsory: SELF/CROSS, CRYSTAL, LABIN.
   
  TITLE <title>
  
   The rest of the line is taken as a title.
   
  SELF <arad> <eps>
  
   Set flag for self rotation (cf CROSS)
   
   <arad>
          integration radius in Patterson space (default 20Å)
          
   <eps>
          Radius (Angstrom) of sphere within which the Patterson is
          removed. Default Eps set = 0.7*<resmax>.
          
  CROSS <arad> <eps>
  
   Set flag for cross rotation (cf SELF)
   
   <arad>
          integration radius in Patterson space (default 20Å)
          
   <eps>
          Radius (Angstrom) of sphere within which the Patterson is
          removed. Default Eps set = 0.7*<resmax>.
          
  RESOLUTION <resmin> <resmax>
  
   Read resolution limits in Å, in either order. If only one treat as
   high resolution limit. Note that because of the limit of 30 Bessel
   functions in this version, the integration radius ARAD cannot be
   greater than 5.83*<resmax>: if it is, the program resets <resmax> to
   ARAD/5.83
   
  CRYSTAL FILE <nfile> ORTH <ncode> BFAC <badd> FLIMITS <fmin> <fmax> [CELL
  SYMMETRY]
  
   This card is COMPULSORY for each hklin set (one for self-rotation, two
   for cross-rotation). The first subkeyword FILE (or NUMBER) indicates
   whether this CRYSTAL card refers to crystal 1 or to crystal 2.
   
   FILE
          followed by crystal number <nfile>. This sets the crystal
          number, 1 or 2 (default 1). The syntax is any one of FILE 1 or
          FILE 2.
          
   ORTH
          followed by orthogonalisation code <ncode> (default 1). If the
          PEAK option is used ORTH should be given. Ncode defaults to 1
          if unspecified.
          

            ncode      orthogonalisation code for this crystal
                  = 1, orthogonal x y z  along  a,c*xa,c*  (Brookhaven, default
)
                  = 2                           b,a*xb,a*
                  = 3                           c,b*xc,b*
                  = 4                           a+b,c*x(a+b),c*
                  = 5                           a*,cxa*,c   (Rollett)

   BFAC
          followed by temperature factor <badd> (default = 0). This can
          be used to sharpen the data (e.g. = -20). Fused = Finput *
          exp(-badd*ssq/lsq)
          
   FLIMITS
          followed by <fmin> and <fmax> (order unimportant). (Defaults to
          0 and 32767.) These tests are done after application of the
          temperature factor, but before squaring to intensities.
          
   SYMMETRY
          followed by symmetry operation or crystal space group name or
          number. Default: take from MTZ file.
          
   CELL
          followed by cell dimensions. Default: take from MTZ file.
          
  LABIN <data assignments>
  
   LABIN FILE <nfile> F=<label> SIGF=<label2>
   File column data assignments for F, SIGF.
   
   FILE sets the crystal number, 1 or 2 (default 1). The syntax is any
   one of FILE 1 or FILE 2.
   
  LIMITS <iphi1> <iphi2> <nphi> <iomega1> <iomega2> <nomega> <ikappa1>
  <ikappa2> <nkappa>
  
   i.e. limits and steps on phi, omega, kappa
      iphi1 iomega1 ikappa1   start points in degrees
      iphi2 iomega2 ikappa2   stop  points in degrees
      nphi  nomega  nkappa    intervals in degrees

   (Default =  0 180 5   0 180 5   0 180 5. This covers the basic
   asymmetric unit at 5 degree intervals).
   
  [NO]PRINT <LPRINT>
  
   Switch on or off printing of map as a figure-field in the logfile, and
   set print threshold LPRINT. The rotation function is scaled to a
   maximum of 100. Values less than 0 are printed as ' -' and values
   between 0 and LPRINT are printed as ' .'. NOPRINT (= PRINT 0)
   suppresses printing of the figure-field. The default is to print the
   map (PRINT +1), except in the case of the READ option, for which the
   default is NOPRINT.
   
  MAP
  
   Write rotation function to a map file. This may be read back later for
   plotting, peak searching, etc. using the READ option.
   
  PLOT <cstart> <cint> [ NOTITLE ]
  
   Plot rotation function as a stereographic projection of each kappa
   section. These sections have omega = 0 or 180 at the centre, omega =
   90 around the edge, and phi as marked around the periphery.
   
   <cstart>
          contour start level (default = 10)
          
   <cint>
          contour interval (default = 10)
          
   If the keyword NOTITLE is present, the maps are plotted with no labels
   or titles: this may be useful for publication purposes. The plots are
   not normally useful if a small part of the function is being
   calculated.
   
  JOIN <kappa> <omega1> <phi1> <omega2> <phi2> [DASHED [<repeat> <dash>]]
  
   Draw arc connecting two peaks at (omega1,phi1) and (omega2,phi2) on
   section kappa.
   
   If the keyword DASHED is present, the arc will be dashed with repeat
   and dash length as specified (in multiples of the radius of the
   stereogram). Default values for <repeat> and <dash> are 0.05, 0.025.
   Up to 30 JOIN commands may be given.
   
   Warning: this option is primarily intended for self-rotation
   functions, and probably will not work sensibly if the kappa sections
   are split into two sections or half sections.
   
  FIND <peak> <maxpeak> [RMS] [OUTPUT <filename>]
  
   Read peak threshold and maximum number of peaks. Peak searching may be
   suppressed by PEAK 0 0.
   
   Note that although the program attempts to interpolate the positions
   of peaks, this may not be very accurate in regions where the peaks are
   very spread out (kappa near 0) or on the edges of the map.
   
   <peak>
          threshold for peaks (default = 10).
          
   <maxpeak>
          maximum number of peaks to find (default = 20)
          Up to <maxpeak> peaks above <peak> will be found, and all
          symmetry related peaks generated
          
   If the keyword RMS is present, then the peak threshold is <peak> * RMS
   density, otherwise <peak> is the absolute threshold in the scaled map.
   
   If the keyword OUTPUT is present, the unique peaks will be output to a
   file whose name may also be given (default filename or logical name
   PEAKS). The keyword RMS must precede OUTPUT if both are present.
   
  READ <kappa1> <kappa2>
  
   Instead of calculating a rotation function, read a previously
   calculated one (written out using the MAP flag). Sections <kappa1> to
   <kappa2> will be processed (if no values are given, the whole map will
   be used), printed (if PRINT is on, NOPRINT is default), plotted (if a
   PLOT card is present) and searched for peaks (see FIND).
   
  SAVE [ <fname> ]
  
   save output from first stage of rotation (calculation of Almn
   coefficients for each crystal) in files <fname>1.dat and <fname>2.dat.
   <fname> defaults to 'COEFFS'. These files can be used to save time on
   a later run of the program (see SUM card) to calculate a rotation
   function on a different grid (e.g. on a fine grid around a peak).
   
  SUM [ <fname> ]
  
   read Almn coefficients from files generated in a previous run of the
   program with the SAVE option. The files are <fname>1.dat and
   <fname>2.dat <fname> defaults to 'COEFFS'
   
  PEAK [ MATRICES ]
  
   read a list of peak positions (omega, phi, kappa in degrees) from
   subsequent lines, terminated by blank line, 'END' or end of file. The
   program will not calculate a rotation function, but will generate all
   symmetry related peaks from the peaks given, and print out the
   corresponding matrices. This option requires cards SELF or CROSS,
   CRYSTAL or CELL, and SYMMETRY (ie the number of crystals, their
   symmetry and orthogonalisation codes must be defined). If the keyword
   MATRICES is present, the rotation matrices corresponding to each peak
   will be printed.
   
  END
  
   Terminates input. If present must be the last card.
   
A NOTE ON SYMMETRY AND ASYMMETRIC UNITS

   The polar angles omega, phi, kappa have an intrinsic symmetry
   operation 180-omega, 180+phi, -kappa by definition. This gives an
   asymmetric unit in the absence of other symmetry of omega 0 to 180,
   phi 0 to 360, kappa 0 to 180. Additional symmetry relations between
   omega and phi for a given kappa are created in self rotation
   functions, and by parallel dyad axes in the two crystals (ie any dyad
   axis in a self rotation function). These are as follows
    1. Self-rotation function, and also kappa=180 in all cases:
       kappa = -kappa, hence 180-omega, 180+phi
    2. dyad axes in both crystals parallel to orthogonal x axes (after
       any permutation produced by the orthogonalisation code NCODE):
       180 - omega, -phi
    3. dyad axes parallel to orthogonal y axes:
       180 - omega, 180 - phi
    4. dyad axes parallel to orthogonal z axes:
       omega, 180 + phi
       
   If more than one of these symmetries is present, additional symmetry
   is generate by their combination. The asymmetric units required are
   given in the following table:


Symmetry                            Asymmetric unit
--------                           omega   phi  kappa

      no symmetry                   180    360   180

1.   180 - omega, 180 + phi          90    360   180
                                 or 180    180   180

2.   180 - omega, -phi               90    360   180
                                 or 180    180   180

3.   180 - omega, 180 - phi          90    360   180
                                 or 180    -90)  180
                                        to +90)

4.   omega, 180 + phi               180    180   180

   In the program, the PLOT option will always try to plot a complete
   stereogram of all kappa sections. In the absence of symmetry, each
   kappa section is split into two hemispheres, omega 0 to 90 and omega
   90 to 180. For symmetries 1, 2 and 3, only the hemisphere omega 0 to
   90 is plotted. For symmetry 4, the two quarter spheres phi 0 to 180
   for omega 0 to 90 and omega 90 to 180 are plotted together in the same
   circle. The PLOT option is not normally useful if only a small part of
   the asymmetric unit is calculated.
   
INPUT AND OUTPUT FILES

   HKLIN
          input amplitudes for crystal 1
          
   HKLIN2
          input amplitudes for crystal 2
          
   MAPIN
          input map for READ option
          
   MAPOUT
          output map for MAP option
          
   PLOT
          plotter output
          
   SYMOP
          symmetry library (normally defaulted).
          
   COEFFS1
          Almn coefficients for crystal 1 default created as scratch
          files
          
   COEFFS2
          Almn coefficients for crystal 2
          
   + two internal scratch files
   
EXAMPLES

  Self-rotation
  
polarrfn hklin tpfktrunc.mtz
         mapout tself.map
         plot self.plt
         << eof
TITLE T-PFK self-rotation  R=29A, 5 - 7 A
SELF 29
RESOLUTION 7 5
CRYSTAL FILE 1  ORTH 1  BFAC -20  SYMMETRY P21
LABIN FILE 1 F=FP SIGF=SIGFP
LIMITS 0 180 5 0 180 5 0 180 5
MAP
PLOT 10 10
FIND 2 20 RMS OUTPUT peaks.dat
eof


#!/bin/csh -f
#
#  Self-rotation function
#
set resolution = 15 3
set radius = 20
set u1af = {$scr0}/u1afobs_fc117

#  Calculate whole map, & search for peaks
polarrfn hklin {$u1af} mapout u1aself << eof-1
title U1A Self-Rotation function, resolution ${resolution} radius ${radius}
self  ${radius}
resolution  ${resolution}
crystal  file 1 bfac -20
labin  file 1  F=FP SIGF=SIGFP
limits 0 180 5 0 180 5 0 180 5
map
find  5 100
eof-1

# Now plot just the kappa = 180 deg section
plot:
polarrfn hklin {$u1af} mapin u1aself plot u1aself << eof-2
title U1A Self-Rotation function, resolution ${resolution} radius ${radius}
self  ${radius}
resolution  ${resolution}
crystal  file 1 bfac -20
labin  file 1  F=FP SIGF=SIGFP
limits 0 180 5 0 180 5 0 180 5
read 180 180
plot  10 10
eof-2

  Cross rotation
  
polarrfn hklin  tpfktrunc
         hklin2 uniqsfpfk.mtz
         mapout tcross.map
         << eof
TITLE T-PFK cross-rotation  R=29A, 5 - 7 A
CROSS 29
RESOLUTION 7 5
CRYSTAL FILE 1  ORTH 1  BFAC -20  SYMMETRY 4
LABIN FILE 1 F=FP SIGF=SIGFP
CRYSTAL FILE 2  ORTH 1  BFAC -20  SYMMETRY 1
LABIN FILE 2 F=FC SIGF=FC
LIMITS 0 180 5 0 360 5 0 180 5
MAP
FIND 10 20
eof

AUTHORS

   Author: W. Kabsch
   Contact: Phil Evans (PRE@UK.AC.CAMBRIDGE.MRC-MOLECULAR-BIOLOGY)