Choosing Scaling Program (CCP4: General)
                                       
NAME

   scalechoose - information about choice of scaling program
   
   The following comes straight from a tutorial by Ian Tickle.
   
   If you do not have the 'symbol' font set up for HTML, you may want to
   view the other version of this document, with gifs.
   
  Contents
  
    1. Background
    2. Scaling procedures
       
  1. Background.
  
   Two CCP4 programs are available for determining and applying the scale
   factor(s) of the derivative dataset(s) relative to the reference
   native dataset: SCALEIT and FHSCAL. In accordance with the CCP4
   philosophy of accumulating all reflection data in one file, the
   datasets must be contained within different columns in the same file
   (column-merging of files is accomplished with the MTZUTILS program).
   
   It should be realised however that the FHSCAL program is designed
   specifically for derivative-to-native scaling, whereas SCALEIT is more
   general purpose, and can also be used for scaling of observed to
   calculated structure factor amplitudes. FHSCAL uses the "Kraut"
   scaling procedure, which is inherently more accurate than the "Wilson"
   and/or least squares procedure used by SCALEIT. Another difference is
   that SCALEIT uses one formula to fit all the scale factors, whereas
   FHSCAL divides the data into resolution shells, smooths the shell
   scale factors and then interpolates to get the final scale factor for
   each reflection. A third option is "local" scaling, where each
   reflection gets an individual scale factor which only depends on the
   relative scales of the reflections in its immediate neighbourhood.
   
   Usually these differences are not important because initially only a
   rough scale factor is needed for the isomorphous difference Patterson,
   and the scale factor is refined later along with the heavy-atom
   parameters (i.e. 3-D coordinates, site occupancies, individual
   isotropic and/or anisotropic thermal parameters), and the relative
   overall thermal parameter for each derivative. SCALEIT has a very
   useful extra feature, the display of Normal probability analysis plots
   that can be used to decide whether the observed isomorphous and
   anomalous differences are really significant, or just due to errors in
   the measurements.
   
  2. Scaling procedures.
  
   The "Kraut" and "Wilson" scale factors are derived by considering the
   origin peak heights of the native (FP), derivative (FPH) and
   heavy-atom (FH) Patterson maps. Any point in a Patterson represents a
   vector, and the Patterson density at the point equals the sum of
   products of pairs of electron densities at points in the unit cell of
   the crystal that are separated by that vector. So the Patterson origin
   peak represents the sum of squares of electron densities in the unit
   cell. Because of the Fourier transform relationship between the
   Patterson and the measured intensities (= amplitude2 ), the Patterson
   origin peak height is simply the sum of squares of the corresponding
   amplitudes (this is basically Wilson's equation).
   
   Provided the derivative structure is obtained simply by summing the
   native and heavy-atom structures, in other words that it is perfectly
   isomorphous, the derivative Patterson origin peak is just the sum of
   the native and heavy-atom Patterson origin peaks. Of course, the
   "heavy-atom structure" exists only in the imagination, as it consists
   only of heavy atoms in the same position as in the derivative
   structure, but otherwise completely empty space. Consequently we have:
   
         S(k |FPH| )2 = S |FP|2 + S |FH|2
   
   Here k is the unknown scale factor needed to multiply all the measured
   derivative amplitudes to put them on the same scale as the measured
   native amplitudes. Both are of course on completely arbitrary scales,
   because the X-ray experiment does not take into account the incident
   beam intensity, crystal size, wavelength, and all the other factors
   that one would need to know to calculate absolute diffracted
   intensities. Consequently, all structure factors and occupancies in
   subsequent calculations are scaled relative to the arbitrarily scaled
   native amplitudes. This is an important point to grasp; if you don't,
   you will be baffled later on by occupancies greater than 1!
   
   The heavy-atom amplitudes |FH| are of course completely unknown at
   this stage, and because they are on average smaller than |FP| or
   |FPH|, a possible assumption is simply to assume that they do not make
   a significant contribution and to ignore them; this gives the "Wilson"
   scale factor:
   
         kWilson = Ö ( S |FP|2 / S |FPH|2 )
   
   Alternatively, the heavy-atom amplitude can be estimated from the
   isomorphous difference: | k |FPH| -  |FP| |. In fact, except for weak
   reflections where we may get a cross-over such that
   |FH| = k |FPH| + |FP|, in the case of centric reflections (where the
   phase can only take 1 of 2 values differing by 180o so the complex
   structure factors are collinear), they are the same. For the remaining
   acentric reflections, which are almost always the majority, because
   the unknown native and heavy-atom phases are uncorrelated, it can be
   shown that the average isomorphous difference squared is half the
   average |FH|2. It is of course this fact that will allow us to use the
   isomorphous difference Patterson as an approximation to the heavy-atom
   Patterson. These relationships allow the unknown S |FH|2 term to be
   eliminated, rather than ignored, so a more accurate estimate of the
   scale factor kKraut is obtained from the resulting quadratic. For full
   details of the algebra, consult the FHSCAL program documentation.
   
   Finally, the least-squares estimate of the scale factor is obtained by
   minimising the sum of weighted squares of isomorphous differences:
   S w (k |FPH| - |FP| )2 with respect to the unknown scale factor, where
   w is a weight equal to the reciprocal variance of the isomorphous
   difference: w = 1/((k sPH)2 + sP2 ). However, the inherent assumption
   is again that the |FH| can be ignored; in practice this introduces an
   error of 5-10% in the scale factor, which may affect correct
   interpretation of the Patterson.
   
   To illustrate the effect of the heavy atoms on the scale factor,
   consider a small protein of 1000 atoms (assume for simplicity they are
   all N atoms). The mean scattering intensity of the protein <|FP|2>
   will be proportional to 1000x72 = 49000. If a single mercury atom is
   then introduced it will contribute 802 = 6400, so the fractional mean
   intensity difference between native and derivative will be 6400/49000
   = 0.13.
   
   In practice, because the introduction of the heavy atoms into the
   protein can anisotropically increase the disorder in the crystal, and
   also because of effects like absorption of X-rays by the heavy atoms,
   the relative scale factor can vary both with resolution and in
   direction, and so the procedure is a little more complicated. Programs
   may therefore have the option of applying an overall relative
   isotropic or anisotropic temperature factor to the |FPH|'s, or of
   applying scale factors either in equi-volume shells or in localised
   regions of reciprocal space.
   
AUTHORS

   Ian Tickle, Birbeck College London, England
   Prepared for CCP4 by Maria Turkenburg, University of York, England.