SCALEIT (CCP4: Supported Program)
                                       
NAME

   scaleit - derivative to native scaling and analysis
   
SYNOPSIS

   scaleit hklin foo_in.mtz hklout foo.mtz
   [Keyworded input]
   
PURPOSE

   The program SCALEIT calculates and applies a derivative to native
   scaling function using either (a) an overall scale factor, (b) a scale
   and isotropic temperature factor or (c) a scale and anisotropic
   temperature factors. SCALEIT would normally be run after the merged
   datasets for native and derivatives had been combined into one file
   with CAD, and before beginning to search for heavy atom sites. See
   also FHSCAL for an alternative to SCALEIT.
   
   In addition, SCALEIT performs several useful analyses of the scaled
   data, which may be useful even if FHSCAL is used for the final scaling
   (see PROGRAM OUTPUT). These analyses include a Normal probability
   analysis using the ideas of Dave Smith and Lynne Howell (J. Appl.
   Cryst. (1992) 25 81-86), which is done if there is only one derivative
   being scaled. SCALEIT also estimates the Kraut Scale using the formula
   of Ian Tickle Daresbury booklet 1991 p.91.
   
DESCRIPTION

   The program has options to refine scale factors, to apply input scale
   factors, or just to analyse the agreement between derivative and
   native amplitudes. Several derivatives may be scaled and analysed in
   one run of the program, but the same type of scaling must be used for
   all of them. It is important to look at the final analysis which
   compares <FP **2> and <FPH**2> after scaling. If their ratio is not
   near to unity, something has gone wrong! See below for some possible
   reasons for the problem. Maybe the range you are scaling over is
   inappropriate; it is often best to exclude the lowest resolution data.
   Maybe there are a few reflections obscured by the backstop in one data
   set; this can distort scales badly. Maybe the sigmas are not
   appropriate. In the analysis, large differences (both isomorphous and
   anomalous) are listed (only if scales are refined): these reflections
   are candidates for spuriously large differences, and should be
   checked.
   
   Note that there is no unique solution to the problem of scaling
   together two different data sets. Problems arise from:
     * Scaling over an inappropriate resolution range. Derivative data
       are often poorly isomorphous at low resolution, and there is no
       point trying to scale to a resolution where the data are too
       inaccurate.
     * random errors, particularly if the two data sets are of very
       different strengths. Excluding weak data (EXCLUDE SIG) may help in
       this case
     * Poor estimates of SIGMA. The default option is NOT to use weights
       derived from the standard deviations of the reflections in the
       scaling, since these are often unreliable, or the two data sets
       are of very different quality. Use keyword WEIGHT to use the
       standard deviations if you think they are reliable.
     * Systematic errors: the anisotropic scaling will take out some
       systematic errors, but proper scaling to remove such errors must
       be done on data processed as P1 data; i.e. the indices should be
       those of the actual observation, not those of a symmetry
       equivalent. If the LAMBDA values defined by the anisotropic
       ellipsoid are very different there is some problem in scaling the
       two data sets.
     * Rogue information; e.g. a reflection behind a backstop. If such an
       observation has a very low SIGMA it will be given a lot of weight
       in the refinement calculation (see EXCLUDE options for possible
       cures).
     * actual differences between the crystals: scaling can only be done
       properly with a model for the difference, thus in refinement of
       heavy-atom parameters, the derivative scale factor is also
       refined. The scale calculated by this program can only be regarded
       as a rough estimate but it is usually adequate for calculating
       Patterson functions. The program FHSCAL may provide a better
       estimate of scale for heavy-atom derivatives.
       
   In general, scales may be calculated either by a least-squares
   procedure, or by Wilson scaling, i.e. making <Fph**2> = <Fp**2>. These
   procedures will give different answers, and it is not clear which is
   better. This program allows the option of a final Wilson scaling after
   least-squares determination of isotropic or anisotropic temperature
   factors: this changes the scale factor, but not the temperature
   factors (option REFINE [AN]ISOTROPIC WILSON).
   
   Note that all scales output by the program apply to Fph, although they
   are determined from F**2.
   
   It also possible to apply the scales to all ''scaleable'' columns in a
   dataset (i.e. to F+/- and to the structure intensities; see the LABIN
   keyword), and this is advisable to avoid mixtures of scaled and
   unscaled data for a single derivative. For input mtz files with
   dataset information, SCALEIT will attempt to check and warn you
   accordingly if it detects datasets which will be output with such a
   mixture. In these cases, specifying the AUTO keyword will cause the
   appropriate scale factor to be applied automatically to all such
   columns.
   
KEYWORDED INPUT

   A line beginning with an '#' or '!' indicates to the parser that it is
   a comment line and will be ignored: this is useful for command
   procedures. Parameters given in [] below are optional.
   
   The various data control lines are identified by keywords. The only
   compulsory keyword is LABIN to specify the MTZ column labels; other
   keywords have sensible defaults and are optional. The principal
   keywords controlling the function of the program are REFINE and
   ANALYSE. The full list of available keywords is as follows:
   
     ANALYSE, AUTO, CONVERGE, EXCLUDE, GRAPH, LABIN, NOWT, REFINE,
     RESOLUTION, SCALE, SCATTER, SYMMETRY, TITLE, WEIGHT, END
     
  TITLE <string>
  
   title to replace header in output file
   
  LABIN <program_label>=<file_label>...
  
   Assign columns to be used. This both assigns columns, and defines how
   many derivatives to scale, and whether they have anomalous data.
   
   The items required (<program_label>s) are as follows:
           H
           K
           L
           FP        F of native data
           SIGFP     sigma(F) of native data
           FPHn      F of data for nth derivative
           SIGFPHn   sigma(F) of derivative data
          [DPHn]     Anomalous Delta(F) of derivative data
          [SIGDPHn]  sigma anomalous Delta(F) of derivative data

   and so on for up to 20 possible derivatives.
   
   Additionally the following data items can be included, if present, for
   each derivative:
         FPHn(+)     F(+) of hkl for nth derivative
         SIGFPHn(+)  sigma of above
         FPHn(-)     F(-) of -h-k-l for nth derivative
         SIGFPHn(-)  sigma of above
         IMEANn      Average Structure Intensity for nth derivative
         SIGIMEANn   sigma of above
         In(+)       Structure Intensity of hkl for nth derivative
         SIGIn(+)    sigma of above
         In(-)       Structure Intensity of -h-k-l for nth derivative
         SIGIn(-)    sigma of above

   If any of these items are specified then SCALEIT will also apply the
   appropriate scale factor (in the case of F+/-) or the scale factor
   squared (in the case of structure intensities) to those columns,
   however no analysis will be performed using the data in the columns.
   
   Alternatively, by specifying the AUTO keyword, the scale factor will
   be applied automatically to all ``scalable'' columns in a dataset.
   Only FPHn and SIGFPHn need to be specified for each derivative on the
   LABIN line (see separate entry for AUTO).
   
  AUTO
  
   Switches on AUTOmatic column selection. This option can only be used
   if the input file contains dataset information.
   
   It is only necessary to specify FPHn and SIGFPHn for each dataset on
   the LABIN line (except in special cases, see below). Other labels can
   also be specified if desired. The program will then try to identify
   all ''scalable'' columns in the dataset, automatically read them in
   and then apply the appropriate scale factor determined from FPHn.
   
   This option is intended to prevent a mixture of scaled and unscaled
   columns within a dataset, e.g. FPHn is scaled but not FPHn(+) and
   FPHn(-). There are a couple of caveats:
   
    1. It is assumed that each dataset contains the information for one
       derivative.
    2. There may be problems with the automatic scaling if datasets
       contain both SIGIMEAN and SIGDPHn. This is because the program
       cannot distinguish between sigmas for intensities (which need to
       be scaled by the square of the scale factor) and those for other
       quantities (which are multiplied by the scale factor).
       In these cases the automatic selection will make a best guess at
       which sigma is which; the ambiguity can also be resolved provided
       that IMEAN and SIGIMEAN are explicitly set by the user on the
       LABIN line (which is safer).
       
  REFINE [ SCALE | ISOTROPIC | ANISOTROPIC ] [WILSON]
  
   Alternative to ANALYSE. Default for program is REFINE ANISOTROPIC,
   which defines the type of scale-factors to be refined. This applies to
   all derivatives specified in this run.
   
   SCALE
          overall scale only
          
   ISOTROPIC
          scale and isotropic temperature factor
          
   ANISOTROPIC
          scale and anisotropic temperature factor (default)
          
   WILSON
          apply a final Wilson scale, after determining relative
          temperature factors. This can be combined with SCALE, ISOTROPIC
          or ANISOTROPIC keywords. I have no idea if this is a good thing
          to do.
          
  ANALYSE
  
   Alternative to REFINE
   
   Analyse differences between derivative and native without refining
   scale factors. SCALE commands may be given to change the scale and
   temperature factors from no scaling. If this command is given, no
   output file is written.
   
  CONVERGE [ NCYC <n> ] [ ABS <m> ] [ TOLR <l> ]
  
   Conditions for convergence.
   
   <n>
          number of cycles of refinement required (default 4)
          
   <m>
          convergence limit. The refinement will be ended if all the
          shifts are less than (ABS * the standard deviation of the
          parameter). (Default = 0.001)
          
   <l>
          tolerance (default 0.00000001)
          
  SCATTER
  
   Include scatter plots of scales in logfile. Default is not to.
   
  SCALE [FPHn] Scale [Biso]/[B11 B22 B33 B12 B13 B23]
  
   Alternative to REFINE, not usually used.
   
   Input scales (and temperature factors) to be applied to derivative n
   (i.e. column assigned to FPHn). If the FPHn key is not given, the
   scale is used for the 1st derivative FPH1. If any scales are given
   with this command, then the scales are NOT determined, just applied
   and the analysis performed. Isotropic and anisotropic temperature
   factors may NOT be mixed for different derivatives. No scale factor
   may be given for the native.
   
  SYMMETRY <spacegroup name or number>
  
   Not normally required.
   
   Spacegroup name or number to override symmetry in input file.
   
  RESOLUTION <rmin> <rmax>
  
   Resolution range (either 4sin(theta)**2/lambda**2, or Angstrom).
   Reflections outside this range will be excluded from scale
   determination and analysis, but will be scaled and written to the
   output file. If this command is not given, all data in the file is
   included.
   
  EXCLUDE [ FP | FPH<n> ] [ SIG <nsig> ] [ FMAX <fmax> ] [ DMAX <fmax> ] [ DIFF
  <diffmax>]
  
   Set criteria for excluding data from the scale determination and
   analysis. Excluded data will still be scaled and written to the output
   file. The default is to include all data. If the first key is FP the
   exclusions apply to the native data, if FPH<n> to the <n>th
   derivative: if this key is omitted, the exclusions apply to all data,
   native and derivatives. Several EXCLUDE commands may be given.
   
   SIG <nsig>
          exclude reflections if FP < <nsig>* SIGFP or FPH<n> < <nsig>*
          SIGFPH<n>
          
   FMAX <fmax>
          exclude reflections if FP or FPH<n> > <fmax>
          
   DMAX <fmax>
          exclude reflections if abs(DPHn) > <fmax>
          
   DIFF <diffmax>
          exclude reflections if abs(FPHn-FP) > <diffmax>
          
  GRAPH [ H K L MODF ]
  
   List of the analyses to be included as well as that against
   4sin(theta)**2/lambda**2. H,K,L and MODF can be in any order The
   default is just to analyse against resolution.
   
  NOWT
  
   If this command is present, the scale determination will be unweighted
   (the default).
   
  WEIGHT
  
   Weight the observations for scale determination according to the input
   standard deviations. The default is not to weight them.
   
  END
  
   End of input. If present, this must be last keyword.
   
INPUT AND OUTPUT FILES

   The input files are:
   (a)
          The control data file
   (b)
          The input reflection data file in standard MTZ format.
          
   The output is a reflection data file in standard MTZ format. This is a
   copy of the input reflection data file but with the data items for the
   selected derivative re-scaled.
   
PROGRAM FUNCTION

   The program SCALEIT is used to calculate a derivative to native
   scaling function and apply it to the derivative data. Scales are
   determined from the squared amplitudes. The scaling function for F may
   be of the form:
   
   An overall scale (REFINE SCALE)
       C

   Isotropic temperature factor (REFINE ISOTROPIC)
       C * exp (-B sintheta/lambda)

   Anisotropic temperature factor (REFINE ANISOTROPIC) (default)
       C * exp(-(h**2 B11 + k**2 B22 + l**2 B33 +
                      2hk B12 + 2hl  B13  +  2kl B23))

   An initial (and optional final, see REFINE WILSON) scaling factor is
   calculated from the expression
              Kinit = Sqrt(Sigma FP**2 / Sigma FPH**2)
                       (relative Wilson scaling)

   The scale and anisotropic temperature factors are then refined using a
   modification of the method of Fox and Holmes. The function minimised
   is
          Sigma Sigma w( h )i(I( h )i - GiI( h ))**2
            h     i

   with respect to all parameters (2 scale factors and 6 beta values in
   the anisotropic case)
             G1   1.0
             G2 = (1/C) exp(+ 2 h_ B h_ )

   Anisotropic temperature factors are determined on data expanded by
   symmetry to a hemisphere, which constrains certain combinations of
   coefficients in some space groups, e.g. in orthorhombic symmetry
   B12=B13=B23=0, in cubic spacegroups B11=B22=B33.
   
   The scale and temperature factors are applied to the derivative data
   and an output file is written with the corrected data. The scale
   factor SigmaFP**2/SigmaFPH**2 is then analysed in ranges of h, k, l
   and 4sin**2 theta/lambda**2.
   
PROGRAM OUTPUT

   The program output starts with details of the input reflection data
   file produced by the MTZ file handling routines, and details of the
   control data. Then for each cycle of the refinement the following
   details are output.
    1. The eigenvalues of the matrix
    2. The mean residual
    3. The scaling parameters giving the new values, the shifts and the
       standard deviations.
       
   At the end of the refinement, there is an analysis of the scaled data.
   For each derivative, an estimate of the acceptable isomorphous and
   anomalous differences is given, followed by a list of individual
   reflections with abnormally high differences. This information can be
   used to exclude outliers from Patterson calculations or direct methods
   calculations.
   
   Then for each derivative, the following information is given as a
   function of resolution:
     * Kraut scale factor and relative Wilson scale factor.
     * R factor ("Rfactor" or "Rfac") and weighted R factor ("Rfactor_W"
       or "Wted_R") for agreement between native and derivative.
     * <diso> and max(diso)
     * <dano> and max(dano)
       
   These statistics may also be given as a function of h, k, l or |FP|,
   see keyword GRAPH.
   
   Some terms defined:
   
     Rfac = [sum( abs(FPH - FP))]/[sum(FP)]
     
     RF_I = [sum( abs(FPH*FPH - FP*FP))]/[sum(FP*FP)]
     
     Wted_R = [sum( abs(FPsq-FFmean)/Var(FPsq) +
     abs(FPHsq-FFmean)/Var(FPHsq)] / [ sum(FPsq/Var(FPsq) +
     FPHsq/Var(FPHsq) ]
     
     FFmean = [FPsq/Var(FPsq) + FPHsq/Var(FPHsq)] / [1/Var(FPsq) +
     1/Var(FPHsq)]
     
     Var(FPsq) = Var(FP) * 4FPsq
     
     Diso = abs(FPH - FP)
     
     Dano = abs(DPH)
     
   Diso and Dano are very useful analytical tools. Diso should fall off
   with increasing resolution, and certainly should not increase! That is
   a good indication of either non-isomorphism, or data quality falling
   off. You need to run your Pattersons with resolution ranges which only
   use reliable data, and with sensible EXCLUDE terms based on the plots
   of Diso and Dano. However MLPHARE has a built in weighting scheme
   which means that it doesn't do much harm to include less good data in
   phasing. After all the poor hkl should get low FOMs, and then DM can
   use the few reflections with reasonable phases to help in the phase
   extension procedure.
   
   If there is only one derivative then the results of a normal
   probability analysis are also given (see Lynne Howell and Dave Smith,
   J.Appl. Cryst. 25 81-86 (1992)). The reflections in each resolution
   bin are sorted according to the value of:
   
     delta(real) = (FPH - FP)/sqrt(SIGFPH**2 + SIGFP**2)
     
   where FPH and SIGFPH are the scaled values for the derivative. For
   each reflection, delta(expected) is then calculated based on an
   assumed normal distribution and the position of the reflection in the
   sorted list. A plot of delta(real) against delta(expected) is called a
   normal probability plot.
   
   If the native and scaled derivative data sets are essentially
   identical (in statistical parlance, they represent two samplings of
   the same population), then the spread of the two data sets will be the
   same within the errors defined by SIGFP and SIGFPH, and the normal
   probability plot will be linear with a slope of about 1 and an
   intercept of 0. However, if the heavy atoms make a significant
   contribution to the observed structure factors, then (FPH - FP) will
   be larger than expected from SIGFP and SIGFPH, and the slope will be >
   1. The intercept may also be non-zero.
   
   The program plots the slope and intercept of the normal probability
   plot (obtained by a least squares fit) as a function of resolution for
   both centric and acentric reflections. These values are also plotted
   for the case where reflections at the tails of the distribution are
   excluded: these reflections tend not to lie on the straight line and
   distort the least squares fit. The existence and size of the heavy
   atom contribution to the structure factors can be gauged from the
   values of the slope and intercept, and the variation with resolution
   indicates to how high a resolution such contributions extend. A
   similar analysis can be applied to MAD data by assigning FP and FPH to
   data at different wavelengths (dispersive differences) or to F+ and F-
   (anomalous differences). In general, the size of the slope will be
   smaller in this case.
   
SEE ALSO

   fhscal, mlphare.
   
REFERENCES

    1. Normal Probability Analysis:
       Lynne Howell and Dave Smith, J.Appl. Cryst. 25 81-86 (1992)
       
AUTHORS

   Phil Evans / Eleanor Dodson / Richard Dodson
   
EXAMPLES

  Simple unix example script found in $CEXAM/unix/runnable/
  
     scaleit.exam (Example of derivative to native scaling)
   
   (A vms version found in $CEXAM/vms/scaleit.com)
   
  Also found combined with other programs in the example scripts
  ($CEXAM/unix/runnable/)
  
     rsearch.exam (Use of scaleit in R factor search).
   
     fhscal.exam (Analysis after Kraut scaling of derivative data.)