SFALL (CCP4: Supported Program)
                                       
NAME

   sfall - Structure factor calculation and X-ray refinement using
   forward and reverse FFT
   
SYNOPSIS

   sfall [ XYZIN foo.brk ] [ MAPIN foo.map ] [ HKLIN foo.mtz ] [ MAPOUT
   foo_out.map ] [ HKLOUT foo_out.mtz ] [ XYZOUT foo_out.brk ] [ GRADMAT
   foo.sfmat ]
   [Keyworded input]
   
CONTENTS

    1. DESCRIPTION
         1. Generate atom map
         2. Calculate structure factors
         3. Generate X-ray gradients for refinement
         4. Space Groups
    2. KEYWORDED INPUT
    3. MEMORY ALLOCATION
    4. INPUT AND OUTPUT FILES
         1. Notes on Formfactors
         2. Notes on XYZIN, Atom names, etc
         3. Notes on HKLIN
         4. Notes on MAPIN
         5. Output from Structure Factor Calculation
         6. Notes on XYZOUT
         7. Notes on HKLOUT
         8. Notes on MAPOUT
         9. Output from the Gradients Calculation - notes on GRADMAT
        10. Output from the Calculation of the Optimum Shifts
        11. Notes on stepsize
    5. COMMON PROBLEMS
    6. EXAMPLES
         1. Calculate map from atom coordinates
         2. Read in coordinates to calculate structure factors
         3. Read in map to calculate structure factors
         4. Iteration cycles to do back-transformation and phase
            combination cycles in solvent flattening procedure
         5. Unrestrained refinement
         6. Prolsq refinement cycles Please note: PROLSQ is no longer
            available as refinement program in the CCP4 Suite.
         7. Simple Runnable Examples
    7. AUTHORS
    8. PROGRAM FUNCTION
         1. Modelling of the electron density and calculation of
            structure factors
         2. Calculation of the gradients
         3. The Normal Matrix
         4. Calculation of the shifts
    9. REFERENCES
   10. SEE ALSO
       
DESCRIPTION

   This program calculates structure factors and X-ray gradients for
   refinement using inverse and forward fast Fourier techniques.
   
   If coordinates are input, it builds an `atom map' on a suitable grid
   over the asymmetric unit of the spacegroup. Atomic density is
   distributed as a Gaussian centred on the atom position. The value of
   the Gaussian depends on the distance from the atom centre, the atom
   type, and temperature factor. Its value is calculated at each grid
   point within a given radius for each atom, and the values are summed
   to give an `atom map'. This `map' can then be used for an inverse fast
   Fourier transform, which gives the structure factor. It is important
   that the grid is fine enough to sample the atomic Gaussians accurately
   - the accuracy of the structure factor estimates depends on this. I
   recommend using a grid which gives a sampling of ~0.5Å.
   
   X-ray gradients are estimated by `differential synthesis'. A
   difference map is calculated, and this is convoluted with the atomic
   density.
   
   By default, SFALL scales Fobs to Fcalc. This then lets you do maps on
   (or close to) an absolute scale if the map comes from coordinates. If
   you are back-transforming a map, e.g. in solvent-flattening or
   averaging, then the map isn't on an absolute scale anyway, and so this
   scaling is not particularly sensible (although not usually harmful).
   Note that in iterative procedures, the Fobs you bring in to SFALL on
   each cycle should be the original Fobs, not the one carried through
   from the previous cycle (which may have been scaled, selected, or
   otherwise corrupted). In this case, it is probably more sensible to
   use the NOSCALE option in SFALL, then either (i) use SIGMAA to
   generate Partial or Combined Fourier coefficients for the next map (if
   you want to weight them); or (ii) use RSTATS to scale Fcalc to Fobs.
   
   For a description of the original method see [1]. A modification in
   calculating the gradients suggested by Alain Lifchitz is used.
   
   A list of common problems (with possible solutions) can now be found
   below.
   
  1) Generate atom map
  
   Input:
   
   i) XYZIN
   
          Coordinates (Brookhaven format with CRYST1 and SCALEi lines).
          
   Output:
   
   i) MAPOUT
   
          Atom map. Various modifications can be made to this map:
          
   a)
          The `solvent' map. This map has zero at all points where there
          is atomic density, and a constant value for all points where
          there was no atomic density. It is used for calculating
          structure factors for `bulk solvent' (see ICOEFL for ideas on
          using this); or for use as a mask.
          
   b)
          A tagged `atom map' where each grid point is tagged with a flag
          to say which residue, or which atom number, contributed most to
          it. This is used for analysing map correlations, and real space
          R-factors.
          
  2) Calculate structure factors
  
   By default a scale factor is calculated between Fobs and Fc and is
   applied to the output Fobs. If this is not wanted then the keyword
   NOSCALE must be used.
   
   Input:
   
   i) either coordinates or a map (compulsory)
   
          If map is input it can be `truncated' to eliminate very high or
          low density.
          
   ii) HKLIN (optional)
   
          This must contain: H K L FP SIGFP [ FREE FPART PHIP ...]
          It MUST be sorted on h k l, and be in the CCP4 chosen
          asymmetric unit. See NOTES ON HKLIN for further details.
          
          The FREE value is generated by FREERFLAG or in X-PLOR and
          transferred to MTZ format using F2MTZ. See the FREERFLAG
          documentation. (Note that X-PLOR 3.1 only assigns flags of 0 or
          1.) The keyword FREERFLAG allows reflexions with a given FREE
          value to be excluded from refinement and Fc calculations.
          
          IF FPART and PHIP have been assigned, the structure factor
          output will equal the scaled FPART vector plus the contribution
          calculated from the input plus the scaled FPART vector.
          
   Output:
   
   i) HKLOUT containing: H K L ... FC PHIC (WANGWT)
   
          (If you are preparing the 'averaged map' for generating the
          Wang envelope, (flagged by keyword AVMODE) the WANGWT will be
          calculated as well as the structure factor modified for use in
          solvent flattening.)
          
   ii) MAPOUT - The atom `map' (optional).
   
          You can also keep the atom map if you want to.
          
  3) Generate X-ray gradients for refinement
  
   These are used for minimisation of X-ray differences between FP and
   FC. This calculation uses the forward FFT.
   
   Input:
   
   i) XYZIN
   
          Coordinates (Brookhaven format with header).
          
   ii) HKLIN
   
          Containing: H K L FP SIGFP [ FREE ]
          When FREE is assigned then a subset of reflections is excluded
          from the gradient calculation (see above for details). Hence
          the agreement between them and Fc plays no part of the
          refinement procedure. The Free R factor calculated for these
          reflections is a useful indicator of the quality of the
          refinement [4]. It must be stressed that during a particular
          refinement procedure only one freeR set of reflections should
          be used. It is meaningless to change the freeR set in the
          middle of refinement. However, with several freeR sets, it is
          possible to compare the same refinement procedure against
          different freeR sets. It is still possible for all the freeR
          sets to be unsuitable e.g. if the NCS and the crystal symmetry
          are related, as they often are, there may be special
          relationships between classes of reflections, and this may mean
          that the FREE set is not truly independent of the other
          observations.
          
   Output:
   
   i) XYZOUT
   
          A coordinate file in which the least squares shifts have been
          applied.
          
   ii) GRADMAT
   
          A direct access file containing information about the X-ray
          gradients, ready for input into PROLSQ (no longer available in
          the CCP4 Suite).
          
   Further details of the specification of input and output files is
   given in section INPUT AND OUTPUT FILES.
   
   See description of keyword MODE and examples for uses for the various
   options.
   
  Space Groups
  
   SFALL has special subroutines to handle the following spacegroups:

  P1                  P21(4)               P21212(1018 - alt. origin)
  P212121(19)         P4122/P4322(91/95)   P41212/P43212 (92/96)
  P31/P32(144/145)    P3/R3(143/146)       P3121/P3221(152/154)
  P61/P65 (169/170)

   It is possible to use the P1 version (or any suitable lower symmetry)
   for the calculations. In particular, any non-primitive spacegroup can
   be run in the appropriate primitive one. See keyword SFSGROUP for
   details.
   
   BUT BEWARE: To use SFSG P1 you must have your reflections sorted with
   l>=0. This is NOT the default for P3121/P3221 or P6i22. You would be
   sensible to run CAD with the keyword: `OUTLIM SPACEGROUP P1' before
   calculating structure factors.
   
   The crystal symmetry will be used to generate atom positions from a
   unique molecule. See NOTES ON HKLIN for special requirements for the
   HKLIN file when using a lower symmetry version.
   
KEYWORDED INPUT

   All input is keyworded. Only the first 4 characters of a keyword are
   significant. The keyworded records can be in any order.
   
   Anything on a line after an ! or # is ignored and lines can be
   continued by using a minus sign.
   
   The possible keywords are:
   
   Compulsory
          
     MODE
     
   Optional
          
     AVMODE, BADD, BINS, BRESET, CELL, CHAIN, EDEN, END, FORMFACTOR,
     FREERFLAG, GRID, H2OBG, LABIN, LABOUT, NOSCALE, OMIT, RATIO,
     RESOLUTION, RMSSHIFT, RSCB, SCALE, SFSGROUP, SIGMA, STEPSIZE,
     SYMMETRY, TITLE, TRUNCATE, VDWR, VERBOSE, WEIGHT.
     N.B. Some of these are compulsory for some MODEs.
     
DESCRIPTION OF KEYWORDS

  MODE [ ATMMAP ... | SFCALC ... | SFREF ... ]
  
   This keyword controls the course of the calculation.
   
   ATMMAP [ RESMOD ] [ ATMMOD ] [ SOLVMAP ]
          Calculating `atom maps' from coordinates. The map extends over
          the asymmetric unit of the appropriate space group (which may
          be different from the true spacegroup, see keyword SFSGROUP for
          possible groups). N.B. XYZIN and MAPOUT must be assigned.
          
          Subsidiary keywords:
          
   RESMOD
          output `atom map' values tagged by a residue number flag.
          
   ATMMOD
          output `atom map' values tagged by a atom number flag.
          
   SOLVMAP
          output `solvent map' with value specified by the H2OBG keyword
          (default=0.03) at all points not occupied by atom density. All
          points occupied by atom density set to 0.0.
          
   SFCALC ...
          Structure factor calculation.
          
          Subsidiary keywords:
          
   XYZIN or MAPIN (one essential)
          Define input type, either coordinates or a map. N.B. XYZIN or
          MAPIN must be assigned.
          
   followed by:
          
   HKLIN (optional)
          Only reflections which exist in the HKLIN file are output to
          HKLOUT. The output FC PHIC are appended to input H K L FP
          SIGFP... See keywords LABIN and LABOUT for further details.
          N.B. HKLIN and HKLOUT must be assigned. See NOTES ON HKLIN for
          the requirements placed on the HKLIN file.
          
   ATMMAP or SOLVMAP (optional)
          Either an `atom map' or a `solvent map' is output. The map
          extends over the asymmetric unit of the space group used in the
          structure factor calculation (see keyword SFSGROUP). Note that
          for non-primitive space groups, only density for symmetry mates
          corresponding to primitive symmetry operations is output; use
          MODE ATMMAP to obtain a complete map. N.B. MAPOUT must be
          assigned.
          
   SFREF
          Coordinate and/or B-factor refinement; will calculate least
          squares gradient and shifts. N.B. XYZIN and HKLIN must be
          assigned.
          
          Subsidiary keywords:
          
   MAPIN
          (This option is exceedingly unlikely to be needed.) Gradients
          will be taken from an input difference map. Usually this
          difference map is generated internally from the structure
          factors calculated from the atomic coordinates. However, in
          some special situations, e.g. if you had averaged a difference
          map earlier, you may want to input it rather than use the
          internally generated one.
          
   RESTRAINED
          Atom parameter gradients calculated from the fit of the X-ray
          data are output to GRADMAT, to be combined with geometric
          restraints calculated by PROTIN and PROLSQ (no longer available
          in the CCP4 Suite).
          
   UNRESTRAINED
          Parameter shifts to be applied without restraints; a file will
          be written to XYZOUT.
          
          If followed by:
          
   XYZ
          refinement of the X Y and Z parameters will be done.
          
   XYZB
          refinement of the XYZ and B parameters will be done.
          
   B
          refinement of the B parameters will be done.
          
   Only possible with the UNRESTRAINED option.
   
   Example 1: MODE ATMMAP
          An electron density map is created from the atomic coordinates.
          
   Example 2: MODE ATMMAP RESMOD
          An electron density map is created from the atomic coordinates
          with an extra residue identifying flag added to the atomic
          density; this is 100*IRES+MCHFLG (If there are several chains
          in your protein you will need to describe the chain limits
          using the keyword CHAIN to avoid the same flag being given to
          atoms from different chains). This allows OVERLAPMAP to analyse
          the correlation coefficient between 2 maps or the `real space
          R-Factor' for contributions from each residue.
          
   Example 3: MODE ATMMAP ATMMOD
          An electron density map is created from the atomic coordinates
          with an extra atom identifying flag added to the atomic
          density; this is 100*atom_number. This allows OVERLAPMAP to
          analyse the correlation coefficient between 2 maps or the `real
          space R-Factor' for contributions from each atom (This was used
          to see if the hydrogen or deuterium atoms in a neutron study
          could be distinguished in the electron density map).
          
   Example 4: MODE SFCALC XYZIN HKLIN [ ATMMAP ]
          A structure factor calculation is performed using the input
          coordinates. HKLIN is read, and the FP are scaled to FC. HKLOUT
          contains at least H K L scaled_FP scaled_SIGFP FC PHIC
          (You can output unscaled FP by using the keyword NOSCALE). An
          R-factor is calculated. If keyword ATMMAP is given the electron
          density map created from the atomic coordinates is saved on
          MAPOUT.
          
   Example 5: MODE SFCALC MAPIN HKLIN
          A structure factor calculation is performed using the input
          map. The map MUST cover the asymmetric unit expected for the
          SFSGROUP. This will be true if you have calculated the map
          using FFT with the FFTSPACEGROUP the same as the SFSGROUP and
          have NOT reset the AXIS order. Details are given below. HKLIN
          is read, and the FP are scaled to FC. HKLOUT contains at least
          H K L scaled_FP scaled_SIGFP FC PHIC
          (You can output unscaled FP by setting keyword NOSCALE). An
          R-factor is calculated.
          
   Example 6: MODE SFCALC XYZIN (ATMMAP)
          A structure factor calculation is performed using the input
          coordinates. Since no HKLIN is read, the SYMMETRY you wish to
          use for the structure will have to be given. The default is to
          use the symmetry of the SFSGROUP. Output HKLOUT containing h k
          l FC PHIC (WANGWT if AVMODE set) for all reflections within the
          requested resolution limits.
          
          If keyword ATMMAP is given the electron density map created
          from the atomic coordinates is saved on MAPOUT.
          
   Example 7: MODE SFCALC MAPIN
          A structure factor calculation is performed using the input
          map. The map MUST cover the asymmetric unit expected for the
          SFSGROUP. This will be true if you have calculated the map
          using FFT with the FFTSPACEGROUP the same as the SFSGROUP and
          have NOT reset the AXIS order.
          
   Example 8: MODE SFREF XYZ (or XYZB) RESTRAINED
          Used for restrained refinement of XYZ coordinates or XYZ
          coordinates and B factors. It is used in conjunction with
          PROTIN and PROLSQ (no longer available in the CCP4 Suite).
          First a structure factor calculation is done, the FP scaled and
          an R-factor calculated. Then the program calculates the normal
          matrix and gradient contributions for the parameters to be
          refined. Gradients of atomic shifts are output to GRADMAT.
          Reference: R. Agarwal, A. Lifchitz, J. Konnert, W.A Hendrickson
          [6].
          
   Example 9: MODE SFREF XYZ (or XYZB or B) UNRESTRAINED
          Used for unrestrained refinement of XYZ coordinates or XYZ
          coordinates and B factors or Bfactors alone. First a structure
          factor calculation is done, the FP scaled and an R-factor
          calculated. Then the program calculates the normal matrix,
          gradient contributions and shifts for the parameters to be
          refined. The shifts are analysed using arguments from STEPSIZE,
          RATIO and a set of modified coordinates output to XYZOUT.
          Reference: R. Agarwal, A. Lifchitz [6].
          
  SFSGROUP <sfsgroup>
  
   <sfsgroup> is the spacegroup number or name of the spacegroup used for
   the calculation. You don't normally need to specify this as a sensible
   default will be used (the highest symmetry one the program can use
   which is compatible with your data) as printed in the output.
   
   N.B. - This IS NOT NECESSARILY the spacegroup of your structure. E.g.,
   you may well be calculating structure factors in P1 for a structure
   with spacegroup F43212. The program will check whether the requested
   <sfsgroup> is compatible with your data.
   
   The possibilities for <sfsgroup> are: P1, P21 (4), P21212 (1018 -
   alternative origin), P212121 (19), P4122/P4322 (91/95), P41212/P43212
   (92/96), P31/P32 (144/145), P3/R3 (143/146), P3121/P3221 (152/154),
   P61/P65 (169/170).
   
   Any spacegroup can be run in an appropriate one whose symmetry
   operators are a subset of the one of interest (P1 can always be used
   as long as the hkl data are sorted with l>=0). By judiciously shifting
   origins many spacegroups become supergroups. $CLIBD/symop.lib contains
   the modified symmetry operators for some spacegroups. You may move the
   origin of your coordinates with PDBSET. For example:
   
          SYMGEN X + 1/4, Y + 1/4, Z
          
  LABIN <program label>=<file label> ...
  
   Note: This is essential for all refinement and if HKLIN is assigned
   for a structure factor calculation.
   
   The following labels can be assigned.

         H     K     L     FP    SIGFP   FREE   FPART   PHIP
         PHIP  F0    F1    F2    F3      F4     F5      F6
         F7    F8    F9    F10   F11     F12    F13     F14
         F15   F16   F17   F18   F19

   Assignments for FP and SIGFP are always required. If the free R flag
   is assigned to FREE, a subset of reflections can be excluded from the
   calculation or refinement. See the keyword FREERFLAG. If you wish to
   add a known FPART to the structure factors, assign FPART and PHIP.
   This is useful if you want to calculate hydrogen contributions, add in
   an anisotropic heavy atom, add in a bulk solvent correction, which has
   been calculated somewhere else. The FPART can be scaled relative to
   the FC by inputting a SCALE.
   
   If you wish to copy some but not all the other columns from your input
   to your output file, you may assign F0 F1 ... F19. These will be
   transcribed to the output file. If you want to copy everything over,
   use ALLIN on the LABOUT line.
   
  LABOUT <program label>=<file label> ... [ ALLIN ]
  
   <program labels> can be given for FC PHIC (and WANGWT, if required).
   Any column assigned on LABIN will be copied to the output file. You
   can change that file label with LABOUT if you absolutely have to, but
   it is unwise!
   ALLIN will copy all columns in the input file to the output file.
   
OPTIONAL KEYWORDS:

  AVMODE [ RADIUS <radius> ] [ WEIGHT <modewt> ]
  
   When you are preparing the 'averaged map' for generating the Wang
   envelope, this sets the radius of the map sphere and the type of
   weighting.
   
   Subsidiary keywords:
   
   RADIUS <radius>
          Specify the <radius> of the averaging sphere (angstroms)
          
   WEIGHT <modewt>
          
   <modewt> = 1
          Use weighting scheme w=1-(r/R) (Wang's method)
          
   <modewt> = 2
          Use weighting scheme w=1-(r/R)**2
          
  BADD <badd>
  
   A parameter added to all atomic B values. It will smear the Gaussians
   used to generate the atomic density over a larger volume. L.Ten Eyck
   suggests this should allow a coarser sampling grid. G. Bricogne is
   sceptical and certainly it introduces serious errors into the B12
   coenzyme structure factors at 1Å resolution (ref Hugh Savage). EJD
   shares the scepticism. The default value (0.0) gives reasonable
   results for most problems.
   
  BINS <nbins>
  
   <nbins> (default 50) is the number of bins for the analysis of
   R-factor v. resolution. Ranges of 4sin**2/Lambda**2 are of width
   1.0/<nbins>. For high resolution data this needs to be reset.
   
  BRESET <bmin>
  
   B-factors less than <bmin> (default bmin=5.0) are set equal to <bmin>.
   For high resolution data this needs to be reset.
   
  CELL <a> <b> <c> [ <alpha> <beta> <gamma> ]
  
   Input cell parameters explicitly. This is checked against the cell
   read from the MTZ file and that read from the PDB file. The program
   will continue with a warning if there is a small inconsistency and
   stop if there is a serious one. <alpha> <beta> <gamma> default to 90
   degrees.
   
  CHAIN <chnlab> <iresn> <iresc>
  
   Only needed for MODE ATMMAP RESMOD if your coordinate file has more
   than one chain. You will need one CHAIN card for each chain.
   
   <chnlab>
          single character label (e.g. A)
          
   <iresn>
          first residue number
          
   <iresc>
          last residue number
          
  EDEN <escale> <cmp> <cmn>
  
   Done for Cecil Tate. The input map is scaled by:
   xscal=escale/nx*ny*nz
   and truncated.
if density(x,y,z)<0
       density(x,y,z)=xscal*cmn*tanh(density(x,y,z)/cmn))
if density(x,y,z)>0
       density(x,y,z)=xscal*cmp*tanh(density(x,y,z)/cmp))

  END
  
   This ends input.
   
  FORMFACTOR [ NEUTRON | NGAUSS <ngauss> ] <atnam1> <atnam2> ...
  
   See the NOTES ON FORMFACTORS.
   
   SFALL has hardcoded X-ray and neutron formfactors available for atom
   types H C N O S. (Default CuKa X-ray formfactors.) Other atom types
   are tabulated in $CLIBD/atomsf.lib (X-ray) and
   $CLIBD/atomsf_neutron.lib (neutron). If your atom identifier is not
   recognised (i.e. it is not C, N, O, or S) the program will read
   atomsf.lib and take the FIRST table which matches your atom ID. This
   may not be satisfactory if your atom type is Fe+3, say, and you may
   wish to specify the formfactor yourself.
   
   Subsidiary keywords:
   
   NEUTRON
          Use neutron formfactors. Remember to assign ATOMSF
          $CLIBD/atomsf_neutron.lib to read the correct library of
          formfactors.
          
   or
   
   NGAUSS <ngauss>
          <ngauss> (default 2) is the number of Gaussian terms requested
          for the default atoms H C N O S. The only possible values are 2
          or 5.
          
   <atnam1> <atnam2> ...
          Atom names for any other atom types used in XYZIN. The atom
          names MUST exactly match the entries in ATOMSF library.
          
   Example:
   FORM NEUTRON   P Co+3 D
   FORM NGAUSS 5  Fe+3

  FREERFLAG <freeflag>
  
   Reflections where the value of the column FREE, taken from the MTZ
   file, equals <freeflag> (default 0) are omitted from the refinement or
   FC calculation and their R-factor is monitored separately. If you do
   not wish a free-R set to be used don't assign FREE.
   
  GRID <nx> <ny> <nz>
  
   <nx>, <ny>, <nz> are integers giving the number of divisions along
   each whole unit cell edge. The atomic density is sampled on this grid,
   so if it is too coarse you will introduce errors into the structure
   factor calculation. These default to values near to celledge*2, which
   defines a grid spacing of 0.5Å. Different spacegroups have special
   requirements for factorisation. No prime factors higher than 19 are
   permitted (The `atom map' generated on this grid has the asymmetric
   unit defined for this spacegroup. See table below.).
   
   The following general restrictions must be observed:
                  <nx> >= 2 * HMAX + 1
                  <ny> >= 2 * KMAX + 1
                  <nz> >= 2 * LMAX + 1

   In addition there are further space group dependent conditions as
   follows (where `n' is an integer, i.e. <nz> must be even, for
   instance):
                          <nx>     <ny>     <nz>
             P1            -        2n       2n
             P21           2n       4n       2n
             P21212        4n       4n       4n
             P21212a       ''       ''       ''
             P212121       ''       ''       ''
             P4122/P4322   4n       4n       8n
             P41212/P43212 ''       ''       ''
             P31/P32       6n       6n       6n
             P3/R3         ''       ''       ''
             P3121/p3221   ''       ''       ''
             P61/P65       6n       6n      12n

  H2OBG <h2obg>
  
   Bulk water scattering to fill in all empty regions. <h2obg> (default
   0.0) is the value which will fill the SOLVMAP. ICOEFL uses this.
   
  NOSCALE
  
   Scale between FP and FC is calculated but not applied to output FP and
   SIGFP.
   
  OMIT <th>
  
   Reflections are not included in the refinement if mod(Fo/Fc)><th> or
   mod(Fc/Fo)><th>. This provides a means of excluding data with bad
   agreement from the refinement and it should be used with care
   (Default: 1000).
   
  RATIO <ratio>
  
   Large xyz and B shifts are truncated to <ratio>*rms shift. This is
   only used for UNRESTRAINED refinement.
   
   At the beginning of a refinement, the value of ratio should be kept
   fairly low (1.5 - 2.0) as shifts tend to be large when the errors in
   the parameters are large. When most atoms are well refined, then the
   ratio may be increased to 3 or 4, to allow for the refinement of these
   atoms which are poorly placed.
   
  RESOLUTION <dmin> [ <dmax> ]
  
   <dmin>, <dmax> (default 1, 1000) are resolution limits in Angstroms
   (or in 4*sin**2/l**2 if both are <1.0. They can be given in either
   order. If only one value is given, it is assumed to be the high
   resolution cutoff. The SFCALC option outputs FC for all reflections to
   the outer limit (You usually calculate SFs to make maps and it is best
   to calculate all SFs and then limit resolution etc. in FFT).
   
   Default values are overwritten from HKLIN to include all reflections.
   
  RMSSHIFT [XYZ] <rmsxyz> [B] <rmsb>
  
   The shifts are scaled to limit the rms XYZ shift and B shift to be
   equal to the set value, or to the calculated one, whichever is
   smaller. Only useful during unrestrained refinement. Equivalent to
   setting STEPSIZE. If RMSSHIFT is given STEPSIZE will be ignored.
   Default values: 0.0 0.0.
   
  RSCB <dsmin> <dsmax>
  
   in Angstroms (either order) or 4s**2/lambda**2. Default values: 4.5Å
   and 1.0Å.
   
   If appropriate the program refines the value of the scale and overall
   B value to fit <Fo**2> to <Fc**2> using reflections within this
   resolution range. The default resolution range is chosen to use only
   those reflections where the <Fo**2> distribution fit Wilson statistics
   reasonably well. A standard protein distribution shows a sharp 5Å dip,
   which can distort the scale factors. <Fc**2> is often unrealistically
   high for low resolution data, until the solvent is adequately
   modelled. The lack of `solvent contrast' causes this.
   
   Users are often worried because they get lower R-Factors if this scale
   is fitted for all data. This does not necessarily mean such a scale is
   more correct!
   
   The default HKLOUT will have:
   
          H K L Scale*FP Scale*SIGFP ... FC*exp(-overall_B*ss) PHIC
          
   If NOSCALE is specified HKLOUT will have:
   
          H K L FP SIGFP ... FC*exp(-overall_B*ss) PHIC
          
   After the end of each structure factor calculation a new scale factor
   is calculated from the following expression, where SCNEW is the new
   scale factor and SCALE is the previous scale factor.
                   Sum {(SCALE * Fcalc) * (Fobs)}
  SCNEW = SCALE *  --------------------------------------
                   Sum {(SCALE * Fcalc) * (SCALE * Fcalc)}

  SCALE [FPART] <scale> <bov>
  
   These parameters are applied to the Fpart as
   <scale>*exp(-<bov>*ssq/ll) (Defaults: <scale>=1, <bov>=0).
   
   Some structure factor outputs (notably SHELX) include an Fcalc scaled
   as 10*absolute. SFALL calculates FC on the absolute scale. If you
   wanted to combine these values you would need
   SCALE FPART 0.1
   
  SIGMA <sigma>
  
   Data with Fobs < sigma * sd(Fobs) will not be included in refinement
   calculations. This cutoff has no effect on structure factor
   calculations. Do not be alarmed when your R-Factor appears to be
   higher for them than when you are refining; you will have more
   reflections in the structure factor sum. Default value: -1.0, i.e. no
   cutoff.
   
  STEPSIZE <szo> <szb> <szfrc>
  
   This is only used during UNRESTRAINED refinement. XYZ shifts are
   multiplied by <szo>, B shifts are multiplied by <szb>. <szfrac> is the
   fractional change in step size above which a second calculation is
   done. NOT used if RMSSHIFT is given. Default values: 1.0 1.0 0.3.
   
   The program tries to estimate these using an algorithm of R.
   Agarwal's. See NOTES ON STEPSIZE.
   
   If you are doing unrestrained refinement, structure factor calculation
   will be repeated if abs(initial step - optimum step)/(initial step).
   
  SYMMETRY <sg>
  
   (Defaults to the symmetry of the SFSGROUP). <sg> is the spacegroup
   number or name. If HKLIN is assigned the symmetry will be picked up
   from the MTZ file header and should NOT be specified with this
   keyword. If HKLIN is not assigned you may need to give this. See
   examples below.
   
  TITLE <title>
  
   Title (up to 80 characters) used on the printer output. The title
   information after the keyword is used as a heading for map sections
   and also as title information for the output reflection data file if
   present.
   
  TRUNCATE <rhmin> <rhmax>
  
   The input map is truncated - all values <<rhmin> are set to <rhmin>,
   and all values ><rhmax> set to <rhmax>. This should be used for the
   solvent flattening procedure.
   
  VDWR <dlim>
  
   <dlim> specifies the maximum radius for which an atom is considered to
   contribute to the electron density while building the `atom map'.
   Default: 2.5.
   
   The speed and accuracy of the calculation depend to some extent on the
   values chosen. For 1.5Å data a value of 2.5 is sufficient (a maximum
   value of 3.0 is allowed). For neutron data, or for atoms with low B
   values, it could safely be reset to 1Å.
   
  VERBOSE
  
   Lots and lots of output - useful if debugging. Please note that this
   may produce a message telling you that atom names have been set to ZZZ
   or residue names to DUM if you have non-standard names. This is not
   important as the atomic number is determined from the original atom
   type. See Notes on Formfactors and Notes on Atom Names below.
   
  WEIGHT <w>
  
   The weight (default 0.0) applied to each structure factor is given by
   (2sintheta/lambda)**<w>
   (See [1]). At the beginning of the refinement use <w>=-1.5 or -1.0 to
   put most weight on the low angle data. As the refinement proceeds
   increase <w> to 0.0 (But actually we never use it...).
   
MEMORY ALLOCATION

   The program allocates a large work array, whose size may be changed
   from the default by setting the logical name MEMSIZE to an appropriate
   integer value. The current value is printed in the output (look for
   `Memory allocation'). There are other dimensions which can currently
   only be changed by recompilation and the error messages are currently
   not very clear about changing the MEMSIZE.
   
INPUT AND OUTPUT FILES

   The following input and output files are used by the program (in
   addition to some scratch files which are deleted at the end of program
   execution):
   
   Input Files:
   
   XYZIN
          Input Coordinates File (Brookhaven format)
          
   HKLIN
          Input Reflection Data File (MTZ format)
          
   MAPIN
          Input Map File (standard map file format)
          
   Output Files:
   
   XYZOUT
          Output Coordinate File (Brookhaven format)
          
   HKLOUT
          Output reflection data file in standard MTZ format
          
   MAPOUT
          Output map file (Standard map file format)
          
   GRADMAT
          Output matrix file for Hendrickson Konnert program
          
   The files used in a single run of the program depend on the options
   requested via the data control keywords.
   
  NOTES ON FORMFACTORS
  
   The form factors are read from the file assigned to ATOMSF. This
   defaults to $CLIBD/atomsf.lib. Coefficients for analytical
   approximation to the scattering factors for atom identifier at a given
   resolution sintheta/lambda (=S) are given as:
   
    a1*exp(-b1*s*s) + a2*exp(-b2*s*s) - 2 Gaussian approximation
                                                 (Agarwal, 1978)
or as:

    a1*exp(-b1*s*s) + a2*exp(-b2*s*s) + a3*exp(-b3*s*s)
                                   + a4*exp(-b4*s*s) +  c
                                      - 5 Gaussian approximation

   See [2] pp. 99-101 (Table 2.2B) or [5] p. 500ff, table 6.1.1.4 for
   values a1-a4, b1-b4, c for X-rays. For neutron scattering see [2] pp.
   99-101 (Table 2.2B).
   
   The atom name can be used to assign a formfactor to it.
   
   WARNING 1)
          The program distinguishes CA - the metal - from CA - main chain
          atom in a protein by its position on the coordinate line... And
          older versions of FRODO get this wrong! The rules on defining
          atom names are the same as those used by PDB. The chemical
          symbol is specified in columns 13 and 14 and the symbol is
          RIGHT justified.
          
                 0        1
e.g.    column   1   5    0  34
                 ATOM  ...   ZN            is Zinc
                 ATOM  ...    U            is Uranium

   For the common atom types the program includes tables for form factors
   for the required value of NGAUSS. They are C N O H and S. All others
   must be read from the library files atomsf.lib or atomsf_neutron.lib
   which are automatically assigned. These contain tables of formfactors
   for every known atom (Kim Henrick monument).
   
   atomsf.lib contains the five Gaussian form for X-ray data and the two
   Gaussian form for atoms H C N O and S. Unless you are working at very
   high resolution (>1.5Å) the two Gaussian approximations are adequate
   and speed up the calculations somewhat.
   
   atomsf_neutron.lib has the constant value needed for neutron
   scattering.
   
  NOTES ON XYZIN, ATOM NAMES ETC.
  
   Coordinates are assigned to XYZIN in Brookhaven format.
   
   The CRYST1 card (which gives the cell dimensions) and the SCALEi cards
   (which give the required transform for turning the coordinates into
   fractional ones) should be included in XYZIN.
   
   Cell parameters from the HKLIN file or CELL keyword (if either are
   present) will be used in the absence of CRYST1 and SCALEi cards, but
   otherwise the results of omitting the cards are somewhat unpredictable
   - in some cases the program may fail, in others it may proceed but
   using random or inappropriate values for the cell parameters.
   
   If an atom has occupancy set =0.0 it will be copied to the output file
   if appropriate, but not used in the calculation. This means it is easy
   to exclude suspect atoms from any calculation without deleting them
   from the file.
   
   Example of part of XYZIN:

REMARK 2ZN refined coordinates
CRYST1   82.500   82.500   34.000  90.00  90.00 120.0 1       R3
SCALE1       0.01212   0.00700   0.00000        0.00000
SCALE2       0.00000   0.01400   0.00000        0.00000
SCALE3       0.00000   0.00000   0.02941        0.00000
ATOM      1  N   GLY A 201  1   -8.863  16.944  14.289  1.00 21.88
 .................................
ATOM    826  CA  ALA D 130  4   -5.022  21.709 -11.876  1.00 15.58
ATOM    830 CA   WAT A 249  1   -0.002  -0.004   7.891  0.33 10.40
ATOM    831 ZN2  WAT A 249  1    0.000   0.000  -8.039  0.33 11.00
ATOM    832  OW1 WAT A 249  1    0.000   0.000  -8.039  0.00 11.00
 .................................

Atom 1 is Nitrogen, 826 is Carbon, 830 is Calcium, 831 is Zinc and
832 is Oxygen.

  NOTES ON HKLIN
  
   List of H K L .. FP SIGFP ( FPART PHIP F0 .. F19 )
   
   An MTZ file with column labels corresponding to H K L .. FP SIGFP
   [FREE FPART PHIP F0 .. F19]. The header will contain the cell
   dimensions and spacegroup of the structure (if you want to change
   these, use MTZUTILS).
   
   For SFCALC this file MUST BE SORTED on h k l (i.e. so h is the slowest
   varying index, then k and l is the fastest), and be within the
   asymmetric unit expected by the program; see below for expected limits
   (CAD will reorder your file if necessary). It is sensible to do this
   if your data has not been processed by CCP4 programs. XDS, MADNESS
   etc. sometimes have different default asymmetric units to the CCP4
   suite.
  # an example of sorting native data and checking for correct
  # asymmetric unit
  cad  HKLIN1 $CEXAM/toxd/toxd HKLOUT toxd_sorted <<EOF
  TITLE  Toxd data sorted - default symmetry P212121
  LABIN FILE 1 E1=FTOXD3 E2=SIGFTOXD3
  CTYPE FILE 1 E1=F  E2=Q
  EOF

   For SFREF this file MUST BE SORTED on h k l (i.e. so h is the slowest
   varying index, then k and l is the fastest), and be extended if
   necessary to cover the whole asymmetric unit expected by the program
   for the SF spacegroup; see below for expected limits. If you are
   working at a lower symmetry than optimal the data must have been
   extended and sorted (CAD will do this too). There is a reason -
   sorting data is quite slow, and you will probably use this file many
   times during the course of a refinement.
  # an example of extending and sorting native data to P1 +-h,+-k,+l
  cad HKLIN1 $CEXAM/toxd/toxd HKLOUT toxd_p1  << EOF
  OUTLIM SPACEGROUP P1
  TITLE  Toxd data extended to P1 cell
  LABIN FILE 1 E1=FTOXD3 E2=SIGFTOXD3
  CTYPE FILE 1 E1=F  E2=Q
  EOF

   The agreement factor analysis is carried out against the values of FP.
   Sigma values are assumed to be in column SIGFP.
   
   IF FPART and PHIP have been defined, the FC vector equals the FPART
   vector plus the FC contribution calculated from the input. FPART can
   be scaled by entering a suitable value on the SCALE input.
   
   Other columns in the input file can be copied to the output file by
   assigning them to F0= F1= ... Or all columns can be copied over if the
   ALLIN subkeyword is given in LABOUT.
   
   Limits for Indices for the various space groups (these are the same as
   those used in the data reduction programs and FFT):

     P1          h k l : l >= 0
                 h k 0 : h >= 0
                 0 k 0 : k >= 0
     P21         h k l : k >= 0, l >= 0
                 h k 0 : h >= 0
     P21212      h k l : h >= 0, k >= 0, l >= 0
     P212121     h k l : h >= 0, k >= 0, l >= 0
     P41212      h k l : h >= 0, k >= 0, l >= 0, h >= k
     (+ other tetragonal)
     P31/P32     h k l : h >= 0, k > 0
                 0 0 l : l > 0
     P3/R3       h k l : h >= 0, k > 0
                 0 0 l : l > 0
     P3121/P3221 h k l : h >= 0, k >= 0, k <= h   (all l)
                 h h l : l >= 0
     P61/P65     h k l : h >= 0, k >= 0, k <= h   (all l)
                 h h l : l >= 0

  NOTES ON MAPIN
  
   A standard MAP file. The header will contain the cell dimensions and
   spacegroup of the structure.
   
   If you wish to generate structure factors from a input map it is
   essential that the map is in an appropriate format for the SFALL
   spacegroup you request.
   
   Common errors are:
   
   1) using a different grid for the FFT calculation and the SFALL
   calculation. FATAL!
   
   2) Changing the axis order in the FFT calculation - both have the same
   defaults for the same spacegroup! FATAL!
   
   3) Choosing a different asymmetric unit for the FFT and the SFALL
   calculation. You must make sure your map has the one which covers the
   SFALL requirements. There is no flexibility here.
   
   Limits for axes for the various space groups (these are the same as
   those used as defaults in FFT):
   
     In space group P1, P21 and P21212a, 'b' is taken as the unique
     axis.
     
     In space group P21212a, 1/4 is subtracted from the X and Y values
     of the equivalent positions given in International Tables.
     

                   X1     X2     X3     Range of X3  Axis order

       P1          Z      X      Y      0 to Y         Z X Y
       P21         Z      X      Y      0 to Y/2-1     Z X Y
       P21212a     Z      X      Y      0 to Y/4       Z X Y
       P212121     X      Y      Z      0 to Z/4       Y X Z
       P4122       X      Y      Z      0 to Z/8       Y X Z
       P41212      X      Y      Z      0 to Z/8       Y X Z
       P4322       X      Y      Z      0 to Z/8       Y X Z
       P43212      X      Y      Z      0 to Z/8       Y X Z
       P31         X      Y      Z      0 to Z/3-1     Y X Z
       P32         X      Y      Z      0 to Z/3-1     Y X Z
       P3          X      Y      Z      0 to Z-1     Y X Z
       R3          X      Y      Z      0 to Z/3-1     Y X Z
       P3121       X      Y      Z      0 to Z/6       Y X Z
       P3221       X      Y      Z      0 to Z/6       Y X Z
       P61         X      Y      Z      0 to Z/6-1     Y X Z
       P65         X      Y      Z      0 to Z/6-1     Y X Z

  OUTPUT from Structure Factor Calculation
  
   Note: The logfile has been flagged with XLOGGRAPH symbols to allow
   selected output to be displayed on an Xterminal.
   
   (a)
          The limits of the box used in modelling the electron density.
          
   (b)
          A list, with coordinates, of the first 10 atoms included in
          generating the model electron density map.
          
   (c)
          The number of atoms input, the number of atoms in the sorted
          list of atoms, and the number of atoms used in generating the
          electron density.
          
   (d)
          The minimum, average and maximum values of the temperature
          factors for the atoms.
          
   (e)
          Minimum and maximum electron density values are printed for
          each section of the generated density. The number of slabs used
          depends on the space allocated for the work arrays in the
          program.
          
   (f)
          The number of reflections used and the number of reflections on
          file.
          
   (g)
          Old and new scale factors (with an overall temperature factor
          BOV if temperature factor dependent re-scaling was applied).
          
   (h)
          A structure factor summary table in ranges of
          4sin**2theta/lambda**2 giving, for each range, the number of
          reflections, the average values of Fobs and Fcalc, the
          reliability index and an average value of the weighted errors.
          
   (i)
          The overall reliability index after re-scaling.
          
  NOTES ON XYZOUT
  
   Coordinates in Brookhaven format with the XYZ or B shifts applied -
   output of unrestrained refinement.
   
   The proportion of the shift to be applied can be modified (see the
   description of keyword STEPSIZE).
   
   If an input atom has occupancy of 0.0 it will be copied to the output
   file.
   
  NOTES ON HKLOUT
  
   The output file contains FC and PHIC only for those reflections which
   exist in the HKLIN file, even if the structure factor calculation has
   covered more of reciprocal space. The list will include ALL
   reflections in HKLIN within the outer resolution limit. There is no
   inner resolution cutoff, or sigma cutoff. Hence there may well be more
   reflections included than during refinement and your R-factor may well
   be higher than the one output during refinement. All columns specified
   in LABIN will be written to HKLOUT. If ALLIN is specified then all
   input columns will be in HKLOUT.
   
   If no HKLIN has been assigned the program outputs a list of H K L FC
   PHIC for all possible reflections within the reciprocal asymmetric
   unit for the SFSGROUP that are within the requested resolution limits.
   
   FC and PHIC can be modified for use in solvent flattening (see keyword
   AVMODE).
   
  NOTES ON MAPOUT
  
   Several types of maps can be output - see keyword MODE for how to
   produce each one.
   
   a)
          The `atom map'. All density assigned at each grid point due to
          a neighbouring atom.
          
   b)
          The `atom map' modified to include a residue flag for each main
          chain and side chain atom which has contributed most to this
          grid point. This allows the map correlation program to produce
          a set of correlations residue by residue between an ideal map
          (the `atom map') and any other map - part of real space
          R-factor stuff.
          
   c)
          The `atom map' modified to include an atom number flag. This
          can be used to look at hydrogen density in a neutron map.
          
   d)
          A `solvent map' with zero at all points within the protein and
          some constant (H2obg) at all other points. This is a step on
          the way to adding in bulk solvent to calculated structure
          factors.
          
  OUTPUT from the Gradients Calculation - NOTES ON GRADMAT
  
   A direct access file of gradient information is output ready for input
   to PROLSQ (no longer available in the CCP4 Suite). The following items
   are output in this section:
   
   (a)
          The value of the minimisation function (PII). Plus the number
          of reflections included in the calculation of PII.
          
   (b)
          The average and peak values of the gradients and shifts.
          
   (c)
          The slope of the search direction and the initial step size
          used in the quadratic approximation to find the optimum step
          size.
          
   (d)
          For unrestrained refinement a table of estimated error against
          B-factor is given. For each temperature range there is the
          number of atoms and the estimated error (standard deviation).
          
  OUTPUT from the Calculation of the Optimum Shifts
  
   This section gives PII (minimisation function) values, relative
   slopes, calculated optimum step sizes and, when determined, the actual
   step size used in applying the shifts.
   
  NOTES ON STEPSIZE
  
   R. Agarwal attempted to estimate the best step size to use during
   UNRESTRAINED refinement. A displacement of the form alphaDelta(u),
   which minimises the minimisation function of the least squares P(u +
   alphaDelta(u)), will be the optimum where alpha is the optimum step
   size. As P as a function of alpha approximates to a quadratic
   function, it is possible to calculate the optimum step size, alphaopt,
   from the values of P(alpha) at alpha = 0 and alpha = alpha1 and from
   the slope of P(alpha) at alpha = 0. The initial step size alpha1 used
   in the calculation is chosen as 1.0 or the value input in the control
   data. If the fractional change in step size is greater than SZFRC (by
   default 0.3) then a second calculation is done with alpha1 taken as
   the optimum step size just calculated.
   
COMMON PROBLEMS

    1. Problem: Warning after opening the input reflection file HKLIN
       about the sort order not being H K L.
       Solution: This may not crash the program (sometimes it does) but
       even so some of the output may be unreliable if the reflections in
       HKLIN have not been sorted with h as the slowest, k as the
       intermediate, and l as the fastest varying index. See NOTES ON
       HKLIN above for the requirements placed on HKLIN.
    2. Problem: No conversion from orthogonal to fractional atom
       co-ordinates (ie listed fractional co-ordinates have no value, or
       the same values as the orthogonal co-ordinates).
       or
       Problem: Program stops with the message:
       **** No Cell Input to subroutine rbfro1?? ****
       after reading in XYZIN.
       Solution: Check that CRYST1 and SCALE cards are present in the
       input co-ordinate file XYZIN.(See NOTES ON XYZIN above).
    3. Problem: Program crashes or stops after reporting statistics on
       B's in MODE SFCALC. (May also occur in other MODEs for the same
       reason.)
       Solution: Check that the input reflection file has the correct
       asymmetric unit and that the reflections have been sorted so that
       h is the slowest changing index, k is the next, and l varies the
       fastest. (See NOTES ON HKLIN above). Nb: the program should now
       generate an explicit error message suggesting that this is the
       problem.
    4. Problem: Program fails after printing the title and the line
       "Chain Names - First Residue - Last Residue - serial Kcount"
       (possibly also with error messages concerning array sizes).
       Solution: You may have to increase the value of MEMSIZE (see
       MEMORY ALLOCATION above). N.B.: the program should now generate an
       explicit error message suggesting that this is the problem.
    5. Common problems associated with the input map can be found in the
       section NOTES ON MAPIN.
       
EXAMPLES

  Calculate map from atom coordinates
  
sfall
XYZIN  /f/scratch/swift/pa_model1_2.pdb
XYZOUT  $SCRATCH/junk.pdb
MAPOUT $SCRATCH/junk.map
<< END-sfall
TITL Phasing on initial PA structure (refined twice)
GRID 52 64 76
MODE ATMMAP
RESO 30 2.1
BINS  60
RSCB 5.0 2.1
SFSG 1
END
END-sfall

  Read in coordinates to calculate structure factors
  
sfall
HKLIN $SCRATCH/pt2_pt4_shhg2_os2_nat.mtz
HKLOUT $SCRATCH/pa_model1_2_phase.mtz
XYZIN  /f/scratch/swift/pa_model1_2.pdb
<< END-sfall
TITL Phasing on initial PA structure (refined twice)
GRID 52 64 76
MODE SFCALC XYZIN HKLIN
RESO 30 2.1
BINS  60
RSCB 5.0 2.1
SFSG 1
LABI FP=F_V4 SIGFP=SIGF_V4 FREE=FreeRflag
LABO FC=FC PHIC=AC
END
END-sfall

  Read in map to calculate structure factors
  
sfall
HKLIN $SCRATCH/pt2_pt4_shhg2_os2_nat.mtz
HKLOUT $SCRATCH/pa_model1_2_phase.mtz
MAPIN $SCRATCH/junk.map
<< END-sfall
TITL Phasing on initial PA structure (refined twice)
GRID 52 64 76
MODE SFCALC MAPIN HKLIN
RESO 30 2.1
BINS  60
RSCB 8.0 2.1
SFSG 1
LABI FP=F_V4 SIGFP=SIGF_V4
LABO FC=FC PHIC=AC
END
END-sfall

  Iteration_cycles to do the back-transformation and phase combination cycles
  in solvent flattening procedure
  
#   - back-transform map with sfall to obtain Fcs and phases, scale
#     and calculate R-factor
#   - combine the phases with sigmaa
#   - run fft to calculate a new map with Fobs and combined phases as
#     input to flatmap
#
sfall     HKLIN ../mtz/fvb18_sigmaa.mtz
                HKLOUT fvb_flat_14.mtz
                MAPIN  fvb_flattened_14.map
                << EOF-sfall
titl back transformation for cyc 14
mode SFCALC MAPIN HKLIN
grid 104 128 160
reso 200.0  3.0
BINS 40
rscb 10.0 3.0
sfsg  19
AVMODE RADIUS 8
badd 0
FORM NGAUSS 5  C H N O S
LABI FP=fvb_Fnp SIGFP=fvb_SIGFnp -
F0=PHIB_I3 F1=FOM_I3  -
F2=A F3=B F4=C F5=D
LABO   FC=FCWANG  PHIC=PHICWANG WANGWT=WC8
END
EOF-sfall

  Unrestrained refinement
  
sfall
HKLIN ../data/taka_fx_trunc.mtz
XYZIN ../data/takaxp_model8_b.pdb
XYZOUT $SCRATCH/junk.pdb
<< END-sfall
TITL TAKAXP_MODEL8_9 SFS
GRID 104 136 264
MODE SFREF XYZ UNRESTRAINED
FREE 3.0
RESO 20 2.1 60
RSCB 8.0 2.1
SFSG 19
FORM NGAU 2 Ca Cr Fe+2 P
LABI FP=FP SIG=SIGFP FREE=FreeRflag
END-sfall

  Prolsq refinement cycles
  
#!/bin/csh -f
#
#          REFINE consists of sfall, protin and prolsq
#
set LastCycle=146
set Number_of_Cycles=8
set CycleCounter=0
#
Begin:
#
@ CurrentCycle=$LastCycle + 1
#
#    ========== SFALL ==========
#
set DATE=`date`
echo ' *************************** '$CurrentCycle' **************'
echo '    '
echo ' Running SFALL for Cycle Number :' $CurrentCycle' on '$DATE
echo '    '
echo ' *************************** '$CurrentCycle' **************'
#
sfall    HKLIN   s91a.mtz
        XYZIN   s91a_cyc${LastCycle}.brk
        GRADMAT s91a_GRADMAT${CurrentCycle}.tmp
        << END-sfall
TITL Barnase s91a Mutant
MODE SFREF XYZB RESTRAINED  ! for prolsq
GRID 90 90 120       !div CELL by these should give .=. 0.7 A
BINS 60
RESO 10 2.2        !last no. is nstep
RATI 3             !truncate xyz and B shrifts to RATI*RMS
BADD 0             !smear the gaussians to gen atomic density [10.0]
RSCB 4 1.5         !limits for refining scale and B, same as RESO ?
SFSG 145      ! fft space group
LABIN FP=S91A_F SIGFP=S91A_SIGF FREE=FreeRflag
END
END-sfall
#
/bin/rm ${SCRATCH}s91a_junk.brk ${SCRATCH}sfall*
#
#    ========== PROTIN ==========
#
set DATE=`date`
echo ' *************************** '$CurrentCycle' **************'
echo '    '
echo ' Running PROTIN for Cycle Number :' $CurrentCycle' on '$DATE
echo ' Running PROTIN for Cycle Number :' $CurrentCycle' on '$DATE
echo '    '
echo ' *************************** '$CurrentCycle' **************'
#
protin XYZIN      s91a_cyc${LastCycle}.brk
       PROTOUT    s91a_protout.out
       PROTCOUNTS s91a_protcounts.out
       DICTPROTN  ${LIBD}protin.dict
       << END-protin
TITLE Barnase Ser91 -> Ala
SYMMETRY 145
!
CHNNAME ID A CHNTYP  1 ROFFSET 0
CHNNAME ID B CHNTYP  2 ROFFSET 0
CHNNAME ID C CHNTYP  3 ROFFSET 0
chnname id E chntyp  4 roffset 0
!
CHNTYP  1    NTER 3   VAL 3     CTER 110 ARG 2
CHNTYP  2    NTER 3   VAL 3     CTER 110 ARG 2
CHNTYP  3    NTER 2   GLN 3     CTER 110 ARG 2
chntyp  4    wat
!
LIST  FEW          ![few]/some (for >20A)/all
PEPP  5            !no. of atoms restrained to be in a plane [5]
VDWR 1 CPR  8 3.4
END
END-protin
#
#    ========== PROLSQ ==========
#
set DATE=`date`
echo ' *************************** '$CurrentCycle' **************'
echo '    '
echo ' Running PROLSQ for Cycle Number :' $CurrentCycle' on '$DATE
echo '    '
echo ' *************************** '$CurrentCycle' **************'
#
prolsq XYZIN      s91a_cyc${LastCycle}.brk
       PROTOUT    s91a_protout.out
       PROTCOUNTS s91a_protcounts.out
       GRADMAT    s91a_GRADMAT${CurrentCycle}.tmp
       XYZOUT     s91a_cyc${CurrentCycle}.brk
       << END-prol
TITLE    Barnase s91a Mutant
CGCYCLES 20  100 1 !max no. cyc for conjugate gradient soln [50]
ORIGIN 0 0 0           !origin constraint flags
RESOLUTION 10 2.2      !select Fobs
OUTPUT XYZ             !o/p XYZ(.brk)/SF(.mtz)/SHIFTS(shifts file)
RTEST -1 1 1 1 1 1 1 1       !-1 -> +1 when R factor .=25%
NOUPDATE                    !not update atomic coord in PROTIN o/p file
MATRIX .30 .85 .85          !1st param adjusts SF/geom contribution
                            !start=.08;.12;.2;.25;.3;.35; final=.08
                            !2nd&3rd:shift factors for position and B
BATOM                       !(+) when refining indiv B
!
!               ***** Restraints *****
DISTANCE     1 0.02 0.04 0.05 0.01 0.1
PLANE        1 0.02
CHIRAL       1 0.12
TEMPERATURE  1.0 1.0 1.5 1.5 2.0 0.1   !start
!TEMPERATURE  1.0 1.5 2.0 2.0 2.5 3.0  !when R factor <25%
HOLD         0.1 1.0 0.1
!TORSION      1 20 20 30 50            !when R factor >25%
TORSION      1 10 10 15 45            !when R factor <25%
VANDERWAAL   1 0.2 -0.3 0.0 -0.2 0.0
!
!                ***** Monitor *****
MONITOR  DISTAN 3. VANDERWAAL .5  TORSION 3
MONITOR  PLANE 3 CHIRAL 3 !for R factor<25%
END
END-prol
#
Cleanup:
#
/bin/rm s91a_protout.out s91a_protcounts.out s91a_GRADMAT${CurrentCycle}.tmp
#
@ CycleCounter=$CycleCounter + 1
@ LastCycle=$LastCycle + 1
#
#    Test to see whether Number_of_cycles done
#
if ($CycleCounter<$Number_of_Cycles) goto Begin
#

  Simple Runnable Examples
  
     examples/unix/runnable/sfall.exam
   
AUTHORS

   Eleanor Dodson and Ted Baker, based on a program by Ramesh Agarwal and
   Neil Isaacs. Documented for the Daresbury Laboratory protein
   crystallography system by John Campbell.
   
PROGRAM FUNCTION

   The program is based on a least-squares refinement technique using
   fast Fourier transform (FFT) methods as devised by Ramesh Agarwal. His
   paper [1] on the technique should be studied to get a detailed
   understanding of the method and only a broad description of the method
   is given in this section.
   
   The program may be used for
    a. calculating and outputting the matrix and gradient terms required
       by the restrained least squares refinement program PROLSQ (no
       longer available in the CCP4 Suite). The calculated shifts can be
       applied directly to the atomic coordinates/B-factor, unrestrained
       refinement.
    b. The generation and calculation of an electron density map from an
       input set of atomic coordinates and its transformation, using FFT
       techniques, to obtain a set of calculated structure factors. The
       program SFALL is used to calculate structure factors from an
       electron density map using Fast Fourier Transform techniques.
       Whenever possible, the crystallographic symmetry is exploited to
       increase the efficiency of the calculation. Care must be taken by
       the user to ensure that the map has been calculated on a
       sufficiently fine grid if significant errors in the calculated
       structure factors are to be avoided. As a rough rule a grid size
       of approximately three times the maximum index of the data in each
       direction is appropriate. The use of the Fast Fourier Transform in
       structure factor calculations for large molecules has been
       described and discussed by L.F. Ten Eyck [3].
    c. The calculation of structure factors from an electron density map.
       The same cautionary measures must be applied as those explained in
       (b).
       
  Modelling of the Electron Density and Calculation of Structure Factors
  
   The contribution of an atom to a structure factor is the product of an
   atomic form factor function and a Gaussian temperature factor
   function. If the form factor function is approximated by a sum of
   Gaussian functions, then this contribution may be represented by the
   sum of Gaussian terms and so may the modelled electron density. The
   amount of computation required in setting up the electron density map
   is proportional to the number of Gaussian terms used in approximating
   the form factor. The use of a two term Gaussian is probably adequate
   in most cases where the resolution of the data does not extend beyond
   1.5Å. The program does, however, allow for the input of other numbers
   of terms. Non default atoms defined in FORMFACTOR are usually
   represented as five Gaussians since heavy atom scattering factors are
   more complex.
   
   Tables of coefficients for a five term Gaussian approximation to the
   atomic form factors are given in the International Tables for X-ray
   Crystallography Vol.IV [2]. Some values for two and one term Gaussian
   approximations are given in the Agarwal paper.
   
   The radius of the atoms (beyond which the electron density is
   considered to be negligible) is also required in the calculation. The
   value for this radius must be chosen to balance the requirements of
   accuracy (large radius) and speed (small radius). The tables below
   indicate the radii required for carbon atoms, for different
   temperature factors (Bm), to give a given fractional loss of electron
   density (DeltaZm/Zm).

                    DeltaZm/Zm     0.02     0.01     0.005
Two term Gaussian         Bm
                           5       1.89     2.06     2.22
                          10       2.02     2.21     2.38
                          20       2.26     2.47     2.68

More values are given in the Agarwal paper.

   The electron density map is built up using the contributions from each
   atom within, or near (within the atom radius) to, the part of the map
   being calculated. A three dimensional FFT of the electron density map
   is used to calculate the structure factors. In this calculation the
   space group symmetries are used whenever possible.
   
   If the sampling grid is too coarse, significant errors may occur in
   the calculation of the structure factors. These errors may be reduced
   [3] either by using a finer grid for the calculation or by adding an
   artificial extra temperature factor to all the atoms when modelling
   the density (not recommended). This factor has also to be taken into
   account when the calculated structure factors are compared with the
   observed structure factors.
   
  Calculation of the Gradients
  
   The gradients are calculated by convoluting a modified difference
   density function with the electron densities of the individual atoms
   being refined. The density function is calculated by calculating the
   Fourier transform (again using the FFT) of a difference function based
   on the weighted values of the errors in the structure factors. A three
   dimensional difference FFT is calculated and convoluted with the
   derivatives of the atomic density for x y and z, or B. The convolution
   is carried out by summing, over all the grid points enclosed by the
   atom (radius defined as described above), the product of the electron
   density of the atom and the value of the modified difference density
   function. Thus, the calculation of the gradients is similar to the
   calculation of the structure factors with the steps being reversed.
   
  The Normal Matrix
  
   Only the diagonal terms (interacting between parameters of the same
   atom) are calculated for the normal matrix. The method described by
   Agarwal is used but is generalised to allow for a variable number of
   terms in the Gaussian approximations to the atomic form factors. Also
   the function A'xx(bi) is tabulated for each value of bi from 1 to 150
   and the nearest values, rather than interpolated values, are selected
   from the table when forming the diagonal terms of the matrix.
   
   A set of terms, H, is only calculated for one parameter as the other
   diagonal terms may be calculated to a good degree of accuracy from
   this initial set. An inverse matrix is set up for calculating the
   orthogonalised contributions of the gradient.
   
  Calculation of the Shifts
  
   The shifts, calculated as described above, may not in fact be the
   optimum ones to use due to the approximate nature and the
   non-linearity of the method used. In practice, it is unwise to apply
   large shifts as these may give rise to instability in the refinement
   or to `oscillating atoms' and thus provision is made to truncate the
   larger shifts. The program allows for the input of a ratio, RATIO,
   which may be used to truncate the maximum value of a shift to
      RATIO * r.m.s. value of the shifts

   At the beginning of a refinement, the value of RATIO should be kept
   fairly low (1.5-2.0) as shifts tend to be large when the errors in the
   parameters are large. When most atoms are well refined, then the ratio
   may be increased to 3 or 4, to allow for the refinement of these atoms
   which are poorly placed.
   
   Even these truncated shifts may not be the optimum shifts to be
   applied. A displacement of the form alphaDelta(u), which minimises the
   minimisation function of the least squares P(u + alphaDelta(u)), will
   be the optimum where alpha is the optimum step size. As P as a
   function of alpha approximates to a quadratic function, it is possible
   to calculate the optimum step size, alphaopt, from the values of
   P(alpha) at alpha = 0 and alpha = alpha1 and from the slope of
   P(alpha) at alpha = 0. The initial step size alpha1 used in the
   calculation is chosen as 1.0 or the value input in the control data.
   If the fractional change in step size is greater than SZFRC (by
   default 0.3) then a second calculation is done with alpha1 taken as
   the optimum step size just calculated.
   
REFERENCES

    1. Agarwal, R.C., Acta Cryst., (1978), A34, 791-809.
    2. International Tables for X-ray Crystallography, Vol.IV, (1974),
       Kynoch Press.
    3. Ten Eyck, L.F., Acta Cryst., (1977), A33, 486.
    4. Bruenger, A.T., Nature 355, 472-4 (1992)
    5. International Tables for Crystallography, vol. C, (1995), Kluwer.
    6. "Refinement of protein structures", Proceedings of the Daresbury
       Study Weekend 15-16 November, 1980 (Compiled by P.S. Machin, J.W.
       Campbell and M. Elder).
       
SEE ALSO

   cad, freerflag, fft, icoefl, mtzutils, overlapmap, pdbset, prolsq (no
   longer available in the CCP4 Suite), protin, sigmaa, watersearch (1),
   xloggraph, X-PLOR manual