JOYLESS SKEWING
                             by   FRUSTRATED of YORK.

                     or

               YORK AGAINST SKEWING.
                                    Four down and some to go..

  This is 
   1) a typescript of Gerard Bricogne's original SKEW writeup which  
         Adam Ralph typed up at York.
      This was prepared for the IBM version.

   2) a typescript of the skew procedure from the CCP4 suite with
       comments.

   3) a description of the procedure in use at York.  People seem to 
      be able to implement it reasonably easily.
 
  Carefully annotated examples of COM files for averaging in
  space groups P41212  P21 C2 and R3 are given at the end.

    We aim to produce skewed maps on the same grid as the original 
  map.  This allows the original map and the skewed map(s) to be
  displayed together in FRODO.


    To do this according to Gerard would require that the output 
  (i' j' k') frame is not orthogonal.  
    But we choose to align the (i' j' k') frame with the (i j k) 
  frame "canonically" associated to the crystallographic frame 
  and to "stretch" the output map . The "stretching" matrix is a 
  function of the crystal angles and is defined below.
     The origin is kept at (0.0,0.0,0.0) .

        Our technique has been carefully tested .
              ***   TRUST   ME  ***

        A good test is to put the rotation matrix equal to the identity
  and check that you are mapping grid 1 onto grid 2  with the 
  transformation 
             1  0  0               0
             0  1  0               0
             0  0  1               0
  This is output at the end of the GENERATE step.

.....
         MAPPING BETWEEN GRID COORDINATES ( #2 TO #1 ) :

                 MATRIX                                    VECTOR

 0.9999971   0.0000003   0.0000000                         0.00000
 0.0000000   0.9999992   0.0000000                         0.00000
 0.0000000   0.0000001   0.9999954                         0.00000
......



    We  always work in the P1 system and run EXTEND to extend the map 
   to cover the unit cell and to change the spacegroup number to 1. 
   Running EXTEND is much quicker than using the SKEW symmetry stuff.
   
     The rotation matrices and translation vectors can be obtained from
   LSQKAB which gives the Least Squares fit of one set of cordinates
   on to another
            ********** IF   AND ONLY IF ***********
   your coordinates are othogonalised  in the same convention as 
   SKWPLANES expects. 



   1)       This is a typescript of Gerard's old writeup.
             It is probably best to begin with the theory 
            given here; then look at the examples and remind
            yourself of what each data line is about..


                          THE  JOY  OF  SKEWING
                         -----------------------
                         -----------------------

                                                   (in part)



              III.2            GENERATE
                              ----------


              III.2.1          Purpose
                               -------


	This program generates the mapping between grid coordinates in
    the final and initial maps. It can work in several modes;  mode  1
    corresponds to skew-section calculation with  optional  averaging.
    Its output is a file of records of the form :
                             _
                        I2 , X1(Tm I2)          m=1....n



              III.2.2    Algebra of coordinate frame
                         ---------------------------

	The notation may not be everywhere identical to that  of  §II,
    but this should not lead to any confusions.

              FRAMES

	(a, b, c) : crystallographic frame, on which grid G1 is based.
    Origin O. Coordinates E1, n1, C1 are dimensionless, and vary  from
    0 to 1 in the unit cell.

	(i, j, k) : orthogonal frame of 1Å-length vectors, 
    "canonically" associated to the crystallographic frame. Origin  O.
    Coordinates x,y,z in this frame are in Å. This frame is used as  a 
    reference to define the orientation of the skew grid.
	The convention used to  define  this  frame  for  some  common 
    crystal classes are shown below :

a)                      TRIgonal
                      ----------
                          Axes  (a,b*, axb*)

     NB:   This is NOT the Brookhaven convention (NCODE=1).  It is 
   given as NCODE=6 in all CCP4 orthogonalisation conventions.
    But for all crystal systems except trigonal it is the same as 
   the Brookhaven default  which is
               Axes     (a, c*xa, c*)       (NCODE=1)


b)                      MONOCLINIC
                      ----------



                           j    i
                        b O_________________a
                         /l  
                        / l k
                       /  l
                      /   l                  i.e. NCODE=1 in York
                     /    l                         convention
                    /     l
                 c /      l c*

 
  
                      (i, j, k)= normalised    b // k and out of page

                      (a, b, c*) frame


c)                     ORTHORHOMBIC
                       -----------
  

                            k
                        c O___________________b
                          l          j
                          l
                          l
                          l i
                          l                     NCODE=1
                          l
                          l
                          l
                         a 

  
                       (i, j, k)= normalised   c // k and out of page

                       (a, b, c) frame

                
d)                    RHOMBOHEDRAL
                      ------------

                          k
                        c O____________________ b
                         /      .
                        /  90         .
                       /                    .
                      /                    j          NCODE=1
                     /
                  a /
                   / i                  ???? EJD - is this correct??

                      (i, j, k)= normalised   c // k and out of page
                      (i, j, k)      ? parallel to  a+b , a-b ,c ???

                      (a, b*, c) frame     ???????


 
           N.B. A 'normalised' frame is a frame of 1Å-long vectors


	(i', j', k') : normalised  frame  (not necessarily orthogonal)
    on which the output grid G2 is based. The origin of this frame can
    be an arbitary point O', with crystallographic  coordinates  noted
    (E°1, n°1, C°1). Coordinates in this frame are denoted x2, y2, z2;
    and are in Å, but not necessarily orthogonal.
	

   ( In York we align (i' j' k') with (i j k) and keep the origin at
     the crystal origin)






                  b l           j' \     / i'
                    l               \   /
                    l                \ /
                    l                 O'
                    l                    °
                    l                        ° k'
                    l
                    l
                 j  l
                    l
                    l       i
                    O------------------------ a
                 . /
               .  /
             .   / k
           .    /
         .     /
       .      /                      For mongonal
     . c     /
            /c*                      (a, b, c) crystallographic frame

                                     (i, j, k) intermediate frame

                                     (i', j', k') new frame





               GRIDS
               -----

	  Intial grid G1.
	Based on (a, b, c).  Defined  by  na, nb, nc,  numbers  of map
    divisions along a, b, c respectively. The grid coordinates  in  G1
    will be denoted by x1, y1, z1.
	The initial domain D1 is defined by na(i), na(f), nb(i), nb(f)
    , nc(i),nc(f)  initial  and  final  values  of  intergral  grid 
    coordinates for which the density is given in  the  original  map. 
    The relation of these numbers to na, nb, nc will be discused below
    in §III.2.3.
          Final grid G2.
	Based on (i', j', k'). Defined by Dx, Dy, Dz,  grid  intervals 
    in Å along i', j', k' respectively. Grid  coordinates  in  G2  are 
    intergral and are denoted by i2, j2, k2.
	The final domain D2 is defined by  nx(i), nx(f), ny(i), ny(f),
    nz(i), nz(f), initial and final values of grid  coordinates  along 
    i', j', k' for which the density is calculated.

      	       MATRICES
               --------

	     na   0   0                Dx   0   0
	G1=   0  nb   0       and G2=   0  Dy   0
              0   0  nc                 0   0  Dz

                   define grids G1 and G2.

	Q= the transition matrix from (a, b, c) to (i, j, k).  Q  thus
    discribes the relation of the intermediate  orthonormal  frame  to 
    the crystallographic frame. It is  calculated  in  a  space  group 
    specific routine (see III.2.3)


         astar*sin(Bstar)*sin(G)  -astar*sin(Bstar)*cos(G)  astar*cos(Bstar)
      Q=    0                      bstar*sin(Astar)        -bstar*cos(Astar)
            0                           0                   cstar
                                 for a trigonal space group.
 

            1/a     0    -cot(B)/a
	Q=    0   1/b       0            for a monoclinic space group
              0     0   1/(c sin(B))

            1/a     0     0
	Q=    0   1/b     0            for an orthorombic space group 
              0     0   1/c

            1/a   -1*tan(60°)/a     0
        Q=  1/b   +1*tan(60°)/b     0     for a rhombohedral space group 
             0         0          1/c

	P = transition matrix from (i, j, k) to (i', j', k').  P  thus
    describes the orientation of the skew relative to the intermediate
    orthonormal frame.
	It may be useful at this point to recall the definition  of  a 
    transition matrix. The transition matrix P from an 'old' base to  a
    'new' base has its ith column the coordinates in the old base  of 
    the the ith vector of the new base. If x is a vector,  represented
    by the 1-column matrices Xold and Xnew in the old  and  new  bases
    respectively, then one has the well known contra-variance  property
    that :

                         Xold = P Xnew
                         ~      ~ ~

	(Um, Vm) , m=1...n : rotation matrix and translation vector of
    the mth averaging operation, expressed in (i', j', k').


                      TRANSFORMATION OF INDICES
                     ---------------------------


            x             x2               -1   E°1
            y     =   P * y2        +     Q   * n°1
            z         ~   z2              ~     C°1

        Å coords          Å coords              coords of O' in
      in (i,j,k)         in (i',j',k')            (a,b,c)


           E1            x                x2           E°1
           n1     =  Q * y      =    QP * y2     +     n°1
           C1        ~   z           ~~   z2           C°1

     crystallographic
     coords in (a,b,c)

                                  
	in matrix notation :      E  =  QP * X2 + X°
                                  -     ~~   

	Now :        x1     na    0    0      E1
                     y1 =    0   nb    0  *   n1     i.e. X1 = G1*E1
                     z1      0    0   nc      C1               ~  -


                     x2     Dx    0    0      i2
                     y2 =    0   Dy    0  *   j2     i.e X2 = G2*I2
                     z2      0    0   Dz      z2              ~
  

	thus,      X1 = G1[QP(G2*I2) + X°] = (G1*QP*G2)I2 + G1*X°

 	If the averaging transformations have the form :

                   X2(m)  = Um*X2 + Vm = Um(G2*I2) + Vm    m=1...n

                   X1(m)  = G1[QP(Um*G2*I2) + X°]

	Therefore 

                   X1(m)  = (G1 * QP * Um * G2)I2 + (G1*QP*Vm + G1*X°)


( C EJD December 1988. Program MATMUL will read n matrices and multiply
       them together to help check you have all these correct...)


              IV.          THE  PROCEDURE - See new procedure for 
                          ----------------     alterations





                 NB: 1987  Adam Ralph
       Much of the information required here is now in the Map header.
 Information about cards marked with *** is still needed.

	A  commented  procedure  is  provided  to  run  skew-section 
    calculations. It is listed on the next pages, followed by EXEC and 
    data cards. These data cards are :

    //SHNK.SYSIN DD *

    1)	SCALE	(E10.1)

	Multiplicative scale factor applied to the REAL*4 map before
    the shrinking operation (§III.1)

    //GNRT.SYSIN DD *

    1)	MODE	(1I5)                              ***

	Option number, should be 1 for skew-section calculations
    (§III.2.1)

    2)	A,B,C,ALPHA,BETA,GAMMA	(6F10.5)           

	Unit cell parameters in Å and degrees.

    3)	NA,NB,NC	(3I5)                      

	Numbers of divisions along a,b,c  (§III.2.2, GRIDS)

    4)	NAI,NAF,NBI,NBF,NCI,NCF	  (6F10.5)         


	Initial and final grid coordinates along a,b,c defining the
    asymmetric unit of the initial space group (do see §III.2.3).

    5)	Dx,Dy,Dz	(3F10.5)                   ***

	Grid intervals in Å along skew axes (§III.2.2 GRIDS)

    6)	NXI,NXF,NYI,NYF,NZI,NZF	  (6I5)            ***

	Initial and final grid coordinates along skew axes, defining
    the domain desired on output (§III.2.2, GRIDS)

    7)	Xo,Yo,Zo	(3F10.5)                   ***

	Crystallographic coordinates of origin of new frame (E°1,n°1
    ,C°1 of §III.2.2, FRAMES).

    8.1) to 8.3)    P	(3F10.5/3F10.5/3F10.5)     ***

	Transition matrix is defined in §III.2.2, MATRICES.

    BEWARE: As P is read in  array  notation,  cards   correspond   to 
    columns of P.

    Thus

	Card 8.1 contains the direction cosines of i' in frame (i,j,k)
        Card 8.2 --------------------------------- j' ----------------
        Card 8.3 --------------------------------- k' ----------------

    9)	NROT	(1I5)                              ***

	Number of operations on skew coordinates by which the skew map
    is averaged, including the identity if it needs to be used.
	if NROT=0 the identity is assumed

    10) et seq.  (omitted if NROT=0) :             ***
                
                    (ROT(I,J,N),I=1,3),J=1,3     3*(3F10.5)
         N=1, NROT 
                    TRANSL(I,N),I=1,3              (3F10.5)

	The rotation matrix and translation vector for each  averaging
    transformation, expressed in the normed skew frame (i',j',k');  be
    careful if the frame is not orthogonal since  in  this  case  your 
    rotation matrices may not be orthogonal.
	Here again, each of the first three  cards  corresponds  to  a
    column of the rotation matrix, and the 4th to the components (in Å
    ) of the translation vector. There is such a pack  of  four  cards 
    for each transformation.
	NOTE : to compute these matrices and vectors,  bear  in  mind 
    that the translation is applied after the rotation (as in x'=Rx+T)

    10 + 4*NROT)   JSEC,JFAST,JSLOW	(3I5)      

	Sectioning flags for envelope array (omitted in mode 1, so you
    may ignore it)

    //SRT1.SYSIN DD *

	See example deck and §III.3

    //INTP.SYSIN DD *

    1)	JSECI,JFASTI,JSLOWI	(3I5)

	Sectioning flags for initial map (§III.4). Other columns are
    reserved for other options of the program. A 1 in column 30 will
    cause a detailed account of the interpolation to be printed.

    //SRT2.SYSIN DD *

	See example deck in §III.5

    //RECN.SYSIN DD *

    1)	NXI,NXF,NYI,NYF,NZI,NZF	 (6I5)

	Same card as card 6 in step GNRT

    2)	JSECF,JFASTF,JSLOWF	(3I5)

	Sectioning flags fro skew map (§III.6).  Other  columns  are 
    reserved for other options of the program.

    3) NROT 	(1I5)

	Same card as card 9 of step GNRT.

    4)	TITLE	(A80)                              *

	Any 80-character title for final skew map

    5) et seq. : any cards you want ; the program will not read 
                 them.


      *  Cards needed for new procedure

    //

									AM. 10.02.82




    2)   The CCP4 procedure.

         		SKEW PLANES PROCEDURE .
	        	-----------------------


	
	This file describes a procedure that can be used for running
G. Bricogne's skew planes package. A complete and detailed description
of the programs can be found in G. Bricogne's manual "THE JOY OF
SKEWING" (sic). The programs are identical to the ones described there
except for the sorting steps and some other minor changes described here.
The sort is done with a special purpose program written in Harvard.
Documentation for this can be found under BSORT.DOC.

	Besides the different sorts, the programs had been changed so as
to be compatible with the map-format subroutines available. For this
purpose an extra card has been added to the RECONSTITUTION program. This
should not be noticeable when running the programs under this procedure
but should be considered if the programs are to be run separately, as
described below.

	The data for the programs is created by program MAKEDATA that reads
the map file and creates the appropriate data files. The scale for the SHRINK 
step is calculated in basis of the maximum and minimum density in the map. In
the RECONSTITUTION step all densities are multiplied by the inverse of the
scale applied in SHRINK so as to leave the output map in the same scale as
before. Note that the values of the output densities may be smaller due to
interpolation and averaging effects. The output map has a header with space
group 1, and cell parameters and grid sampling corresponding to a P1 box of
arbitrary size. This values should make the map compatible with other programs
that take information of the map from the header. However, if there is a need
of changing this values it can be done with the program HEADER. 

	The data cards needed are described below.  There is no need of
all the cards  described in "THE JOY OF SKEWING" , but the ones
needed are identical to the ones in the manual. All input is read in free
format, so no item should be left blank.


0.  IBACK.
    -----
		Background flag. Usually set to zero. For other values
		refer to full write-up.

1.  MODE,ISPA.
    ----------
		MODE:
		Option number, should be 1 for skew-section calculations.

		ISPA:
		Only required when P1 option is to be used. Then ISPA
		should be set to 1. Other cases set ISPA to any number
		you like but different from 1. If your map header has
		1 as space group number, you can set ISPA to anything
		as well.

2.  DX,DY,DZ.
    --------
		Grid intervals, in A, along skew axes.

(  York procedure - see commented COM files. 
            Dx Dy Dz are the projections of the intervals in 
       the original map (ie a/nx b/ny c/nz)  onto the (i j k) axes.)

3.  NXI,NXF,NYI,NYF,NZI,NZF.
    ------------------------
		Initial and final grid coordinates along skew axes, defining
		the domain desired on output.  
  (York:  Cover the interesting  molecule. MINLIM will tell you these)

4.  Xo,Yo,Zo.
    ---------
		Crystallographic coordinates of the origin of skew frame.
(  York procedure - always (0,0,0) )

5.  P(3,3).
    ------
		Transition matrix. Described thoroughly in "The Joy of Skewing".
		Three cards, each card corresponds to a column of the matrix 
		and not to a row as in most cases.
(  York procedure - always the identity matrix )

6.  NROT.
    -----
		Number of operations by which the map is to be averaged. This
		is referred in the skewed frame. Should include the identity.

7.  ROT,TRANSL.
   ------------
		Rotation matrix and translation vector for each averaging 
		transformation, expressed in the normed skew frame. Again,
		the first three cards of each operation correspond to the
		columns of the rotation matrix and the fourth to the translation
		vector. There are as many groups of four cards as averaging
		operations.


  ( York: these are difficult!!! Use LSQKAB to tell you...)

Card 8a is included for MODE .ne. 1 only

8a.  JSECE,JFASTE,JSLOWE.
    -------------------
		Sectioning flag for envelope.

8.  JSECF,JFASTF,JSLOWF.
    -------------------
		Sectioning flag for output map.

9.  TITLE.
    ------
		Title for final skew map.


10. IHEAD.
    -----
		Header information. If zero writes arbitrary header. If
		1 reads in next card cell parameters (6), space group number
		and sampling (3). Any other number, copies the values of
		input map.


	For running the procedure it is necessary to assign an input map file as
well as an output map file. The input map goes to assignment MAPIN whereas the
output map goes to MAPSKEW. Intermediate files are created and deleted by
the procedure, in case of a crash it may be necessary to delete some files
left behind by the procedure. If the programs are to be used in a manner different
from the simple skew planes calculation or very big maps are to be skewed, it
may be convenient to run the programs separately and to break the sort steps
into several small jobs merging the files later with program MRGSORT.

	The command for running the procedures consists of three key-words:
SKWPLANES, DATA and START, in that order. Before the START card but after the
DATA card all data should be typed in the fashion and order described above.
After the word SKWPLANES the space group number of the programs to be linked
has to be provided. For example, if a map in space group P21212 is to be skewed
the number 18 (or 1018) has to appear after the word SKWPLANES. This is
absolutely unavoidable and compulsory. The input and output files are assigned
by means of the key-words MAPIN and MAPSKEW in the first command line. The
various scratch files are created on the device specified with logical name
SCRATCH: this defaults to dr1: but may be reassigned using the keyword SCRATCH
on the SKWPLANES command. If you are doing a series of cycles with the same
transformations, it can save time to save the sorted indices file from 
GENERATE from the first cycle: this can be done with a keyword on the START
command: on the first cycle SAVE saves the file (SCRATCH:SORT1.IND), and on
subsequent cycles SKIP skips the GENERATE and first sort. This is easily
understood by means of the following example. 


EXAMPLE 1.           CAMBRIGDE MRC
----------

$SKWPLANES 0 MAPIN [AM38.MAPA]SKWTWOF MAPSKEW [AM38.MAPA]RRSKW SCRATCH DR0:
$DATA
0,
1,0 
.93333,.93333,.93333
5,100,-5,5,-55,0
0.,0.,0.,
0.992546151,0.121869343,0.,
-0.121869343,0.992546151,0.,
0.,0.,1.,
1
1.,0.,0,
0.,1.,0.,
0.,0.,1.,
0.,0.,0.,
2,3,1
TMV DIFFERENCE MAP (2Fo-Fc).  Y SECTIONS  + 7 DEGREES.  09.02.82
28,
$START  SAVE

	In this case, the space group number is zero because the program needed
is the one linked with the dummy space group subroutine P0. The sorted indices
file is saved for another skew.







			HEADER PROCEDURE.
 			-----------------
	
	The purpose of this procedure is to change the header information of a map.
It does not add nor cuts any part of the map, just the header. The user should
watch that the new header parameters are consistent with the map characteristics.
The program can be easily run on line answering the prompts. For very big maps
it is reccomended to run it as a job as it has to read and write the whole map.
The way of using the procedure is exemplified below.

EXAMPLE 2.
----------

$HEADER MAPIN MAPA MAPOUT MAPA
$GO
:
:
:




			MRGSORT PROCEDURE.
			------------------

	The purpose of this procedure is to merge index files from the skew 
planes programs. The data card needed are described below.

1. Record Length.
-----------------
	Record length of index files. For INTERPOL files is 10, 6 for GENERATE
files.

2. Name of output file.
-----------------------

3. Number of files to be merged.
--------------------------------

4. Name of files to be merged.
-----------------------------
	One name per line, as many names as the number given in card 3.



EXAMPLE 3.
----------

$MRGSORT
$GO
10
SORT2.IND
2
INTER1.IND
INTER2.IND



			SHRINK  PROCEDURE.
			-----------------

     Logical names used by procedure :

             MAPIN     input map        (.MAP)
             MAPOUT    output map       (.MAP)
             INDICES6  input index file (.IND)

	The procedure requires a number inmedeately after the word SHRINK.
This number serves as identifier for the programs to link. If it
is ZER0 it will create and execute program for dummy space group
P0, if ONE it will create and execute program for space group P1,
any other number will default to normal program. In the last case
it will create program SHRINKDLB if an index file is present, else 
program SHRINK. The former can accept deleting records.

EXAMPLE 4
---------

$SHRINK 1 MAPIN MAPA MAPOUT OTROMAPA INDICES6 SOBRE
$GO
:
:


   WARNING:  The procedure creates a file for the execution step. The
   ========  name of this file is SHRINK.EXE and should be deleted by
             the user after the program has run.





			GENERATE  PROCEDURE.
			--------------------

     Logical names used by procedure :

             ENVIN     input envelope    (.MAP)
             INDICESA  output index file (.IND)

	The procedure requires a number inmedeately after the word GENERATE.
This number serves as identifier for the programs to link as the
program is space group specific. The space groups available are:
0,1,1018,23,and 4. 

EXAMPLE 5.
---------

$GENERATE 1018 ENVIN MAPA  INDICESA SOBRE
$GO
:
:


   WARNING:  The procedure creates a file for the execution step. The
   ========  name of this file is GENERATE.EXE and should be deleted by
             the user after the program has run.






			INTERPOL  PROCEDURE.
			--------------------


     Logical names used by procedure :

             MAPIN     input shrunk map    (.MAP)
             RECORD0n  input index files (n=1,2,...8)
			                   (.IND)
             RECORDUT  output index file   (.IND)

	No more than four assignments can be made in the procedure. If more 
assignments are needed use procedure STREAM before.

EXAMPLE 6.
----------


$INTERPOL MAPIN MAPA RECORD01 SORT1 RECORDUT TOSORT2 
$GO
:
:





			RECONST  PROCEDURE.
			-------------------

     Logical names used by procedure :

             MAPOUT     output map         (.MAP)
             DENSITY    input index file   (.IND)

	An extra card has been added to this program. It is the last card and it is
in free format. It needs the six cell parameters, the space group number of the 
output map, the grid sampling and an scale factor by which the output map is
multiplied. This last one is useful to reset the map to the initial density values
after boosting them with program SHRINK. Also, if the sampling values are set to
zero the values will be those of the output section as set in the first card. If
the last value is set to zero it will defaults to one. All values are compulsory
for this last card as it is read in free format.


EXAMPLE 7.
---------

$RECONST MAPOUT [AM38.MAPA]SKWBILD DENSITY DR1:[AM38]OUTINTER 
$GO
-25,30,-60,6,0,105,
2,1,3,,,
17,
TMV - DIFF. MAP  (Fo-Fc) : AVERAGED from FFT AFTER B2/BILD CYCLE OF ENEREF  09.02.82
223.8,174.3,227.8,90.0,90.0,90.0,1018,0,0,0,1.00E-03,
$DEL RECONST.EXE;*




			BSORT PROCEDURE.
			----------------

	This procedures runs the sort for the sorting steps in the skew planes
procedure. Information about it and the data cards it needs can be found under
BSORT.DOC. An example for the procedure is given below.

EXAMPLE 8.
----------

$BSORT
$GO
DRA0:[AM38]INDEX.TEM
DRA0:[AM38]RECORD01.TEM
10,
69,11,
452,518,
<CR>






    YORK EXAMPLES : 



  sk_AtoB_chmi.com   -    P41212  example

$!*****HAVE TO RUN THIS FROM DSSCR - it needs LOTS of scratch space****
$!  Here I want to output map for molecules B and C in the 
$!  orientation of molecule A.  Use the few coordinates assigned to 
$!  each molecule to get the appropriate matrices.

$!    Use the log file from the LSQKAB (command file below) to get
$!    rotation matrix and translation R and t which rotate A onto B.

$!    SKEWPLANES needs matrices P U and translation V = see writeup
$!    Keep P as the identity... 
$!    U  = R but must be input as the  transpose of R . 
$!     ( Remember: Gerard reads columns across the page!!!!)
$!    V = t.

$!    It is possible to understand why if you read Gerard's
$!    write up carefully.
$!    If you have a non orthogonal cell there will be more problems..

 
$!  SKEW PROCEDURE  _ I always work in P1 - it is a lot quicker..
$!  First use extend to extend map to whole unit cell and
$!  change SG number to 1 .

$!goto skew
$ass sys$input data
$ass sys$output printer
$ass ylib:symop.lib symop
$ass ds:[dbw2]solv55.map mapIN
$ass dsscr:protein_p1_1.map mapout
$run xtals3:extend
xyzlim 0 95 0 95 0 127
newspg 1
end

$!	This the SKEW COM file

$skew:

$ass dsscr:protein_p1_1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:chm_AtoB_skew.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dsscr:protein_p1_1.map -
MAPSKEW dsscr:chm_AtoB_skew2.map -
SCRATCH dsscr:
$DATA
0
1,1
0.9406 0.9406 1.0141          ! Dx,Dy,Dz
0 95   0 95      -30 30       !   gridlimits for molecule A
0.0,0.0,0.0
1.0   0   0                       
0    1.0  0               
0    0   1.0                       
1
          -0.42787 -0.63720 -0.64102
           0.11568  0.66478 -0.73803
           0.89641 -0.38993 -0.21073
   38.80169  40.65714  63.89231
3,2,1
TEST ON SKEW FOR CHMI
20
$START SAVE


$!   Here is the procedure for AVERAGING the 3 molecules...

$!

$skew:

$ass dscr:protein_p1_1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:chm_ctoa_skew.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dscr:protein_p1_1.map -
MAPSKEW dsscr:chm_abctoa_skew.map -
SCRATCH dsscr:
$DATA
0
1,1
0.9406 0.9406 1.0141          ! Dx,Dy,Dz
0 50   51 110      -30 30       !   gridlimits for molecule A
0.0,0.0,0.0
1.0   0   0                       
0    1.0  0               
0    0   1.0                       
3
          -0.47914  0.08719  0.8734
          -0.64221  0.64347 -0.41655     A to B rotation
          -0.59833 -0.76049 -0.25232     (transposed from LSQKAB output)
   85.08172  19.34877  -3.69910          A to B translation
          -0.42787 -0.63720 -0.64102
           0.11568  0.66478 -0.73803     A to C rotation
           0.89641 -0.38993 -0.21073     (transposed from LSQKAB output)
   38.80169  40.65714  63.89231          A to C translation
1.0   0   0                       
0    1.0  0               
0    0   1.0                             A to A rotation
0 0 0                                    A to A translation
3,2,1
TEST ON SKEW FOR CHMI  A B and C averaged.
20
$START SAVE




       Information obtained from:

            lsq_chm.com    ( gives R and V)

$set verify
$ass sys$output printer
$ass sys$input data
$ass dscr:chmi_sept18.pdb workcd
$ass dscr:chmi_sept18.pdb refrcd

$ RUN xtals3:lsqkab
TITL   ttttt
output  rms 
fit   WRES ALL 1 TO 127  WCHAIN A
match RRES ALL 1 TO 127  RCHAIN C
end
c   Result:
     ROTATION MATRIX:
          -0.47914 -0.64221 -0.59833
           0.08719  0.64347 -0.76049
           0.87340 -0.41655 -0.25232
 TRANSLATION VECTOR IN AS   85.08172  19.34877  -3.69910


$ass dscr:chmi_sept18.pdb workcd
$ass dscr:chmi_sept18.pdb refrcd

$ RUN xtals3:lsqkab
TITL   ttttt
output  rms 
fit   WRES ALL 1 TO 127  WCHAIN A
match RRES ALL 1 TO 127  RCHAIN B
end

c   Result:
     ROTATION MATRIX:
          -0.42787  0.11568  0.89641
          -0.63720  0.66478 -0.38993
          -0.64102 -0.73803 -0.21073
 TRANSLATION VECTOR IN AS   38.80169  40.65714  63.89231
$stop


   MINLIM:   Gives grid limits for molecule A

$ass dscr:chmi_sept18_mola.pdb xyzin     !  PDB file containing 
                                         !  molecule A coordinates. 
                                          
$run XTALS3:minlim
a  b  c     nx ny nz
0
0
0
0
   This gives limits of molecule in fractions of cell edge, grid points 
                                    and As.





  2)           MONOCLINIC

    skldh15.com   - monoclinic example

$ass DiSK$scratch:[dbw2]ldh_2_5a_p1.MAP mapin
$ass Dsscr:bsort.tmp bsort
$ass Disk$daily:[chem.chem1]ldh_2_5a_p1_15b.MAP mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN DiSK$scratch:[dbw2]ldh_2_5a_p1.MAP -
MAPSKEW DiSK$daily:[chem.chem1]ldh_2_5a_p1_15b.MAP -
SCRATCH DiSK$daily:[chem.chem1]
$data
0
1,1                         !  space group 1
0.9648 0.9850 0.99074       !  84.9/88 118.2/120 135.5*cos(6.07)/136
                            !  Grid point seperation along the 
                            !       ORTHOGONAL axes in As 
                            !  a/nx   b/ny  c*sin(beta)/nz
-13 45 -35 30 -28 25        !  Grid limits for first molecule  in 
                            !   original (and final) map grid
0.0,0.0,0.0                 !   original (and final) map origin
   1 0 0
   0 1 0                    !   defines orthogonal axes - always identity
   0 0 1                    !   - don't change!!!!!
1
  -0.849   -0.312    0.422
   0.024    0.775    0.632
  -0.438    0.579   -0.695

Note:    This matrix  equals
 ie:   R(AtoB) * "Stretching" matrix  (all transposed) 
                      equals
[1.0  0  0       ]         [  -0.849   -0.312    0.422
[0  1.0  0       ]     *   [   0.024    0.775    0.632
[-0.10634  0  1.0]         [  -0.528    0.546   -0.650
   
( "Stretching" matrix(transpose) * R(AtoB) (transpose) obtained from LSQ
                                  by fitting molecule B to molecule A
   The stretching matrix is  1  0  cot(beta)
                             0  1    0
                             0  0    1
   This is generally true for monoclinic spacegroups WITH Y SECTIONS
                                                     IN THE MAPS.)
                         Do NOT change the section output flags below
                          without modifying the "stretching" matrix.
                         In fact DO NOT CHANGE anything!!!!

   95.87763 72.91116 50.26078  T(AtoB)               obtained from LSQ
                                 fitting molecule B to molecule A
2,3,1                             !  Standard section output
 Try to rotate LDH - molecule 5   on 1.  new procedure
20
FORTRAN STOP
$START SAVE



  3)           Trigonal

$set noverify
$ASS mscr:ZN2tst.MAP MAPIN
$ass Dsscr:bsort.tmp bsort
$ASS mscr:ZN2tst_skew.MAP MAPout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN mscr:ZN2tst.MAP -
MAPSKEW  dscr:ZN2tst_skew.MAP -
SCRATCH dsscr:
$DATA
0
1,1                           !  space group 1
0.49107 0.42528 0.47222       !  82.5/158 82.5*sin(120)/168 134.0/78
                              !  Grid point seperation along the 
                              !       ORTHOGONAL axes in As 
                              !  a/nx   b*sin(gamma)/ny  c/nz

-43,28,-5,54,0,5              !  Grid limits for A molecule  in 
                              !   original (and final) map grid

0.0,0.0,0.0                   !   original (and final) map origin

   1 0 0                      !   Matrix P
   0 1 0                      !   defines orthogonal axes - always identity
   0 0 1                      !   - don't change!!!!!
1

  -0.882   -0.468    0.055    !  Gerards matrix U * streching matrix
   0.043    1.154    0.008
  -0.067    0.009   -0.998

Note:    This matrix  equals
 ie:   R(AtoB) * "Stretching" matrix  (all transposed) 
                      equals
( "Stretching" matrix(transpose) * R(AtoB) (transpose) obtained from LSQ
                                  by fitting molecule B to molecule A
                      equals
[ 1        0   0]      [-0.88193 -0.46658 -0.06713    
[-0.5774   1   0]  *   [-0.46816  0.88360  0.00915      
[ 0        0   1]      [ 0.05504  0.03950 -0.99770      

   The stretching matrix is  1 cot(gamma) 0
                             0     1      0
                             0     0      1
   This is generally true for trigonal spacegroups with z sections
                                                     in the maps.)

0.72864,0.47259,1.19243         !   Gerards vector V
                                !   = T(AtoB) obtained from LSQ  by
                                ! fitting molecule B to molecule A
3,2,1
TEST ON SKEW FOR TWO ZINC INSULIN
20
$START SAVE


   LSQKAB and MINLIM were used to get parameters.





4)    C2 molecules.

$!   Skewing 4 molecules in a C2 cell.

$!  First use extend to change SG number to 1 on map
$ass sys$input data
$ass sys$output printer
$ass ylib:symop.lib symop

$goto skew

$ass dscr:sp400_2_1.map mapIN  !map to be skewed
$ass dscr:sp400_p1.map mapout  !P1 map covering whole cell
$run xtals3:extend
xyzlim 0 119  0 119  0 79
newspg 1
end

$!	This the SKEW COM file  rotating all molecules seperately.

$!   The first run is simply to check we are mapping A onto A 
$!             without changing the grid or mucking anything up!!

$skew1:
$set verify
$ass sys$input data
$ass sys$output printer
$ass dscr:sp400_p1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:sp400_AtoA.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dscr:sp400_p1.map -
MAPSKEW dsscr:sp400_AtoA.map -
SCRATCH dsscr:
$DATA
0                              ! background flag
1,1                            ! mode, spacegroup
0.958 0.987 1.019              ! a/120 b/120 c * sin(92.47)/80 grid in As
47 104  -26 27  45 89          ! gridlimits for molecule A
0.0,0.0,0.0                    ! origin of coordinates
1 0 0
0 1 0
0 0 1
1 
 1.0       0.0   0.0  
 0.0       1.0   0.0  
-0.043136  0.0   1.0  
0 0 0
2,3,1                 ! sectioning flags
TEST ON SKEW FOR sp400
20
$START SAVE


$skew2:
$set verify
$ass sys$input data
$ass sys$output printer
$ass dscr:sp400_p1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:sp400_AtoB.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dscr:sp400_p1.map -
MAPSKEW dsscr:sp400_AtoB.map -
SCRATCH dsscr:
$DATA
0                              ! background flag
1,1                            ! mode, spacegroup
0.958 0.987 1.0177             ! a/120 b/120 c * sin(92.47)/80 grid in As
47 104  -26 27  45 89          ! gridlimits for molecule A
0.0,0.0,0.0                    ! origin of coordinates
1 0 0
0 1 0
0 0 1
1                 
   0.760   -0.464   -0.455
   0.537    0.053    0.842
  -0.399   -0.864    0.309
   33.82800  72.93736  31.74081
2,3,1                 ! sectioning flags
TEST ON SKEW FOR sp400
20
$START SAVE


$skew3:
$set verify
$ass sys$input data
$ass sys$output printer
$ass dscr:sp400_p1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:sp400_CtoA.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dscr:sp400_p1.map -
MAPSKEW dsscr:sp400_CtoA.map -
SCRATCH dsscr:
$DATA
0                              ! background flag
1,1                            ! mode, spacegroup
0.958 0.987 1.019              ! a/120 b/120 c * sin(92.47)/80 grid in As
47 104  -26 27  45 89          ! gridlimits for molecule A
0.0,0.0,0.0                    ! origin of coordinates
1 0 0
0 1 0
0 0 1
1                 
   0.719    0.421   -0.553
  -0.595   -0.037   -0.802
  -0.390    0.888    0.248
  34.40696 -12.16524  78.06890
2,3,1                 ! sectioning flags
TEST ON SKEW FOR sp400
20
$START SAVE


$skew4:
$set verify
$ass sys$input data
$ass sys$output printer
$ass dscr:sp400_p1.map mapIN
$ass dsscr:bsort.tmp bsort
$ass dsscr:sp400_DtoA.map mapout
$@dc:[chem3.public.xtal.skew]SKWPLANES 1 -
MAPIN dscr:sp400_p1.map -
MAPSKEW dsscr:sp400_DtoA.map -
SCRATCH dsscr:
$DATA
0                              ! background flag
1,1                            ! mode, spacegroup
0.958 0.987 1.019              ! a/120 b/120 c * sin(92.47)/80 grid in As
47 104  -26 27  45 89          ! gridlimits for molecule A
0.0,0.0,0.0                    ! origin of coordinates
1 0 0
0 1 0
0 0 1
1                 
   0.438    0.073   -0.896
   0.088   -0.995   -0.038
  -0.914   -0.066   -0.404
  14.76543  54.50638  66.30728
2,3,1                 ! sectioning flags
TEST ON SKEW FOR sp400
20
$START SAVE



             Another sort of problem: 

            Fitting a bit of map over a rotated Haem:

   Paul Emsley found a nice view in FRODO for his haem, and recorded the 
   VIEW matrix for this.
    VIEW   v11 v12 v13  v21 v22 v23  v31 v32 v33
 -0.788 -0.0669 0.61166 -0.3501  0.8662 -0.35655 -0.506 -0.495 -0.7062
    This can be used in SKEWPLANES to give the required map by
     setting the rotation matrix =  v11 v12 v13
                                    v21 v22 v23
                                    v31 v32 v33  
           and the translation vector = 0.0 0.0 0.0
         The limits are given by MINLIM for the rotated atoms
         ( Rotate them by using LSQKAB as shown)

   lsqkab.com

rm $output
px lsqkab WORKCD aheam.pdb \  ( these are taken from the ACTUAL coordinates)
LSQOP skew_a1.pdb << 'END'
TITLE    MATCH Hb O2 Boaz to mine
OUTPUT XYZ 
ROTA MATR -0.788 -0.0669 0.61166 -0.3501  0.8662 -0.35655 -0.506 -0.495 -0.7062
END
'END'
           skew_a1.com
/bin/rm *input
/bin/rm *keys
px makedata  					\
	MAPIN ~/scr/2fofcdox23.ext		\
     	<< 'EOF_makedat'
0
1 1
0.401041666 0.408333 0.54883
-26 13 -11 31 -62 39
0.0 0.0 0.0
1.0 0.0 0.0
0.0 1.0 0.0
0.0 0.0 1.0
1
-0.78829 -0.06687  0.61166  
-0.35013  0.86619 -0.35655   
-0.50597 -0.49523 -0.70622
 0.0 0.0 0.0
3 2 1
 alpha 1 Hb haem  skew for nice map.
20
'EOF_makedat'
#
csh {$CXTAL}skewpro.com 1 			\
	MAPIN    ~/scr/2fofcdox23.ext   	\
	MAPSKEW	 ~/scr/2fofcdox23skewa1.map


         minlim.com
px minlim XYZIN skew_a1.pdb << !
96.25000  98.000 65.86000  240  240 120  ! a b c   nx ny nz
0
!