STNET (CCP4: Supported Program)
                                       
NAME

   stnet - Generate stereographic net plot for use with polarrfn
   
SYNOPSIS

   stnet plot file.plo
   
DESCRIPTION

   The PLOT84 plot file on logical name PLOT is a stereographic net
   intended to be printed on a transparency for overlaying on the
   stereographic projection plots produced by polarrfn. A stereographic
   net is used to measure the angle (shortest distance on the surface of
   a sphere) between any pair of points on a stereographic projection.
   (To measure the angular co-ordinates of a point, see STGRID.) Each
   point on the projection corresponds to a point in polar angle space,
   which represents an orientation of a rotated Patterson function. Hence
   this gives the angle of rotation relating any pair of orientations.
   For example, it could be used to identify the 90o rotations relating
   any pair on monomers in a tetramer with non-crystallographic
   point-group symmetry 222.
   
   The angle must be measured along any one of the great circles
   (projected lines of longitude connecting opposite poles - note that
   the sphere is projected so that the poles are at the left- and
   right-hand edges and the equator runs vertically!). The other set of
   lines (projected lines of latitude parallel to the equator) sub-divide
   the great circles and are calibrated in degrees to allow the angle to
   be read off.
   
   Note that the net used must have exactly the same diameter as the
   plot, otherwise the results will not be accurate.
   
   The plot file may be converted to PostScript or HPGL for printing
   (resetting line width) with pltdev:
   pltdev -i file.plo -lnw .2

   Print the PostScript file plot84.ps on your laser printer and
   photocopy the stereographic net onto a transparent sheet.
   
BUGS

   The diameter shown in the title (currently 17.1cm) assumes you are
   using size A4 paper. If not, the diameter should still come out the
   same as your plots from Polarrfn. Just edit the title in the call to
   PLTCTX and recompile. However if you want to make a net with a
   specific diameter, you'll have to unravel the mysteries of PLOT84
   yourself - it probably involves fiddling with the window parameters
   (see DATA statement for array W in the source).
   
SEE ALSO

   stgrid, pltdev, plot84, polarrfn, rfcorr
   
AUTHOR

   Ian Tickle