SYMLIB (CCP4: Library)
                                       
NAME

   symlib - Subroutine Library for handling symmetry operations
   
DESCRIPTION

   The library symlib contains subroutines used for handling symmetry
   operations and performing symmetry related tasks in CCP4 programs,
   although a number of routines unconnected with symmetry operations
   also appear here, presumably for historical reasons.
   
   The subroutines have been arranged as much as possible into groups by
   function. There are often several versions of subroutines apparently
   performing the same or very similar tasks, reflecting the policy of
   never removing an existing routine in order to maintain compatibility
   with programs written using older versions of the library.
   
CONTENTS

    1. DESCRIPTION OF THE SYMMETRY LIBRARY
    2. HOW SYMMETRY OPERATIONS ARE STORED AND APPLIED
    3. DESCRIPTION OF THE GROUPS OF SUBROUTINES
         1. Deriving and manipulating symmetry operations
               o 1.a. Deriving symmetry operator matrices
               o 1.b. Deriving information from symmetry operators
         2. Testing reflection data
               o 2.a. Centric reflections
               o 2.b. Epsilon zones
         3. Choosing asymmetric units
               o 3.a. Choosing asymmetric units for reflection data
               o 3.b. Choosing asymmetric units in real space consistent
                 with FFT expectations
         4. Testing coordinate data
         5. Permuting symmetry operators
         6. Generating and accessing a hash table
         7. Miscellaneous subroutines
    4. SUBROUTINES IN SYMLIB (arranged alphabetically)
    5. DEFINITION OF THE CCP4 ASYMMETRIC UNIT
          + a. Reciprocal space
          + b. Real space
       
1. DESCRIPTION OF THE SYMMETRY LIBRARY

   In CCP4 the information relating together information such as
   spacegroup name, number and symmetry opertions are stored in a library
   file which is defined by the logical name $SYMOP. In the standard
   configuration of CCP4 this is the file symop.lib which normally
   resides in $CLIBD.
   
   symop.lib holds information for all the standard spacegroups in the
   International Tables, plus alternative settings for monoclinic and
   some nonstandard spacegroups (eg I2, I21 ...); R3, H3 and so on.
   
  Format of the symmetry library file
  
   Each spacegroup has an entry consisting of a header line followed by a
   list of symmetry operators. The header line contains the following
   items:
LSPGRP   NLINS   NLINP   NAMSPG  NAMPG   CRYSTAL  NAMSPG_CIF

   where:
          LSPGRP - spacegroup number
          NLINS - total number of lines of symmetry operators
          NLINP - number of lines of primitive symmetry operators
          NAMSPG - spacegroup name
          NAMPG - corresponding pointgroup name
          CRYSTAL - crystal class
          NAMSPG_CIF - string containing one or more recognised names for
          the spacegroup
          
   The subroutine MSYMLB3 should be used to retrieve information from the
   symmetry library. Note that not all the data items are compulsory for
   MSYMLB3, although older versions of the routine (MSYMLB2, MSYMLB,
   MSYGET) still need them.
   
   The unused items are:
          NLINP - the number of primitive symmetry operators
          NAMPG - pointgroup name
          
   MSYMLB3 uses the subroutine PGDEFN to obtain these directly.
   
   The symmetry operations in the spacegroup then follows the header
   line, with one operation per line in the format eg X,Y,Z or
   -Y,X-Y,Z+1/3 etc
   
   For example:
1 1 1 P1 PG1 TRICLINIC 'P 1'
 X,Y,Z
2 2 2 P-1 PG1bar TRICLINIC 'P -1'
 X,Y,Z
 -X,-Y,-Z
3 2 2 P2 PG2 MONOCLINIC 'P 1 2 1'
 X,Y,Z
 -X,Y,-Z
4 2 2 P21 PG2 MONOCLINIC 'P 1 21 1'
 X,Y,Z
 -X,Y+1/2,-Z
...
57 8 8 Pbcm PGmmm ORTHORHOMBIC 'P 2/b 21/c 21/m' 'P b c m'
 X,Y,Z
 -X,-Y,1/2+Z
 -X,1/2+Y,1/2-Z
 X,1/2-Y,-Z
 -X,-Y,-Z
 X,Y,1/2-Z
 X,1/2-Y,1/2+Z
 -X,1/2+Y,Z
...

   The spacegroup numbers are unique, so alternative numbers are
   generated by adding 1000, 2000 etc to the original spacegroup number.
   
2. HOW SYMMETRY OPERATIONS ARE STORED AND APPLIED

  Storage of symmetry operations
  
   In symop.lib the symmetry operations in each spacegroup are listed as
   strings, for example X,Y,Z or -Y,X-Y,Z+1/3 etc. To be useful within a
   program these string representations have to be converted to some
   mathematical representation.
   
   Typically a symmetry operation RSym will consist of a rotation
   operation R and a translation operation T (basically a vector). These
   are applied to a vector x to obtain x':
   
                                x' = Rx + T
                                      
   It is convenient to represent the rotation by a 3*3 matrix:
            ( R11  R12  R13 )
      [R] = ( R21  R22  R23 )
            ( R31  R32  R33 )

   and the translation by a column vector with 3 elements:
            ( T1 )
      [T] = ( T2 )
            ( T3 ).

   CCP4 uses 4x4 arrays to store these symmetry operations as follows:
      RSym = ( R11  R12  R13  T1 )
             ( R21  R22  R23  T2 )
             ( R31  R32  R33  T3 )
             (  0    0    0   1  )

   or
      RSym = (    [R]    | [T] )
             (  0  0  0  |  1  )

   Essentially this is a 4x4 matrix holding 3x3 transformation matrix in
   the "top-left-hand corner", the 3-element column (translation) vector
   in the "top-right-hand corner", and then (0 0 0 1) in the bottom row.
   
   The subroutine MSYMLB3 will obtain the set of symmetry matrices in
   this representation for a given spacegroup, whilst SYMFR2 or SYMFR3
   will obtain individual matrices from the string representation
   mentioned above. (SYMTR4 will perform the inverse operation,
   converting matrices to string representation.)
   
  Application of symmetry operations
  
    1. Real Space Coordinates
    
   Using the convention outlined above, post-multiplying the 4x4 matrix
   by a column vector as follows:
     RSym . [xf]
            [yf]
            [zf]
            [1 ]

   will apply both the symmetry and the translation operations to real
   space coordinates with a single matrix multiplication. The CCP4 MODLIB
   library provides matrix-vector routines MATVEC4 and TRANSFRM which can
   be used to perform this operation.
   
    2. Reciprocal Space
    
   The inverse of real-space symmetry matrices are applied to reflection
   indices by pre-multiplying them by a row vector representing hkl,
   
                               ie. h' = h R-1
                                      
   or,
   
                          (h' k' l') = (h k l) R-1
                                      
   Note that only the operations in the appropriate Laue group are
   applied to reflection indices, so there are no translational
   components (i.e. the vector part of the operation, [T], is zero). The
   subroutine INVSYM will invert a 4x4 matrix stored in this
   representation, for the purpose of applying symmetry operations to
   reflection indices.
   
    3. Axis Vectors
    
   Real space axis vectors are transformed like reciprocal space vectors,
   i.e.
   
                          (a' b' c') = (a b c) R-1
                                      
   while reciprocal space axis vectors are transformed like real space
   coordinates, i.e.
   
                        (a*' b*' c*') = R (a* b* c*)
                                      
   (See also the REINDEX documentation.)
   
3. DESCRIPTION OF THE GROUPS OF SUBROUTINES

   The subroutines have been broken down into groups according to
   function.
   
  Group 1: Subroutines for deriving and manipulating symmetry operations
  
   This group contains routines for obtaining the lists of symmetry
   operators from the library, and converting between the string (eg
   Y,X,-Z etc) and matrix representations of symmetry operators.
   
  Group 1a: Deriving symmetry operator matrices
  
   MSYMLB3
          Gets the symmetry operators in matrix representation for a
          specified spacegroup from the symmetry library. Will match to
          any valid s/g name but always returns the longest name, and
          will match to the spacegroup number if no name matches. Always
          uses the s/r PGDEFN to guess the point group and the number of
          primitive symmetry operations (so that any listed in the
          library are automatically ignored). Checks that the symmetry
          operations form a closed set.
          Replaces: MSYMLB2, MSYMLB, MSYGET
          
   SYMFR2, SYMFR3
          Translates a character string containing symmetry operator(s)
          into matrix represenation, stored in a 4*4 matrix/array.
          NB: SYMFR2 will translate real space coordinate operations
          (e.g. x+z,z,-y), reciprocal space operations (e.g. h,l-h,-k)
          and reciprocal- and real-space axis vector operations (e.g.
          a*+c*,c*,-b* and a,c-a,-b respectively). SYMFR3 only translates
          real space coordinate operations.
          
   SYMTR4
          Translates symmetry matrices into character strings with the
          equivalent symmetry operations.
          Replaces: SYMTRN, SYMTR3
          
   INVSYM
          Invert the 4*4 array holding the symmetry matrices, to get the
          inverse symmetry operation.
          
   Use MSYMLB3 to obtain the set of symmetry operator matrices given the
   spacegroup name or number. SYMFR2/3 will generate individual symmetry
   operator matrices from their string representation (useful if the
   operators are a subset of a spacegroup). SYMTR4 performs the opposite
   action, and generates string representations of individual symmetry
   operations from the matrices.
   
   INVSYM will generate the inverse matrix of a real space symmetry
   operation, to be applied to reflection indices as described in section
   2.
   
    Internal routines:
    
   DETERM
          Calculate the determinant of 4*4 matrix.
          
  Group 1b: Deriving information from symmetry operators
  
   PGDEFN
          Obtain/guess pointgroup and primitive set of symmetry operators
          from analysis of all symmetry operators.
          
   PGMDF
          Gronigen subroutine: determine the nature of the rotation and
          screw axes from the symmetry matrices.
          
   PGNLAU
          Determine the Laue group from pointgroup name.
          
   PATSGP
          Determine the Patterson spacegroup from true spacegroup.
          
   HKLRANGE
          Return HKL ranges chosen in PGNLAU
          
   These routines all derive additional information from the symmetry
   operators or the spacegroup name. The subroutine HKLRANGE returns the
   information stored in the common block which it shares with PGNLAU
   
  Group 2: Subroutines for testing reflection data
  
  a) Centric reflections
  
   CENTRIC
          Sets up symmetry elements; must be called first.
          
   CENTR
          Tests if a reflection is centric
          
   Nb: routines CENTRC and CENPHS both appear to be unused.
   
   Call CENTRIC once to set up the symmetry elements in common blocks
   shared with CENTR. This defines the set of centric reflections. Then
   for each reflection, a call to CENTR will return whether it is
   centric.
   
  b) Epsilon zones
  
   EPSLN
          Sets up tables of epsilon zones; must be called first.
          
   EPSLON
          Returns the epsilon zone of a given reflection, as well as
          whether the reflection is systematically absent (using a call
          to SYSAB).
          
   SYSAB
          Function: determines if a reflection is systematically absent.
          
   Call EPSLN once to generate the epsilon zones (general sets of
   reflections eg 00l or 0k0) and determine the multiplicity/fold. For
   each reflection a call to EPSLON returns the zone and if the
   reflection is systematically absent. SYSAB is not called directly.
   
   HKLEQ - used in SCALA to test if two reflections have equal indices.
   
  Group 3: Subroutines for choosing asymmetric units
  
   Remember that the choice of asymmetric unit is NOT UNIQUE. These
   routines define the set of CCP4 asymmetric units. The limits for these
   definitions are given in section 3.
   
  a) Subroutines for choosing asymmetric units for reflection data
  
   ASUSET
          Set up symmetry for ASUPUT and ASUGET; must be called first.
          Calls PRTRSM.
          
   ASUPUT
          Put reflection into asymmetric unit defined in ASUSET (reverse
          operation of ASUGET). Calls INASU.
          
   ASUGET
          Recover original indices of a reflection in the asymmetric unit
          defined in ASUSET (reverse opertaion of ASUPUT).
          
   ASUPHP
          Change phase for symmetry related reflection.
          
   Call ASUSET first to set up symmetry operations in common blocks
   shared with the other routines. For each reflection calls can then be
   made to ASUPUT (return the unique hkl indices in the asymmetric unit
   and symmetry number) or ASUGET (obtain real space indices given unique
   hkl's and symmetry number). INASU will determine whether a given
   reflection lies in the asymmetric unit and ASUPHP will convert the
   phase.
   
    Internal routines:
    
   INASU
          Funtion: test if reflection is in the asymmetric unit defined
          by ASUSET.
          
   PRTRSM
          Print reciprocal space symmetry operations.
          
   Both these routines are called from within other routines, although
   they can also be called independently. ASUSET must be called before
   INASU can be used.
   
  b) Subroutines for choosing asymmetric units in real space consistent with
  FFT expectations; FFT grids etc.
  
   SETLIM
          Set the appropriate box (=asymmetric unit) for the true
          spacegroup (ie not the FFT spacegroup). For cubic symmetry
          spacegroups, this will be more than one asymmetric unit.
          
   SETGRD
          Set up a suitable sampling grid for FFT. Calls FNSMP.
          
    Internal routines:
    
   FACTRZ
          Function: returns TRUE if N has all prime factors < 19.
          
   FNDSMP
          Find suitable grid sample.
          
  Group 4: Subroutines for testing coordinate data
  
   CALC_ORIG_PS
          Creates a list of equivalent origins for a given spacegroup
          
   XSPECIALS
          Finds which coordinates occupy special positions (i.e. have
          occupancies less than 1.0) from consideration of the symmetry
          operations.
          
   KROT
          Function: apply symmetry operation to coordinate triplet and
          check if the result lies in the asymmetric unit.
          
   Neither of the routines XSPECIALS or KROT appear to be used in
   supported CCP4 programs.
   
  Group 5: Subroutines for permuting symmetry operators
  
   Three subroutines for permuting symmetry operations. They do not
   really belong here in symlib, but are widely used invisibly in FFT
   routines using symmetry operations to permute axes for easier fast
   fourier calculations.
   
   PRMVCI
          Permutes specified column of an integer input matrix using
          another matrix.
          
   PRMVCR
          Equivalent to PRMVCI but operates on a real input matrix.
          
   ROTFIX
          Permutes inverse symmetry operations.
          
  Group 6: Subroutines for generating and accessing a hash table
  
   A set of routines used in SCALA, POSTREF and REBATCH.
   
   CCP4_HASH_SETUP
          Places a value in the internal look-up table.
          
   CCP4_HASH_LOOKUP
          Access a value stored in the table.
          
   CCP4_HASH_ZEROIT
          Initialise contents of the table to zero.
          
   These routines are not directly related to symmetry operations.
   Hashing is a method of storing data value pairs in such a way that
   they can be be efficiently retreived later on; the hash table is the
   resulting data structure.
   
  Group 7: Miscellaneous subroutines
  
   SETRSL
          Routine to calculate set coefficients for calculation of
          (sin(theta)/lambda)**2, from cell dimensions and angles.
          
   STHLSQ
          Calculate (sin(theta)/lambda)**2 from h,k,l, using coefficients
          set by a call to SETRSL.
          
   STS3R4
          Calculate (sin(theta)/lambda)**2 from h,k,l, using coefficients
          set by a call to SETRSL. Duplicates STHLSQ exactly.
          
   These three routines share the common block RECPLT. SETRSL and STHLSQ
   are used only in CAD, whilst STS3R4 does not appear in any supported
   program.
   
   This is how the routines are used in CAD. A call to SETRSL with the
   cell dimensions and angles sets up coefficients in RECPLT, which are
   then used by the function STHLSQ to calculate the quantity
   "(sin(theta)/lamba)**2" for any given set of h, k, l indices. From
   Bragg's Law, this quantity is equal to 1/(4*d**2), that is,
   one-quarter of the resolution. Within CAD, multiplication by 4 yields
   the resolution 1/d**2.
   
   PSTOPH
          Phase angle conversion routine.
          
   The exact function of this routine is unclear and it does not appear
   in any supported program.
   
4. SUBROUTINES IN SYMLIB

   The following subroutines are available. They are arranged
   alphabetically.
   
Subroutine ASUGET(IHKL,JHKL,ISYM)

   Get original indices of reflection from asymmetric unit, i.e. reverse
   operation of ASUPUT. Symmetry defined by call to ASUSET.
   
   On input:
   
   IHKL(3)
          input unique indices hkl
          
   ISYM
          symmetry number for output
          odd numbers are for I+
          even numbers are for I-
          real-space symmetry operation number L = (ISYM-1)/2 + 1
          
   On output:
   
   JHKL(3)
          output original indices hkl
          
   The real-space symmetry matrices are applied in ASUPUT by
   premultiplying them by a row vector hkl, ie (h'k'l') = (hkl)R. So here
   we calculate (hkl) = (h'k'l') R**-1
   
Subroutine ASUPHP(JHKL,LSYM,ISIGN,PHASIN,PHSOUT)

   Generate phase of symmetry equivalent JHKL from that of IHKL.
   
   On input:
   
   JHKL(3)
          indices hkl generated in ASUPUT
          
   LSYM
          symmetry number for generating JHKL ( found by ASUPUT)
          
   ISIGN
          = 1 for I+
          = -1 for I-
          
   PHASIN
          phase for reflection IHKL(3)
          
   On output:
   
   PHSOUT
          phase for reflection JHKL(3)
          
Subroutine ASUPUT(IHKL,JHKL,ISYM)

   Put reflection into asymmetric unit defined by call to ASUSET
   
   On input:
   
   IHKL(3)
          input indices hkl
          
   On output:
   
   JHKL(3)
          output indices hkl
          
   ISYM
          symmetry number for output
          odd numbers are for I+
          even numbers are for I-
          real-space symmetry operation number L = (ISYM-1)/2 + 1
          
   The real-space symmetry matrices are applied by premultiplying them by
   a row vector hkl, ie (h'k'l') = (hkl)R
   
Subroutine ASUSET

   Set up & store symmetry informtion for later use in ASUPUT or ASUGET
   
   On input:
   
   SPGNAM
          space-group name (not used) ( character)
          
   NUMSGP
          space-group number (not used)
          
   PGNAME
          point-group name (if returned from SYMOP.LIB) ( character)
          
   MSYM
          total number of symmetry operations
          
   RRSYM(4,4,MSYM)
          symmetry matrices (real-space)
          
   LPRINT
          - printing flag. ( logical)
          
   On output:
   
   PGNAME
          point-group name ( character)
          
   MSYMP
          number of primitive symmetry operations
          
   MLAUE
          Laue group number - See PGNLAU for details
          
Subroutine
CALC_ORIG_PS(NAMSPG_CIF,NSYM,RSYM,NORIG,ORIG,LPAXISX,LPAXISY,LPAXISZ)

   Creates a list of equivalent origins for the named spacegroup.
   
   ARGUMENTS
   
   (I) NAMSPG_CIF
          spacegroup name (character)
          
   (I) NSYM
          number of symmetry operations
          
   (I) RSYM(4,4,NSYM)
          symmetry ops stored as 4x4 matrices
          
   (O) NORIG
          number of origins.
          
   (O) ORIG(3,i)
          vector of alternate origin (for example : 0.5,0.0,0.5) only
          positive components. include vector: (0,0,0)
          
   (O) LPAXISX
          logical; set true if s/grp is polar along x axis
          
   (O) LPAXISY
          logical; set true if s/grp is polar along y axis
          
   (O) LPAXISZ
          logical; set true if s/grp is polar along z axis
          
   Taken from Alexei Vagin
   
Integer Function CCP4_HASH_LOOKUP(NSER)

   The function CCP4_HASH_LOOKUP returns the value NFIND (which was input
   when setting up the function in the subroutine CCP4_HASH_SETUP) for
   the large range variable NSER. Uses hashing. (see comments for
   CCP4_HASH_SETUP for description of hashing method).
   
Subroutine CCP4_HASH_SETUP(NSER,NFIND)

   This subroutine sets up a value for the function ccp4_hash_lookup.
   
   When ccp4_hash_lookup(nser) is later evaluated it will return nfind
   
   This function will allow the efficient retrieval of an identifier for
   a large range variable (such as a crystal number). The values of the
   function ccp4_hash_lookup(nser) are stored in the array it(2, kpri)
   where kpri is the prime number used to generate the function.
   
   The array 'it' lives in the common block which is shared by
   ccp4_hash_setup and the function ccp4_hash_lookup
   
   NOTES: A hash table is a way of storing information so that it easily
   be retrieved without the need for indexing or long searches. NSER is
   referred to as the "key", which is "hashed" (computer- science speak
   for "messed up") by the hashing function (in this case MOD(NSER4,KPRI)
   + 1) to determine where the value pair will be stored. The function
   LOOKUP can then search on the same basis when supplied with the key,
   to retreive the pair in (at most) 3 calculations. Note that KPRI (the
   table size) MUST BE A PRIME in order for this method to work.
   
Subroutine CCP4_HASH_ZEROIT()

   Initialises elements of array 'it' used in ccp4_hash_setup and
   ccp4_hash_lookup to zero.
   
Subroutine CENTR(IH,IC)

   Input IH(3) - reflection indices
   
   Returns IC
   
   Determine whether a reflection is centric (return IC=1) or not (IC=0).
   If none of the zone tests is satisfied, the reflection is non-centric.
   
Logical Function CENTRC(KHKL,ICENT)

   Returns value as true if reflection khkl is centric, false otherwise.
   It is general for all point groups - but only for the unique set of
   indices which conforms to the criterion of maximising the value of
   
                   (khkl(3)*256 + khkl(2))*256 + khkl(1)
                                      
   as produced by e.g. subroutine turnip in protin and ulysses.
   
   In this case the required tests are controlled by 7 flags in icent for
   
                      0KL H0L HK0 HKK HKH HHL H,-2H,L
                                      
   (the last is needed in pg312)
   
Subroutine CENTRIC(NSM,RSMT,IPRINT)

   This is Randy Read's method of defining centric reflections. It uses
   NSM and the symmetry operators stored in RSMT(4,4,NSM)
   
   It decides how many centric zones there are, and flags them.
   
   set up tests for 0kl h0l hk0 hhl hkh hkk h,-hl hk-h hk-k -h 2h l 2h -h
   l hkl
   
   Zones are encoded using an idea from a program by Bricogne. If
   h*zone(1) + k*zone(2) + l*zone(3) is equal to 0.0, that reflection is
   in that zone. All that is needed is the most general conditions - a
   reflection is either centric or not.
   
Subroutine DETERM(det,a)

   Gets determinant of a matrix
   
   Input A
          4*4 matrix (real)
          
   Output DET
          determinant of A.
          
Subroutine EPSLN(NSM,NSMP,RSMT,IPRINT)

   It works out the epsilon cards using NSM and the symmetry operators
   stored in RSMT(4,4,NSM).
   
   This is Randys program description:
   
     zones defined as for centric zones, but fourth number on each line
     is the multiplicity corresponding to this zone. last card should
     always be 0 0 0 n, where n is appropriate for the lattice (1 for
     primitive, 2 for face- centred, etc.), so that general reflections
     get a value for epsilon. be very careful of the order of the zones.
     cards for reciprocal lattice rows should be given before those for
     planes, because the first test that is satisfied defines the zone.
     
     set up tests for
     h00 0k0 00l hh0 h0h 0kk h,-h0 h0-h 0k-k -h2h0 2h-h0 hhh hkl
     
Subroutine EPSLON(IH,EPSI,ISYSAB)

   Input IH(3) - reflection indices
   
   Returns EPSI ( epsilon zone) , and ISYSAB flag. Systematic absences
   flagged with ISYSAB = 1
   
   Find the zone a reflection falls into, and return the appropriate
   value for the reflection multiplicity factor. Each reflection must
   have a zone.
   
Logical Function FACTRZ(N)

   Returns true if N has all prime factors <= 19
   
Subroutine FNDSMP(MINSMP, NMUL, SAMPLE, NSAMPL)

   Find suitable grid sample, approximately = SAMPLE/2 * maximum index,
   with required factor, and no prime factor > 19
   
   On entry:
   
   MINSMP
          minimum sample, approximately 2 * maximum index
          
   NMUL
          required factor
          
   SAMPLE
          desired sample factor, ie if = 1.0 (minimum), try to get sample
          close to MINSMP
          
   On exit:
   
   nsampl
          grid sample; if MINSMP<=0, nsampl=nmul
          
Logical Function HKLEQ(IH,KH)

   Checks if indices are equal.
   
   Returns true if indices ih = kh
   
Subroutine HKLRANGE(IHRNG0,IKRNG1,IKRNG0,IKRNG1,ILRNG0,ILRNG1)

   Return HKL ranges chosen in PGNLAUE
   
   Arguments: (INTEGER) HRNG0,HRNG1,KRNG0,KRNG1,LRNG0,LRNG1
   
Integer Function INASU(IH, NLAUE)

   Arguments:
   
   NLAUE
          - code number for this pointgroup
          
   IH(3)
          - indices
          
   Returns:
   
   INASU = +1 if h k l chosen
   INASU = -1 if -h-k-l chosen
   INASU = 0 if reflection is out-of-bounds
   
Subroutine INVSYM(S,ST)

   Inverts a 4*4 matrix. Used here to get inverse symmetry operation for
   generating equivalent h k l, i.e.
   
                               [h'] = [h][St]
                                      
                    h'(j) =Sum(I=1,3)[ h(i)*St(I,J,NS)]
                                      
   Arguments:
   
   Input S
          4*4 matrix to be inverted
          
   Output ST
          4*4 matrix (inverse of S)
          
Integer Function KROT(NS)

   Apply NS'th symmetry operation to JP to get LP, check if lies in
   asymmetric unit given by NAU.
   
   Returns KROT=0 correct operation, =1 if not.
   
Subroutine MSYGET(IST,LSPGRP,NSYM,ROT)

   Get symmetry operations for space-group LSPGRP from library file on
   stream IST, logical name SYMOP.
   
   Arguments:
   
   LSPGRP (input)
          Name of spacegroup
          
   IST (input)
          Stream of library file
          
   NSYM (output)
          Number of symmetry operations
          
   ROT(4,4,NSYM) (output)
          Rotation/translation matrices
          
Subroutine MSYMLB(IST,LSPGRP,NAMSPG,NAMPG,NSYMP,NSYM,ROT)

   Get symmetry operations from library file on stream IST, logical name
   SYMOP. Space group defined by LSPGRP - spacegroup number or NAMSPG -
   spacegroup name.
   
   Arguments:
   
   LSPGRP (I/O)
          spacegroup number
          
   NAMSPG (I/O)
          spacegroup name
          
   NAMPG (O)
          pointgroup name
          
   NSYMP (O)
          number of primitive symmetry operations
          
   NSYM (O)
          number of symmetry operations
          
   ROT(4,4,NSYM)
          rotation/translation matrices
          
Subroutine MSYMLB2(IST,LSPGRP,NAMSPG_CIF,NAMPG,NSYMP,NSYM,ROT)

   Identical to MSYMLB, except that on output NAMSPG_CIF has correct CIF
   format, e.g. 'P 21 21 21'
   
   NAMSPG_CIF should be as in _symmetry.space_group_name_H-M
   
Subroutine
MSYMLB3(IST,LSPGRP,NAMSPG_CIF,NAMSPG_CIFS,NAMPG,NSYMP,NSYM,RlSymmMatrx)

   Another version of MSYMLB, with the following changes:
    1. The routine will try first to match the assigned NAMSPG_CIF to ANY
       name given on the spacegroup line:
       It is satisfied by the first fit it finds:
       eg: 47 8 8 Pmmm PGmmm ORTHORHOMBIC 'P 2/m 2/m 2/m' 'P m m m'
       You could call the subroutine with NAMSPG_CIF = 'Pmmm' or 'P 2/m
       2/m 2/m' or 'P m m m'
       But it will always return the LONGEST possible name. ie 'P 2/m 2/m
       2/m'
    2. If there is no match to the spacegroup NAME, the space group is
       identified by its number. This requires that the number is UNIQUE,
       so alternate settings are numbered n000 + Int Tab number
    3. The point group name is always guessed at by the SR PGDEFN and the
       guess on the data line is ignored.
    4. The number of primitive symmetry operators is also determined by
       the SR PGDEFN. The non-primitive operators are stored in the first
       NSYMP symmetry matrices and the guess on the data line is ignored.
    5. The symmetry operators are checked to make sure they are a closed
       group.
       
   In the library file, the header for each entry may contain (Order not
   guaranteed, but must start with)
   
   LSPGRP NLINS and contain either NAMSPG or NAMSPG_CIF
   
   LSPGRP NLINS NLINP NAMSPG NAMPG CRYSTAL NAMSPG_CIF
   
   where:
   
   LSPGRP
          spacegroup number
          
   NLINS
          total number of lines of symmetry operators.
          
   NLINP
          number of LINES of primitive symmetry operators (not used
          now..)
          
   NAMSPG_CIF
          spacegroup name (in CIF format? presumably)
          
   NAMPG
          name of corresponding pointgroup (not used now..)
          
   On entry:
   
   IST
          stream number to read file
          
   LSPGRP
          spacegroup number
          
   NAMSPG or NAMSPG_CIF
          any acceptable spacegroup name: this will be used to identify
          the spacegroup if possible
          
   Returns:
   
   LSPGRP
          spacegroup number
          
   NAMSPG_CIF
          full spacegroup name
          
   NAMSPG_CIFS
          name without any spaces
          
   NAMPG
          pointgroup name ( obtained from pgdefn - not 100% reliable!)
          
   NSYMP
          number of primitive symmetry operations obtained from pgdefn-
          only different from NSYM in non-primitive spacegroups
          
   NSYM
          total number of symmetry operations
          
   RlSymmMatrx(4,4,NSYM)
          Symmetry Rotation/translation matrices
          
Subroutine PATSGP(SPGNAM, PGNAME, PATNAM, LPATSG)

   Determine Patterson spacegroup from true space-group
   
   On entry:
   
   SPGNAM
          space-group name. Only used to determine lattice centering
          
   PGNAME
          point-group name
          
   On exit:
   
   PATNAM
          name of Patterson spacegroup
          
   LPATSG
          number of Patterson spacegroup
          
Subroutine PGDEFN(NAMPG,NSYMP,NSYM,RSYMT,LPRINT)

   Arguments:
   
   Input NSYM
          - number of symmetry operators. ( integer)
          
   Input RSYMT
          - 4*4 symmetry matrices. ( real)
          
   Input LPRINT
          - printing flag. ( logical)
          
   Returns NAMPG
          - name of point group. ( character)
          
   Returns NSYMP
          - number of primitive symmetry operators. ( integer)
          
   Returns RSYMT
          - possibly reordered.
          
   This subroutine chooses the primitive set of symmetry operators.
   
   If necessary it re-orders the symmetry operators to give the primitive
   ones first.
   
   This subroutine works out the point group name NAMPG. That is ; it
   checks rotation axes, etc etc and recognises these point groups. (It
   DOES NOT cope with mirror planes etc)
   
   Gronigen MDF stuff: It now sets up the common block MDFPAR for MDF
   file mods and fills in the symmetry info. See subroutine for details.
   
Subroutine PGMDF(JLASS,JCENTR,JSCREW)

   Gronigen subroutine.
   
   Use this subroutine to transfer information to and from MDFPAR.
   If JLASS eq 0 then fill JLASS JCENTR JSCREW from common block.
   If JLASS gt 0 then fill KLASS ICENTR ISCREW in common block.
   
Subroutine PGNLAU(NAMPG,NLAUE,LAUNAM)

   Choose Laue group from PG name.
   
   On entry:
   
   NAMPG
          point-group name ( character)
          
   On exit:
   
   NLAUE
          Laue group number ( integer)
          
   LAUNAM
          Laue group name ( character)
          
   This subroutine returns a laue code number used to choose the unique
   region of reciprocal space for each point group.
   
   The number nlaue is the same as the one set in CAD for this purpose.
Pointgroup Laue group        Limits

 3 pg1     1bar       hkl:l>=0  hk0:h>=0  0k0:k>=0   1,2
   pg1bar
 4 pg2 (b) 2/m        hkl:k>=0, l>=0  hk0:h>=0       3/b,4/b....
   pgm pg2/m
 5 pg2 (c) 2/m        hkl:k>=0, l>=0  h0l:h>=0       1003,1004
 6 pg222   mmm        hkl:h>=0, k>=0, l>=0            16 ...
   pgmm2 pgmmm
 7 pg4     4/m        hkl:h>=0, l>=0 with k>=0 if  h=0  and
   pg4bar pg4/m                            k>0 if h>0
 8 pg422   4/mmm       hkl:h>=0, k>=0, l>=0            89..
   pg4mm pg4bar2m pg4barm2 pg4/mmm
 9 pg3     3bar      hkl:h>=0, k>0  00l:l>0         143..
   pg3bar
10 pg312   3/m        hkl:h>=0, k>=0 with k<=h for all l.
   pg32 pg3m pg3m1 pg3barm1 if k = 0  l>=0
         Space group numbers :   149-151-153 157 159 162 163
11 pg321   3bar1m     hkl:h>=0, k>=0 with k<=h for all l.
   pg31m pg3bar1m      if h = k  l>=0
         Space group numbers :   150-152-154
12 pg6     6/m        hkl:h>=0, k>=0, l>=0 with k>=0 if  h=0
   pg6bar  6/m        and k> 0 if h>0
13 pg622   6/mmm       hkl:h>=0, k>=0, l>=0 with h>=k 177..
   pg6mm pg6barm2 pg6bar2m  pg 6/mmm
14 pg23    m3         hkl:h>=0, k>=0, l>=0 with l>=h,  k>=h
   pgm3bar
15 pg432   m3m        hkl:h>=0, k>=0, l>=0  with  k>=l
   pg4bar3m pgm3barm

Subroutine PRMVCI(PERM,JV,N,N1)

   Input PERM
          - 4*4 matrix (real)
          
   Input JV
          - N1*3 matrix (integer)
          
   Output JV
          - N1*3 matrix (integer)
          
          This has been modified by permuting the Nth column by matrix
          PERM.
          
   Here is the code for clarity:
C---- Permute
C
C     DO 10 I = 1,3
C       BV(I) = PERM(I,1)*JV(N,1) + PERM(I,2)*JV(N,2) +
C    +          PERM(I,3)*JV(N,3)
C  10 CONTINUE
C
C---- Copy back
C
C     DO 20 I = 1,3
C       JV(N,I) = NINT(BV(I))
C  20 CONTINUE

Subroutine PRMVCR(PERM,AV,N,N1)

   Input PERM
          - 4*4 matrix (real)
          
   Input AV
          - N1*3 matrix (real)
          
   Output AV
          - N1*3 matrix (real) This has been modified by permuting the
          Nth column by matrix PERM.
          
   See PRMVCI - this routine is its real equivalent.
   
Subroutine PRTRSM(PGNAME, NSYMP, RSYMIV)

   Print reciprocal space symmetry operations
   
   The real-space symmetry matrices are applied by premultiplying them by
   a row vector hkl, ie (h'k'l') = (hkl)R
   
Subroutine PSTOPH (PSIX,PSIY,PSIZ,PHIX,PHIY,PHIZ,AVPHI)

   Convert PSIX,PSIY,PSIZ (= epsx,epsy,epsz) to PHIX,PHIY,PHIZ, using
   AVPHI
   
   All angles in radians
   
Subroutine ROTFIX

   Permutes inverse symmetry operations
   
   Matrices passed in Common block ATSYM
   
Subroutine SETGRD(NLAUE,SAMPLE,NXMIN,NYMIN,NZMIN,NX,NY,NZ)

   Set up a suitable sampling grid for FFT
   
   Input:
   
   NLAUE
          Laue-group for FFT/SF calculation
          
   SAMPLE
          default fineness of sample, ie if = 1.0 (minimum), try to get
          sampling as close to minimum as possible.
          Typically = 1.5 to get sample at traditional 3 * maximum index
          
   NXMIN NYMIN NZMIN
          minimum sampling (true XYZ)
          
   Output:
   
   NX,NY,NZ
          sampling intervals along X,Y,Z
          
   The sampling intervals must satisfy the following conditions:
    1. approximately SAMPLE * minimum sampling
    2. no prime factor > 19
    3. special restrictions for particular space-groups
       
   This is ALL the point groups.
 PG1 PG1bar PG2 PGm PG2/m PG222 PGmm2 PGmmm
 PG4 PG4bar PG4/m PG422 PG4mm PG4bar2m PG4/mmm
 PG3 PG3bar PG32 PG3m PG3barm
 PG6 PG6bar PG6/m PG622 PG6mm PG6bar2m  PG6/mmm
 PG23 PGm/3bar PG432 PG4bar3m PGm3bar m

   We use:
 PG1 PG1bar PG2  PG2/m PG222  PGmmm
 PG4 PG4/m PG422 PG4/mmm
 PG3 PG3bar PG32 PG3bar/m
 PG6 PG6/m PG622 PG6/mmm
 PG23 PGm/3bar PG432 PGm3barm

   For grid restrictions we only need to know the laue number. Here is
   the table:
   3 pg1     1bar      hkl:l>=0  hk0:h>=0  0k0:k>=0   1,2
   4 pg2    2/m        hkl:k>=0, l>=0  hk0:h>=0       3/b,4/b....
   5 pg2(c) 2/m        hkl:k>=0, l>=0  h0l:h>=0       1003,1004
   6 pg222  mmm        hkl:h>=0, k>=0, l>=0            16 ...
   7 pg4    4/m        hkl:h>=0, l>=0 with k>=0 if  h=0  and
   8 pg422 4/mmm       hkl:h>=0, k>=0, l>=0            89..
   9 pg3     3bar      hkl:h>=0, k>0  00l:l>0         143..
  10 pg312  3/m        hkl:h>=0, k>=0 with k<=h for all l.
                           if k = 0  l>=0
           Space group numbers :   149-151-153
  11 pg321  3/m        hkl:h>=0, k>=0 with k<=h for all l.
                           if h = k  l>=0
           Space group numbers :   150-152-154
  12 pg6    6/m        hkl:h>=0, k>=0, l>=0 with k=0 if  h=0
  13 pg622  6/mmm
  14 pg23   m3
  15 pg432  m3m

Subroutine SETLIM(LSPGRP,XYZLIM)

   Set appropriate box (asymmetric unit) for spacegroup (true spacegroup
   rather than FFT spacegroup) LSPGRP. For cubic symmetry spacegroups,
   this will be more than one asymmetric unit.
   
   On entry:
   
   lspgrp
          true spacegroup (not FFT spacegroup)
          
   On exit:
   
   xyzlim(2,3)
          minimum, maximum limits on x,y,z (fractions of cell); if
          spacegroup not recognized, returns xzylim(1,1) = -1.0
          Note that the minimum limits (xyzlim(1,)) will always = 0.0
          
Subroutine SETRSL(A,B,C,ALPHA,BETA,GAMMA)

   Routine to calculate coefficients for (sin(theta)/lambda)**2 from
   h,k,l for general axes.
   
   First calculates the components of input axes in an orthonormal basis,
   then calculate components of reciprocal axes in same basis.
   
   The input angles are in degrees.
   
Real Function STHLSQ(IH,IK,IL)

   Calculate (sin(theta)/lambda)**2 from h,k,l. The coefficients are set
   by a previous call to SETRSL. Works for any kind of axes.
   
Real Function STS3R4(IH,IK,IL)

   Calculate (sin(theta)/lambda)**2 from h,k,l. The coefficients are set
   by a call to SETRSL. Works for any kind of axes.
   
Subroutine SYMFR2(ICOL,I1,NS,ROT)

   Read and interpret symmetry operations
   
   SYMFR2 recognises the following types of input:
     real space symmetry operations, e.g. X+1/2,Y-X,Z
     reciprocal space operations,    e.g. h,l-h,-k
     reciprocal axis vectors,        e.g. a*+c*,c*,-b*
     real space axis vectors,        e.g. a,c-a,-b

   The subroutine returns the appropriate 4x4 transformation matrix for
   each operation. The calling program must interpret the resulting
   matrix(ces) correctly.
   
   On entry I1 is the first character of ICOL to look at (say after
   keyword 'SYMM')
   
   NS is the number of the first symmetry operation to be read, & returns
   with the number of the last one read.
   
   On exit, ROT(4,4,NS) contains the real-space symmetry matrices, in
   standard convention, i.e.
   
                               [x'] = [s][x]
                                      
               x'(I)=Sum(J=1,3)ROT(I,J,NS)*x(J) + ROT(I,4,NS)
                                      
   Input:
   
   ICOL
          character string containing symmetry operations
          
   I1
          first character in ICOL to interpret from.
          
   Output:
   
   ROT(I,4,NS)
          contains the fractional translations.
          
Subroutine SYMFR3(ICOL,I1,NS,ROT,EFLAG)

   Read and interpret symmetry operations.
   
   Arguments:
   
   ICOL (I) CHARACTER*80
          Line containing the symmetry operations
          
   I1 (I) INTEGER
          First character to look at in ICOL (say after keyword 'SYM')
          
   NS (I/O) INTEGER
          is the number of the first symmetry operation to be read, &
          returns with the number of the last one read (ie you can have
          more than one on a line!)
          
   ROT (O) REAL
          Array (4,4,at_least_NS), on exit contains the real-space
          symmetry matrices, in standard convention, i.e.
          
                               [x'] = [s][x]
                                      
               x'(I)=Sum(J=1,3)ROT(I,J,NS)*x(J) + ROT(I,4,NS)
                                      
          ROT(I,4,NS) contains the fractional translations
          
   EFLAG (O) INTEGER
          Error flag - on exit, if 0 then OK, > 0, an error occurred.
          
Subroutine SYMTRN(NSM,RSM)

   Symmetry translation from matrix back to characters
   
   This translates the symmetry matrices RSM(4,4,NSM) into INT TAB
   character strings
   
   It gives the real and reciprocal space operations.
                eg     X,Y,Z        H  , K, L
                eg     -Y,X-Y, Z   -H-K, H, L  etc

   That is more complicated than you might think!!
   
Subroutine SYMTR3(NSM,RSM)

   Symmetry translation from matrix back to characters
   
   This translates the symmetry matrices RSM(4,4,NSM) into INT TAB
   character strings
   
   It gives the real and reciprocal space operations.
                eg     X,Y,Z        H  , K, L
                eg     -Y,X-Y, Z   -H-K, H, L  etc

   That is more complicated than you might think!!
   
   Arguments :
   
   NSM (I) INTEGER
          Number of Symmetry operations
          
   RSM (I) REAL
          Array of dimension (4,4,at least NSM) containing symmetry
          operations on input
          
   SYMCHS (O) CHARACTER*(*)
          Array of dimension at least NSM containing int tab char strings
          on output
          
   IPRINT (I) INTEGER
          Print flag
          =0 No printing
          =1 Print the int tab strings
          
Subroutine SYMTR4(NSYM,RSM,SYMCHS)

   Symmetry translation from matrix back to characters
   
   This translates the symmetry matrices RSM(4,4,NSM) into INT TAB
   character strings
   
   It gives the real and reciprocal space operations.
                eg     X,Y,Z        H  , K, L
                eg     -Y,X-Y, Z   -H-K, H, L  etc

   That is more complicated than you might think!!
   
   Arguments :
   
   Nsym (I) INTEGER
          Number of Symmetry operations
          
   Rsm (I) REAL
          Array of dimension (4,4,at least Nsym) containing symmetry
          operations on input
          
   Symchs (O) CHARACTER*(*)
          Array of dimension at least Nsym containing int tab char
          strings on output
          
Subroutine SYSAB(IN,ISYSAB)

   Input IN(3) - reflection indices
   
   Returns ISYSAB flag. Systematic absences flagged with ISYSAB = 1 Only
   reflns with EPSI > 1 need be considered.
   
Subroutine XSPECIALS(NSYM,RSYM,XF,YF,ZF,NSPEC)

   Input NSYM
          - number of symmetry operators. ( integer)
          
   Input RSYM
          - 4*4*NSYM symmetry matrices. ( real)
          
   Input XF YF ZF
          - a coordinate in fractional coordinates.
          
   Output NSPEC
          - the multiplicity of the coordinate. eg: NSPEC = 3 for an atom
          on a 3fod axis.
          
   This subroutine finds what coordinates occupy special positions i.e.
   have occupancies less than 1.0 from consideration of the symmetry
   operations.
   
5. DEFINITION OF THE CCP4 ASYMMETRIC UNIT

   There is no standard defined asymmetric unit so the definitions are
   arbitrary and may differ between differ packages. The subroutines in
   group 3.a are used to define the CCP4 asymmetric unit, and to
   determine whether a reflection falls within this definition.
   
   Below are the definitions of the reciprocal space and the real space
   asymmetric units under the CCP4 convention.
   
  a. Reciprocal Space Asymmetric Unit Definitions
  
   The reciprocal space asymmetric unit is defined in the subroutine
   ASUSET from the Laue group using calls to the s/r's PGDEFN and PGNLAU.
   The limits of the CCP4 asymmetric unit are (from PGNLAU):
   
   Pointgroup Laue group Limits Spacegroup Nos
   3 pg1
   pg1bar 1bar hkl:l>=0
   hk0:h>=0
   0k0:k>=0 1,2
   4 pg2 (b)
   pgm pg2/m 2/m hkl:k>=0, l>=0
   hk0:h>=0 3,4....
   5 pg2 (c) 2/m hkl:k>=0, l>=0
   h0l:h>=0 1003, 1004
   6 pg222
   pgmm2
   pgmmm mmm hkl:h>=0, k>=0, l>=0 16 ...
   7 pg4
   pg4bar
   pg4/m 4/m hkl:h>=0, l>=0 with k>=0 if h=0
   and k>0 if h>0 75,..
   8 pg422 pg4mm pg4bar2m
   pg4barm2 pg4/mm 4/mmm hkl:h>=0, k>=0, l>=0 89,..
   9 pg3
   pg3bar 3bar hkl:h>=0, k>0 00l:l>0 143,..
   10 pg312 pg32
   pg3m pg3m1 pg3barm1 3/m hkl:h>=0, k>=0 with k<=h for all l.
   if k=0 l>=0 149 151 153 157 159 162 163
   11 pg321 pg31m pg3bar1m 3bar1m hkl:h>=0, k>=0 with k<=h for all l.
   if k=h l>=0 150 152 154
   12 pg6 pg6bar 6/m hkl:h>=0, k>=0, l>=0 with k>=0 if h=0 and k>0 if h>0
   168..
   13 pg622 pg6mm pg6barm2 pg6bar2m pg6/mmm 6/mmm hkl:h>=0, k>=0, l>=0
   with h>=k 177..
   14 pg23 pgm3bar m3 hkl:h>=0, k>=0, l>=0 with l>=h, k>=h 195..
   15 pg432 pg4bar3m pgm3barm m3m hkl:h>=0, k>=0, l>=0 with k>=1 209..
   
  b. Real Space Asymmetric Unit Definitions
  
   The subroutine SETLIM contains the definitions of the real space
   asymmetric unit. Note that not all of the spacegroups have a
   definition within SETLIM.
   
   No. Spacegroup Upper limits on x, y, z (*)
   1 P 1 x < 1, y < 1, z < 1,
   2 P -1 x < 1, y <= 1/2, z < 1,
   3 P 1 2 1 x <= 1/2, y < 1, z < 1,
   4 P 1 21 1 x < 1, y < 1/2, z < 1,
   5 C 1 2 1 x <= 1/2, y < 1/2, z < 1,
   10 P 1 2/M 1 x <= 1/2, y <= 1/2, z < 1,
   16 P 2 2 2 x <= 1/2, y <= 1/2, z < 1,
   17 P 2 2 21 x <= 1/2, y <= 1/2, z < 1,
   18 P 21 21 2 x < 1, y <= 1/4, z < 1,
   19 P 21 21 21 x < 1, y < 1, z <= 1/4,
   20 C 2 2 21 x <= 1/2, y <= 1/4, z < 1,
   21 C 2 2 2 x <= 1/2, y <= 1/4, z < 1,
   22 F 2 2 2 x <= 1/4, y <= 1/4, z < 1,
   23 I 2 2 2 x <= 1/2, y <= 1/4, z <= 1,
   24 I 21 21 21 x <= 1/2, y <= 1/4, z < 1,
   47 P 2/M 2/M 2/M x <= 1/2, y <= 1/2, z <= 1/2,
   65 C 2/M 2/M 2/M x <= 1/2, y <= 1/4, z <= 1/2,
   69 F 2/M 2/M 2/M x <= 1/4, y <= 1/4, z <= 1/2,
   71 I 2/M 2/M 2/M x <= 1/2, y <= 1/4, z <= 1/2,
   75 P 4 x <= 1/2, y <= 1/2, z < 1,
   76 P 41 x < 1, y < 1, z < 1/4,
   77 P 42 x <= 1/2, y < 1, z < 1/2,
   78 P 43 x < 1, y < 1, z < 1/4,
   79 I 4 x <= 1/2, y <= 1/2, z <= 1/2,
   80 I 41 x <= 1/2, y < 1, z < 1/4,
   83 P 4/M x <= 1/2, y <= 1/2, z <= 1/2,
   87 I 4/M x <= 1/2, y <= 1/2, z <= 1/4,
   89 P 4 2 2 x <= 1/2, y <= 1/2, z <= 1/2,
   90 P 4 21 2 x <= 1/2, y <= 1/2, z <= 1/2,
   91 P 41 2 2 x < 1, y < 1, z <= 1/8,
   92 P 41 21 2 x < 1, y < 1, z <= 1/8,
   93 P 42 2 2 x <= 1/2, y < 1, z <= 1/4,
   94 P 42 21 2 x <= 1/2, y <= 1/2, z <= 1/2,
   95 P 43 2 2 x < 1, y < 1, z <= 1/8,
   96 P 43 21 2 x < 1, y < 1, z <= 1/8,
   97 I 4 2 2 x <= 1/2, y <= 1/2, z <= 1/4,
   98 I 41 2 2 x <= 1/2, y < 1, z <= 1/8,
   123 P 4/M 2/M 2/M x <= 1/2, y <= 1/2, z <= 1/2,
   139 I 4/M 2/M 2/M x <= 1/2, y <= 1/2, z <= 1/4,
   143 P 3 x <= 2/3, y <= 2/3, z < 1,
   144 P 31 x < 1, y < 1, z < 1/3,
   145 P 32 x < 1, y < 1, z < 1/3,
   146 R 3 x <= 2/3, y <= 2/3, z < 1/3,
   147 P -3 x <= 2/3, y <= 2/3, z <= 1/2,
   148 R -3 x <= 2/3, y <= 2/3, z <= 1/6,
   149 P 3 1 2 x <= 2/3, y <= 2/3, z <= 1/2,
   150 P 3 2 1 x <= 2/3, y <= 2/3, z <= 1/2,
   151 P 31 1 2 x < 1, y < 1, z <= 1/6,
   152 P 31 2 1 x < 1, y < 1, z <= 1/6,
   153 P 32 1 2 x < 1, y < 1, z <= 1/6,
   154 P 32 2 1 x < 1, y < 1, z <= 1/6,
   155 R 3 2 x <= 2/3, y <= 2/3, z <= 1/6,
   162 P -31 2/M x <= 2/3, y <= 1/2, z <= 1/2,
   164 P -3 2/M 1 x <= 2/3, y <= 1/3, z <= 1,
   166 R -3 2/M x <= 2/3, y <= 2/3, z <= 1/6,
   168 P 6 x <= 2/3, y <= 1/2, z < 1,
   169 P 61 x < 1, y < 1, z < 1/6,
   170 P 65 x < 1, y < 1, z < 1/6,
   171 P 62 x < 1, y < 1, z < 1/3,
   172 P 64 x < 1, y < 1, z < 1/3,
   173 P 63 x <= 2/3, y <= 2/3, z < 1/2,
   175 P 6/M x <= 2/3, y <= 2/3, z <= 1/2,
   177 P 6 2 2 x <= 2/3, y <= 1/2, z <= 1/2,
   178 P 61 2 2 x < 1, y < 1, z <= 1/12,
   179 P 65 2 2 x < 1, y < 1, z <= 1/12,
   180 P 62 2 2 x < 1, y < 1, z <= 1/6,
   181 P 64 2 2 x < 1, y < 1, z <= 1/6,
   182 P 63 2 2 x <= 2/3, y <= 2/3, z <= 1/4,
   191 P 6/M 2/M 2/M x <= 2/3, y <= 1/3, z <= 1/2,
   195 P 2 3 x < 1, y < 1, z <= 1/2,
   196 F 2 3 x <= 1/4, y <= 1/4, z < 1,
   197 I 2 3 x < 1, y < 1, z <= 1/2,
   198 P 21 3 x <= 1/2, y <= 1/2, z < 1,
   199 I 21 3 x <= 1/2, y <= 1/2, z <= 1/2,
   200 P 2/M -3 x <= 1/2, y <= 1/2, z <= 1/2,
   202 F 2/M -3 x <= 1/2, y <= 1/2, z <= 1/4,
   204 I 2/M -3 x <= 1/2, y <= 1/2, z <= 1/2,
   207 P 4 3 2 x < 1, y <= 1/2, z <= 1/2,
   208 P 42 3 2 x <= 1/2, y < 1, z <= 1/4,
   209 F 4 3 2 x <= 1/2, y <= 1/2, z <= 1/2,
   210 F 41 3 2 x <= 1/2, y < 1, z <= 1/8,
   211 I 4 3 2 x <= 1/2, y <= 1/2, z <= 1/4,
   212 P 43 3 2 x < 1, y < 1, z <= 1/8,
   213 P 41 3 2 x < 1, y < 1, z <= 1/8,
   214 I 41 3 2 x <= 1/2, y < 1, z <= 1/8,
   221 P 4/M -3 2/M x <= 1/2, y <= 1/2, z <= 1/2,
   225 F 4/M -3 2/M x <= 1/2, y <= 1/4, z <= 1/4,
   229 I 4/M -3 2/M x <= 1/2, y <= 1/2, z <= 1/4,
   
   (*) The limits are in fractional coordinates, and the lower limits are
   always x=0, y=0, z=0.
     _________________________________________________________________