VECREF (CCP4: Supported Program)
                                       
NAME

   vecref - Vector-space refinement of heavy atom sites in isomorphous
   derivatives.
   
SYNOPSIS

   vecref MAPIN foo_in.map ATOUT foo_out.dat
   [Keyworded input]
   
DESCRIPTION

   Vector-space refinement is an alternative to the standard
   reciprocal-space refinement of Busing & Levy ([1]); instead of
   least-squares minimisation of the sum of weighted squared differences
   between observed and calculated structure factor amplitudes with
   respect to the atomic parameters, we minimise the same function of the
   observed and calculated heavy-atom difference Patterson function
   values.
   
   Although the Patterson function is a complete representation in vector
   space of the set of structure factor amplitudes (provided the
   Patterson function is sampled at a sufficiently fine interval), the
   two types of refinement are not equivalent. This is because the
   minimisation in vector space is only done for sample points where the
   calculated Patterson density is significantly positive, in other words
   near the interatomic vector peaks, whereas each structure factor
   contains information from all points in real space (except in special
   zones). In all real crystal structures the atoms fill all the space
   (there are no holes), so there would be no advantage with vector-space
   refinement; indeed there would be problems due to considerable overlap
   of peaks in vector space.
   
   For a difference structure the situation is reversed; most of the
   space is empty and the probability of overlaps is small; and since the
   structure factors represent mostly empty space, they are dominated by
   errors arising from taking a small difference between large quantities
   with small relative errors. As a result, reciprocal-space refinement
   of heavy-atom parameters is notoriously slow to converge and
   insensitive to misplaced sites and to errors in the starting values of
   the parameters, and refinement statistics usually give little
   indication of the correctness of the solution. (Typical conventional
   R-factors for reciprocal-space heavy-atom refinement are in the range
   30% (rarely) to 70%, usually around 50%, compared with the random
   value for acentric data of 58.6%.)
   
   The theoretical convergence radius for reciprocal-space refinement is
   dmin/4, i.e. 0.75Å at 3Å, but this is unlikely to be achieved in
   practice because of random errors; for vector-space refinement the
   theoretical convergence radius is the apparent atomic diameter, which
   is about dmin/sqrt(2), i.e. about 2.1Å at 3Å.
   
   Vector-space refinement also has the considerable advantage over
   reciprocal-space refinement in that it is possible to perform the
   least-squares fit to the 3-dimensional data set using only isomorphous
   differences, so that heavy-atom derivatives for which no anomalous
   scattering data are available (or are of dubious reliability) can be
   refined using information from all data, centric and acentric. In this
   case it is important to have the derivative data already scaled
   accurately against the native data, as the derivative scale-factor
   cannot be refined in real space. The Kraut scaling technique ([2]) is
   recommended for this; see the documentation for program FHSCAL.
   
   In vector space, there exists no procedure corresponding to the
   heavy-atom difference Fourier for finding minor sites. However other
   options which utilise the Patterson, such as superposition methods,
   are available, and of course one can still calculate structure factors
   from the refined atomic parameters and do a difference Fourier.
   
KEYWORDED INPUT

   Free format using keywords. The following keywords may be used; only
   the leading 4 characters are significant and the order is immaterial:
   
     ANISO, ATOM, BLIMITS, BREFINE, CYCLES, DAMP, END, GROUP, ORIGIN,
     RCUT, RESOLUTION, SCALE, SPACEGROUP, THRESHOLD, TITLE.
     
   The keywords SPACEGROUP, RESOLUTION, CYCLES and ATOM are always
   required, the rest are optional, and assume default values if omitted.
   
  TITLE <title>
  
   Title (max 100 characters).
   
  SPACEGROUP <space_group>
  
   Space group name (e.g. P212121) or number (e.g. 19).
   
  RESOLUTION <d_min> [<d_max>]
  
   Approximate minimum and maximum d-spacings (high and low resolution
   cutoffs respectively; may be given either way round) of the data used
   to compute the Patterson map. d_max may be omitted, in which case no
   low resolution cutoff is assumed.
   
  RCUT <radius>
  
   Radius cutoff for Patterson peaks. The default radius is defined by
   the point where the density either becomes zero or a minimum; this is
   usually satisfactory. If RCUT is positive the radius is taken as a
   RCUT times the RMS radius. Note that the RMS radius is typically
   0.5-0.6 times the default radius, so there is no point setting RCUT
   above about 1.5. If RCUT is negative, the radius (in Angstrom) is
   taken as abs(RCUT).
   
  GROUP <gs> <as1> <w1> <r1> <as2> <w2> <r2>
  
   Group symbol, any 2 characters used to represent the group scatterer,
   e.g. HI for HgI4-- (do not use a symbol which could be confused with
   an atomic symbol).
   
   Atomic symbol, multiplicity and radius for the first type of atom in
   the group; i.e. if this is the central atom then w1 = 1 and r1 = 0.
   
   Repeat for the second type of atom (optional).
   
  CYCLES <ncyc1> <ncyc2> <ncyc3>
  
   The program will perform <ncyc1> cycles of refinement of the occupancy
   factors (usually 3 to 5, possibly up to 10 for difficult cases),
   followed by <ncyc2> cycles of refinement of the occupancies and
   coordinates (usually about 5), and finally <ncyc3> cycles of
   refinement of all variables (occupancies, coordinates and thermal
   parameters) (usually 10-20).
   
  ORIGIN
  
   Specify to include Patterson origin. Usually exclude, except in the
   case of 1 atom in space group P1, when the origin is the only vector.
   See note 5.
   
  SCALE <scale(i)>
  
   Scale factors for the coordinates; if these are fractional then
   scale(i) = 1 (this is the default). If they are in grid units (i.e.
   taken directly from a map) then scale(i) = number of grid units along
   each cell edge. (These grid units need not be the same as those used
   in the Patterson read by the program.)
   
  ATOM <as> <iat> <occ> <x> <y> <z> <b>
  
   <as>
          Atomic or group symbol.
          
   <iat>
          Atom/group identifier (integer from 1 to 9999).
          
   <occ>
          Occupancy.
          
   <x> <y> <z>
          Real space (not Patterson space) fractional/grid coordinates.
          
   <b>
          Thermal parameter (B-factor).
          
  ANISO
  
   This is currently not operational.
   
  BREFINE
  
   Specify to refine individual isotropic thermal parameters (ncyc3 must
   also be > 0). The default is to refine an overall B factor (when ncyc3
   > 0). See note 4.
   
  DAMP <damp>
  
   Damping factor for occupancy and B-factor shifts when these are
   refined together. The default value is 0.25. The occupancies and
   B-factors are always highly correlated, so without damping the shifts
   tend to oscillate.
   
  THRESHOLD <trms>
  
   Only atoms with refined occupancies above this threshold times the
   estimated standard deviation are written to the ATOUT file. If
   threshold is given as negative, the absolute value of the occupancy is
   tested, so that negative occupancies may also be written out. Default
   is 2 sigma.
   
  BLIMITS <blim(1)> <blim(2)>
  
   Only atoms with B factors within the specified limits are accepted on
   input, and are written to the ATOUT file. Defaults are 0 200.
   
  END
  
   Terminate input and start the calculation.
   
INPUT AND OUTPUT FILES

   MAPIN:
          A Patterson map in standard CCP4 format is required; see note 2
          for important information concerning its preparation.
          
   ATOUT:
          The refined coordinates are written to a file in a format
          suitable for inclusion in the control data for subsequent runs.
          The standard library of symmetry positions (SYMOP.LIB) is only
          required if the space group number is specified.
          
   Logical names used:
   
   INPUT_DENSITY_FILE MAPIN
   OUTPUT_COORDINATE_FILE ATOUT
   Symmetry library SYMOP
   [default $CLIBD/symop.lib]
   Form-factor library ATOMSF
   [default $CLIBD/atomsf.lib]
   Dynamic array dimension VECREF_MAXPTS
   [default 200000]
   
   The dynamic array dimension will be automatically increased if it is
   not large enough. However, the program will run faster if it is set
   large enough initially (e.g. setenv VECREF_MAXPTS 1000000).
   
NOTES

    1. Lattice type: The program takes account of non-primitive lattices
       by multiplying the atomic form-factor by the multiplicity factor.
       This means that the refined occupancies are true occupancies, not
       multiplied by the lattice multiplicity.
    2. Map file: Great care must be taken in the preparation of the map
       file, particularly with non-primitive space groups such as C2, as
       the VECREF program may not be able to detect mistakes made. The
       most likely result of this is that you will finish up with
       incorrect occupancies, and hence biased protein phases. The
       following points should be carefully observed:
         a. It is recommended that Kraut scaling of the derivative be
            used, with or without anomalous differences. In the latter
            case the FHSCAL program can be used. The scales and
            temperature factors given to FFT will then be 1 and 0
            respectively. A bias factor of 1 is recommended, but this is
            not critical.
         b. It is a recommended that a list of the largest isomorphous
            differences (or Fhle's) be checked for obvious outliers and
            these rejected before the Patterson is computed, otherwise
            these will strongly bias the occupancies. A convenient way of
            checking is to run a program which performs analyses of the
            scaling in terms of the hkl indices, such as SCALEIT or
            LOCAL, as large outliers usually stand out; the fractional
            rms difference in F^2 is a particularly sensitive check. A
            low resolution cutoff e.g. 20Å in FFT will often remove most
            of the outliers, though this should be done with caution.
         c. The number of sampling intervals specified affects critically
            the run-time of the VECREF run, i.e. inversely proportional
            to the cube of the size of the interval. Normally use an
            interval about 1/4th of the resolution, i.e. Nx = 4.hmax etc.
            The Patterson must of course constitute at least an
            asymmetric unit in vector space, but it doesn't matter if it
            is more than an asymmetric unit.
         d. Use the VF000 map scaling option; for V use the value
            computed by FHSCAL, or for Fhle Pattersons use the actual
            volume. F000 should be 0 as VECREF computes the value from
            the occupancies and scattering factors.
    3. Group scattering factors: These are useful for complex ions like
       AuI4-, PtI6--, HgI4-- etc, where a substantial part of the
       scattering arises from atoms not located at the centre of the
       electron density. The spherically averaged combined scattering
       factor is used.
    4. Thermal parameters: For low resolution (dmin > ~4.5) thermal
       parameters cannot be sensibly refined due to high correlations
       with the occupancies, so this should then be zero, otherwise about
       5.
       Usually when refining the thermal parameters, the R-factor
       (residual) goes up initially and then converges slowly (due to the
       high correlations), but not back as far as the level attained by
       refining occupancies and coordinates alone. This in itself should
       not necessarily be taken to mean that the thermal parameters are
       not meaningful. This increases the peak widths and hence the
       number of observations; this by itself will tend to push up the
       R-factor, but also the extra observations will be in the tails of
       the peaks where the signal to noise ratio is poor.
    5. Patterson origin: The program should normally be instructed to
       ignore the origin peak for the purposes of least-squares unless
       you are confident there is no systematic discrepancy between the
       observed and calculated origin peak heights, as there usually is,
       probably because of random errors and/or missing sites.
       
PRINTER OUTPUT

   The refined atomic parameters appear in a table under the following
   headings:
Atom  Parameter  Init  Old  Shift  Change  New  Esd

   Atom
          the atom or group symbols and identifiers.
          
   Parameter
          the names of the atomic parameters being refined.
          
   Init
          the values of the parameters at the start of the current run.
          
   Old
          the values of the parameters before the current cycle of
          refinement.
          
   Shift
          Under Shift appear, on the same line as the atom name, the net
          shifts in Angstrom for the current cycle, and, on the same line
          as the parameter name, the shifts for the current cycle in the
          same units as the corresponding parameter.
          
   Change
          Under Change appear, on the same line as the atom name, the net
          shifts in Angstrom from the initial values, and, on the same
          line as the parameter name, the shifts from the initial values
          in the same units as the corresponding parameter.
          
   New
          the new values of the parameters for the current cycle.
          
   Esd
          Under Esd appear, on the same line as the atom name, the
          estimated standard deviation of the atomic position in
          Angstrom, and, on the same line as the parameter name, the
          estimated standard deviations of the parameters in the same
          units as the corresponding parameter.
          
   Atoms are not allowed to shift from their initial position by more
   than twice the expected convergence radius (approximately
   dmin*sqrt(2)); atoms for which the calculated shift would take them
   over this limit have their occupancy set to zero; the occupancy is
   then allowed to refine upwards only if the coordinate shifts move the
   atom back towards its initial position. Atoms with occupancy exactly
   zero are ignored on input; if this effect is not desired, alter the
   zero occupancy to some small number (e.g. 0.001).
   
   I have not yet had sufficient experience with the program to know what
   constitute good R-factors and correlation coefficients, or which
   statistic to place the greatest reliance on, though the R-factor seems
   to be more discriminating. The best result I have had so far is R =
   17.5%, C = 0.976, (excluding the Patterson origin, and not refining
   B-factors) for the test data distributed with the program. Note this
   is real data ! (Acknowledgements to Dr. Simon Phillips, University of
   Leeds.)
   
   The list of vectors, which appears after the occupancy refinement
   cycles and again at the end of the run, has the Patterson map
   coordinates in the same units as the atomic coordinates if these were
   supplied as map grid coordinates, or in the same units as the map
   supplied if the atomic coordinates were supplied as fractions of a
   unit cell. The columns labelled Pobs, Pcalc, and <Pobs>, <Pcalc> are
   approximate peak heights and mean peak values respectively. They are
   intended only as a guide to the fit; in particular the Pcalc values do
   not include a contribution from any overlapping peaks. (These are not
   the data used in the least squares, where the fit is done on a grid
   point basis, not on a peak basis.)
   
ERRORS

   One or more of the following messages occur when errors are discovered
   in the input control data; the program continues to process the data
   but stops when all data has been read:

   *** ERROR: Centring translation not integer.
   *** ERROR: Identity position not found.
   *** ERROR: Invalid number of atoms.
   *** ERROR: Atom symbol not in scat. fact. list.
   *** ERROR IN GETINP: Error(s) in input data.

   The following conditions indicate that an array is not large enough
   for the problem and should be cured either by correcting the input
   data (in most cases by increasing the sampling interval of the
   Patterson), or by increasing the value assigned to the symbol
   specified in PARAMETER statements in the source code, taking care to
   modify all PARAMETER statements containing the symbol, and
   re-compiling and linking.

   *** ERROR: Array bound check (MSECT).
   *** ERROR: Array bound check (MRHO).
   *** ERROR IN ADDAST: Array bound check (MCF).
   *** ERROR IN PKLIST: Array bound check (MPL).
   *** ERROR IN GENPTS: Array bound check (MPT).

   The following conditions are likely to occur if either the symmetry
   specified is wrong, or the Patterson map is less than an asymmetric
   unit:

   *** ERROR: Point not found.
   *** ERROR IN GENPTS: No points.

   The following errors occur when the standard map handling routine
   detects an error; this is likely to indicate something seriously wrong
   with the map file, like data corruption:

   *** ERROR IN PKLIST: MGULP error.
   *** ERROR IN REFCYC: MGULP error.

PROGRAM DESCRIPTION

   One important point often not clearly understood about this method of
   refinement is that the program does handle overlapping vectors
   correctly, provided first that the overlap is between known atoms and
   second that not all vectors arising from a pair of atoms overlap. This
   is because the calculated Patterson density is summed over all
   contributing atom pairs before being compared with the observed value.
   Vectors which overlap with those due to as yet unknown atoms will
   positively bias the occupancy, and will also affect the refined
   coordinates, but this is also true for the reciprocal-space method.
   
REFERENCES

    1. Busing WR and Levy HA (1961) in Computing Methods and the Phase
       Problem in X-ray Crystal Analysis, Pergamon, Oxford.
    2. Kraut J, Sieker LC, High DF, Freer ST (1962), Proc. Nat. Acad.
       Sci. USA, 48, 1417-1424.
       
SEE ALSO

   MLPHARE - reciprocal-space refinement and phasing program
   FFT - prepare Patterson function for MAPIN
   
EXAMPLES

  Simple unix example script found in $CEXAM/unix/runnable/
  
     * vecref.exam (Use vecref to refine sites determined using RSPS)
       
   (A vms version found in $CEXAM/vms/vecref.com)
   
AUTHOR

   Originator: Ian Tickle, Birkbeck College, London