VECSUM (CCP4: Unsupported Program)
                                       
NAME

   vecsum - program to deconvolute a Patterson function and solve the
   structure.
   
SYNOPSIS

   vecsum MAPIN foo_in.map MAPOUT foo_out.map
   [control data in fixed order]
   
DESCRIPTION

   The purpose of this program is to deconvolute a Patterson function and
   solve the structure. Although it was designed for heavy-atom
   difference Pattersons (isomorphous and FHLE) there is no reason why it
   could not be used to solve structures of small molecules.
   
   The main features of the program are as follows :
   
   1. It is completely space-group general.
   
   2. It takes as input a Patterson function produced by the Fast Fourier
   Transform FFT program in the standard format. Like the FFT program it
   works with a user specified array to optimise use of memory.
   
   3. The Patterson function must comprise at least one asymmetric unit
   of the appropriate point group. However, for high symmetry cases it is
   advisable to compute as many asymmetric units as the available memory
   and disk space will allow in order to minimise searching for
   equivalent positions, although there is probably no advantage in
   computing more than one half of the cell. This will mean generating
   equivalents for and computing the Patterson in P1 bar. This
   incidentally simplifies the problem of unique axis orientation as no
   permutation of axes is required. It is recommended that the sampling
   interval in the Patterson be about dmin/4, i.e. in FFT NX = 4*hmax
   etc.
   
   4. The program requires an estimate of the expected number of major
   sites. This is could be 1 to start with, and increased as more sites
   are found. The value is used to calculate an upper thresholding level
   :


        Pmax = ( P(0,0,0) + Pooo ) / (Ngep * Nexp)

   where

        P(0,0,0) = origin value e.g. 1000

        Pooo = Fooo contribution, typically 5 to 10 for P(0,0,0) = 1000

        Ngep = Number of general equivalent positions (not counting
               centring)

        Nexp = Number of major sites expected

   Then if P(u,v,w) + Pooo > Pmax , the value is truncated to Pmax. Also
   if P(u,v,w) + Pooo < 0 , the value is truncated to 0.
   
   5. The program can calculate a "symmetry function" or a "superposition
   function" or a combination of the two (see Stout & Jensen, X-ray
   structure determination, chapter 14). The user can control which
   Harker vectors, if any, are combined with the superposition function.
   
   6. The program produces a map of the possible sites in the structure
   very much like an electron density map. The symmetry function, which
   is normally calculated first, uses only Harker vectors and therefore
   has higher symmetry than the true space group.


e.g. : P21 has asymmetric unit : x = 0 to 1, y = 0 to 1/2, z = 0 to 1
            equivalent origins : x = 0 or 1/2, y = any, z = 0 or 1/2
             symmetry function : x = 0 to 1/2, y = 0, z = 0 to 1/2
                                 (i.e. only 1 section.)

    P41212 has asymmetric unit : x = 0 to 1, y = 0 to 1, z = 0 to 1/8
            equivalent origins : (x,y) = (0,0) or (1/2,1/2), z = 0 or 1/2
             symmetry function : x = 0 to 1/4, y = 0 to 1, z = 0 to 1/8

   7. Each point in the map produced is a combination of the values found
   for the calculated vectors in the Patterson function. At present there
   are 3 modes of combination :
   a)
          Minimum
   b)
          Arithmetic mean (equivalent to sum)
   c)
          Harmonic mean (reciprocal of mean of reciprocals)
          
   The harmonic mean is strongly biassed towards the minimum, yet takes
   some account of the higher values, and is a reasonable compromise
   between the Minimum and Sum functions.
   
   8. The user is recommended to proceed in a stepwise fashion by first
   choosing a site in the symmetry function. Experience suggests that
   apparent sites lying on true rotation (as opposed to screw) axes are
   more likely than not to be wrong; these can be eliminated by opting to
   ignore Harker vectors falling on the Patterson origin; however the
   possibility that one or more sites do lie on rotation axes should be
   borne in mind. Having chosen a site with high density, the coordinates
   are added to the input data, and a second site chosen. This process is
   repeated until the site densities fall off significantly compared with
   the rms noise leevel printed at the end of the output.
   
   9. The option to print a list of the vectors between the input sites
   should be used to monitor the fit with the Patterson; it is important
   to realise that it is not enough just to find sites which have vectors
   falling on peaks in the Patterson; unexplained peaks of high density
   almost certainly indicate a wrong or at best incomplete solution.
   
   10. The user supplies a "discrimination" which simply truncates the
   lower values in the output map. A value of 0.2 will cause map values <
   0.2*Pmax not to be printed. Use a higher value to get more
   discrimination, but run the rsik of missing weak sites.
   
   11. The user supples a "tolerance" (in grid units). The effect of this
   is to search the local area of each vector in the Patterson function
   within a sphere of the specified radius and return the maximum value
   to the combination function. The program will stop if no grid points
   are found, e.g., if you give a site with coordinates (1.5, 10.5, 0)
   (in grid units) and a tolerance of 0.5, there will be no points on the
   Patterson grid within this distance of the site, the closest being
   0.707 grid units away. Also beware of giving too large a value for the
   tolerance (i.e. > 1.5), as this will require a large amount of
   searching and hence an inordinate amount of cpu time.
   
   12. The user supplies a REAL array to the FFT program and an INTEGER*2
   array to the VECSUM program e.g. :


        INTEGER*2 MAP
        COMMON MAP(70000)
        CALL VECSUM(70000)
        END

   The size of this array must be greater than the number of grid points
   in the Patterson function calculated by FFT. The VECSUM program
   reports the size actually used. Note size of array required = (Number
   of Patterson sections +2) * Number of points per section.
   
Control data for the VECSUM program.


Record 1.       Title


Record 2.       JU  JV  JW

                Sort order for output map.
                JU = fastest (across page) axis on output       with 1 for x
                JV = medium (down page)         .       .            2 for y
                JW = slowest (section)          .       .            3 for z

                For map output in standard orientation (2nd setting
                monoclinic, y sections), JU JV JW = 1 3 2

                For map output with z sections (1st setting monoclinic),
                JU JV JW = 2 1 3


Record 3.       LX  MX  LY  MY  LZ  MZ   limits in x, y, z for output.


Record 4.       Pooo  DISC  TOL  COSA  COSB  COSG

                Pooo = Fooo contribution ( 5 to 10 for Patterson origin
                of 1000).

                DISC = discrimination (e.g. 0.2)

                TOL = tolerance (e.g. 1.1)

                COSA, COSB, COSG are cosines of unit cell angles, used
                to calculate distances in the local search, but the
                values are not critical.


Record 5.       NLINE  LATT  NGEP  NHAR  NUSE  NEXP  NSIT  IFUN

                NLINE = Maximum number of columns per line in printed map.
                        If 0 defaults to normal width (64).
                        If < 0 suppresses printing and produces a map
                        on disk in standard format.

                LATT = lattice type, 1 = P, 2 = I, 3 = R, 4 = F,
                                     5 = A, 6 = B, 7 = C.

                NGEP = number of general equivalent positions (g.e.p.'s)
                in space group counting any centrosymmetrically related, but
                not related by centring translations (minus 1 if identity
                omitted).

                NHAR = number of different Harker vectors to use.

                NUSE = number of g.e.p.'s to use to generate half a primitive
                cell from the Patterson input (0 if the input Patterson is
                already half a cell).

                NEXP = number of major sites expected.  If negative, the
                Patterson origin peak will be removed.  This effectively
                eliminates spurious sites that fall on pure rotation axes
                (if the space group has any), but of course should not be
                used if it is suspected that there are 1 or more sites that
                really do lie on a rotation axis.

                NSIT = number of sites input, or 0 to produce a symmetry
                function.  If both NHAR and NSIT are zero, the program outputs
                the truncated Patterson function.  If NSIT is negative, the
                program only produces a list of all vectors between the input
                sites and their equivalent positions, with the corrsponding
                value in the Patterson.

                IFUN = type of combination function, 1 = Minimum, 2 = Arithmeti
c
                mean (equivalent to Sum), 3 = Harmonic mean.  If IFUN is
                positive, the combination value for all Harker and cross-vector
s
                is calculated;  if IFUN is negative, the combination values are
                calculated for the two types of vectors are calculated
                separately and then combined as a Minimum function (makes no
                difference if IFUN = 1).  The latter option may give improved
                discrimination.


                Omit record 6 if NGEP = 0.

Record 6.       General equivalent positions as in International Tables, Vol 1.
                The identity may be omitted.  This record to be given NGEP
                times.


                Omit records 7 and 8 if NHAR = 0.

Record 7.       Serial numbers of g.e.p.'s to use for Harker vectors (NHAR
                numbers).  If all Harker vectors are to be used this will be
                just the integers from 1 to NGEP (omitting the identity if
                present).  In some space groups some Harker vectors are
                equivalent and in such cases some time will be saved if only
                the unique ones are given, and the appropriate multiplicities
                are given on the next record.  If in doubt give all g.e.p.
                numbers except the identity and give the multiplicites all 1.


Record 8.       Multiplicities of Harker vectors (NHAR numbers).


                Omit record 9 if NUSE = 0.

Record 9.       Serial numbers of g.e.p.'s to be used to generate Patterson
                symmetry (NUSE numbers).  The translation components are not
                used.


                Omit record 10 if NSIT = 0.

Record 10.      Site coordinates in grid units.  This record to be given NSIT
                times.


INPUT AND OUTPUT FILES

  Input
  
   MAPIN
          Patterson map prepared by FFT.
          
  Output
  
   MAPOUT
          Map of the "symmetry function" or "superposition function".
          
SEE ALSO

   RSPS - alternative program
   FFT - prepare Patterson function for MAPIN
   PEAKMAX - look for sites in MAPOUT
   
Example of control data.


GC2 ETHGCL ANOMALOUS/LOCAL SCALED 5.5A FHLE, GRID = 40 40 72.  P41212
2 1 3
0 39 0 39 0 9
10 .2 1.1 0 0 0
0 0 7 6 0 3 5 3
-X,-Y,1/2+Z
1/2-Y,1/2+X,1/4+Z
1/2+Y,1/2-X,3/4+Z
Y,X,-Z
-Y,-X,1/2-Z
1/2-X,1/2+Y,1/4-Z
1/2+X,1/2-Y,3/4-Z
1 2 4 5 6 7
1 2 1 1 1 1
.5 29.5 0
24.1 15.6 2.5
.8 9.7 5
4 26.5 6.7
33 20 7